## Slide 1: Geometric Dimensioning and Tolerancing
Chapter 4, Feature Control Frames

## Slide 2: Review
Chap 1 – Introduction
  importance of interchangeable parts
  need to avoid ambiguity in drawings
Chap 2 – Symbols & Abbreviations
  Dimensioning Symbols ; Geometric Characteristics ; Modifying Symbols
Chap 3 – Datums
  datums define coordinate systems from which measurements are taken during part inspection

## Slide 3: Introduction
The feature control frame provides a specified control for single or multiple features.
A feature control frame must contain at least a geometric characteristic symbol and a tolerance value.

## Slide 4: Geometric Characteristics
Explained in detail in Chapters 6 and 8.

## Slide 5: Attachment
The placement of the feature control frame governs what information it is conveying
surface of cylindrical feature
center axis of cylindrical feature

## Slide 6: Attachment
4 placement styles
  The feature control frame is placed below a dimension pertaining to a feature. The leader is from the dimension.
  A leader from the feature control frame runs to the controlled feature.
  A side or end of the feature control frame is attached to an extension line from the feature. The feature surface must be a plane.
  A side or end of the feature control frame is attached to a feature-of-size dimension extension line.

## Slide 7: Content of a Feature Control Frame
The first compartment is always a geometric characteristic symbol .
The next compartment is a tolerance.

## Slide 8: Content of a Feature Control Frame
The next compartments identify datums as needed to define the reference coordinate system.
The feature control frame may contain modifiers.

## Slide 9
Read from left to right.

## Slide 10: Types of Feature Control Frames
single
combined
feature given a tolerance and then identified as a datum

## Slide 11: Evaluation
control
combined
surface
geometric characteristic
tolerance
left right
primary
line
compartments
no
I O