## Slide 1: Geometric Dimensioning and Tolerancing
Chapter 5, General Rules

## Slide 2: Review
Chap 1 – Introduction
  importance of interchangeable parts
  need to avoid ambiguity in drawings
Chap 2 – Symbols & Abbreviations
  Dimensioning Symbols ; Geometric Characteristics ; Modifying Symbols
Chap 3 – Datums
  datums define coordinate systems from which measurements are taken during part inspection
Chap 4 – Feature Control Frames
  defines a geometric characteristic of a feature or a relationship between different features

## Slide 3: Overview of Rules
There are four general rules
  Taylor’s rule. Limits of size.
  Regardless of Feature Size (RFS) is the default.
  Pitch cylinder axis is reference for thread and screws.
  Virtual condition.

## Slide 4: Rule 1 – Taylor’s Principle
Rule 1 states:
  "where only a tolerance of size is specified, the limits of size of an individual feature prescribe the extent to which variations in its geometric form, as well as size, are allowed.“
The feature surface may not exceed the limits of size.
When a feature is made at MMC, it must be of perfect form.
When not at MMC, the shape may not extend beyond the MMC perfect form.

## Slide 5: Rule 1
Specification for a peg.
If made at MMC, .515, the peg must be perfectly straight.

## Slide 6: Rule 1
If made smaller than MMC, the peg can be bent or tapered.
However, it must not extend beyond the MMC perfect shape boundaries.

## Slide 7
Limits of Size – Rule #1
Taylor Principle (1905)
The limits of size “Rule #1” defines the size and form limits for regular, individual features. It requires perfect form at MMC and ensures the pin will fit in the hole.
If the feature is made at MMC, its form must be perfect.
Notes: The rule that defines size is called Rule #1.

## Slide 8
Limits of Size – Rule #1
The limits of size define the size, as well as the form of an individual feature. The form of the feature may vary within the size limits. If the feature is produced at its maximum material condition, the form must be perfect. The feature may be bent, tapered or out of round as it departs from the maximum material condition.
(Envelope Principle, Taylor Principle)
Notes: This is a formal definition of the limits of size. It is often called by 3 names, The Taylor Principle, Rule 1 and ISO often refers to it as the Envelope Principle.
This principle defines the size limits when plus/minus tolerance is used on a feature. The size of a feature also controls the form of the feature. It requires perfect form at MMC.
The size requirements do not affect stock sizes or commercially produced parts. See workbook for additional info.
The knowledge of this concept is very important because in the form tolerance unit. The size of the feature will allow variations to the form. The object of the form tolerances is to further refine the form better than the size tolerance requires.
ISO standards often use another definition of size called the Independency Principle. This principle does not require perfect form to be included in the limits of size. Form limits must be controlled separately by geometric control or by additional standards.
We will talk about that later.

## Slide 9
Limits of Size – Rule #1
The limits of size define the size, as well as the form of an individual feature. The form of the feature may vary within the size limits. If the feature is produced at its maximum material condition, the form must be perfect. The feature may be bent, tapered or out of round as it departs from the maximum material condition.
(Envelope Principle, Taylor Principle
Verification Check #1
(form or shape check)
Notes: Notice the perfect form boundaries at MMC. No part of the feature may extend beyond this boundary. This will insure the pin will fit into the hole.

## Slide 10
Limits of Size – Rule #1
The limits of size define the size, as well as the form of an individual feature. The form of the feature may vary within the size limits. If the feature is produced at its maximum material condition, the form must be perfect. The feature may be bent, tapered or out of round as it departs from the maximum material condition.
(Envelope Principle, Taylor Principle
Verification Check #2
(local size check)
Notes: There is no requirement for perfect form at LMC so the pin or hole can be bent or tapered as it departs from MMC,

## Slide 11
T
h
i
s
o
n
t
h
e
d
r
a
w
i
n
g
.
8
7
4
.
8
7
0
.
8
7
4
M
a
x
.
8
7
0
M
i
n
M
e
a
n
s
t
h
i
s
Can be waisted within .004. Form can be refined with straightness or cylindricity.
.
8
7
4
M
a
x
.
8
7
0
M
i
n
Can be tapered within .004
Form can be refined with cylindricity.
.
8
7
4
M
a
x
.
8
7
0
M
i
n
Can be barreled within .004
Form can be refined with straightness or cylindricity.
.
8
7
4
M
a
x
.
8
7
0
M
i
n
Can be bent within .004. Form can be refined with straightness or cylindricity.
.
8
7
4
M
a
x
.
8
7
0
M
i
n
Can be oval or out of round within .004
Form can be refined with circularity or cylindricity.
.
8
7
4
M
a
x
.
8
7
0
M
i
n
Can be “D” shaped out of round within .004
Form can be refined with circularity or cylindricity.
Limits of Size – Rule #1
Notes: This slide shows all the variations that the size tolerance alone will allow. The pin can be tapered, bent, barreled, oval, D shaped, etc.
If it is necessary to refine these form variation better it would be necessary to apply a form tolerance as shown in unit 10.
More on this in unit 10. Just introduce the idea.

## Slide 12: Rule 1
Designers may wish to permit a feature to vary beyond the boundary of perfect form at MMC.
In this case, the symbol is used after the dimension to indicate independency.
Also, rule 1 does not control any interrelation of features. The outer and inner surfaces each obey rule 1 individually.

## Slide 13: Rule 2 – RFS default
Regardless of Feature Size (RFS) applies, with respect to the individual tolerance, datum reference, or both, where no modifying symbol is specified.
This will be discussed further with regards to MMC and LMC modifiers.

## Slide 14: Rule 3 - threads
Rule Three applies to all screw threads, gears, and splines.
"for each tolerance of orientation or position and datum reference specified for screw threads applies to the axis of the thread derived from the pitch cylinder, for gears and splines, the MAJOR DIA., PITCH DIA., or MINOR DIA. must be specified."

## Slide 15: Rule 4 – datum/virtual condition rule
applies to datum features subject to size variation
"depending on whether it is used as a primary, secondary, or tertiary datum, a virtual condition exists for a datum feature of size where its axis or center line is controlled by a geometric tolerance.“
virtual condition is the worst acceptable condition of a feature
the virtual condition for an internal or external feature is the LMC size

## Slide 16: Evaluation
size form
individual
MMC LMC
MMC
zero
RFS
pitch
beneath
foundation
not