## Slide 1: Geometric Dimensioning and Tolerancing
Chapter 6, Form, Orientation, Profile, and Runout Tolerances

## Slide 2: Geometric Characteristics
Form, Orientation, Profile, and Runout Tolerances

## Slide 3: Straightness
Straightness can be applied to a surface (either flat or cylindrical).
Straightness can also be applied to an axis.
straightness applied to a
flat surface
straightness applied to a
cylindrical surface

## Slide 4: Straightness
As you measure along a line, the height must be between 12 and 13 mm and the variation may not be more than 0.5 mm from a straight line.

## Slide 5: Straightness
Straightness applied to a cylindrical surface.

## Slide 6: Straightness
Straightness can also be applied to an axis.
12.50.2

## Slide 7: Geometric Characteristics
Form, Orientation, Profile, and Runout Tolerances

## Slide 8: Flatness
Flatness is the condition of a surface where all elements are in one plane.

## Slide 9: Flatness
The surface could be checked by translating the part under a dial indicator.

## Slide 10: Geometric Characteristics
Form, Orientation, Profile, and Runout Tolerances

## Slide 11: Circularity
Circularity is roundness.
At any cross-sectional measurement during one complete revolution of the feature, all points of the surface are perpendicular at an equal distance from a common axis.

## Slide 12: Geometric Characteristics
Form, Orientation, Profile, and Runout Tolerances

## Slide 13: Cylindricity
Cylindricity is the condition of an entire feature surface during one revolution in which all surface points are an equal distance from a common axis.

## Slide 14: Geometric Characteristics
Form, Orientation, Profile, and Runout Tolerances

## Slide 15: Perpendicularity
Perpendicularity is the condition of an entire surface, plane, or axis at a right angle to a datum plane or axis.

## Slide 16: Perpendicularity
Perpendicularity is the condition of an entire surface, plane, or axis at a right angle to a datum plane or axis.

## Slide 17: Geometric Characteristics
Form, Orientation, Profile, and Runout Tolerances

## Slide 18: Angularity
Angularity is the condition of an axis or plane other than 90 degrees to another datum plane or axis.

## Slide 19: Geometric Characteristics
Form, Orientation, Profile, and Runout Tolerances

## Slide 20: Parallelism
Parallelism is the condition of a surface, center plane, or axis that is an equal distance at all points from a datum plane or axis.
bilateral tolerance zone

## Slide 21: Parallelism
Example of a cylinder being parallel to another surface.

## Slide 22: Parallelism
Example of a cylinder being parallel to another cylinder.

## Slide 23: Geometric Characteristics
Form, Orientation, Profile, and Runout Tolerances

## Slide 24: Profile: line , surface
Profile tolerance is specified for designs where the surface is to be controlled within a given basic shape.
Specified for irregular features that are difficult to control with other form or orientation tolerances.

## Slide 25: Profile: line , surface

## Slide 26: Geometric Characteristics
Form, Orientation, Profile, and Runout Tolerances

## Slide 27: Circular Runout and Total Runout
The worst circular runout occurs at the slice with the greatest variation (0.03 mm in this case).
Total runout is the difference between the highest and lowest readings found over the entire feature. (0.11 mm in this case).

## Slide 29: Circularity vs. Runout
Can anyone explain the difference between the two and can they be used on a print interchangeabilty?
http://www.eng-tips.com/viewthread.cfm?qid=186399
tp://communities.ptc.com/message/173195

## Slide 30: Circularity vs. Runout

## Slide 31: Geometric Characteristics
Form, Orientation, Profile, and Runout Tolerances