## Slide 1: Geometric Dimensioning and Tolerancing
Chapter 7, Virtual Condition

## Slide 2: Introduction
Chapter introduces an important concept related to the mating of parts in an assembly.
Interchangeability of parts and assemblies can only be ensured when parts are accepted at virtual condition or better.

## Slide 3: External Feature
Suppose we’re making a clearance hole to fit over a peg.
How big should we make the hole to make sure we have clearance?
Well, what’s the virtual size of the peg?

## Slide 4: External Feature
The virtual condition of an external feature is a constant value equal to its MMC size plus its applicable tolerance of form or location.
For this pin, the virtual condition is a diameter of 12.7 mm (MMC) + the straightness tolerance of the center axis of diameter 0.5 mm.
Total virtual condition of 13.2 mm.
We can guarantee that any peg made to this specification will fit within a cylinder of diameter 13.2 mm. This is the overall outer boundary.

## Slide 5: External Feature, MMC discussion
The feature control frame says that there is a straightness criteria of the center axis of 0.5 mm at MMC
If the as-built size deviates from MMC, you can have more tolerance.
The amount of extra tolerance will equal the deviation from MMC.

## Slide 6: External Feature, MMC discussion
If you make the peg at a diameter of: | Then the diameter of the straightness tolerance zone is:
 12.7 mm |  0.5 mm
 12.6 mm |  0.6 mm
 12.5 mm |  0.7 mm
 12.4 mm |  0.8 mm
 12.3 mm |  0.9 mm

## Slide 7: External Feature, MMC discussion
The feature control frame says that there is a straightness criteria of the center axis of 0.5 mm at MMC
If the as-built size deviates from MMC, you can have more tolerance.
The amount of extra tolerance will equal the deviation from MMC.
For example if the part was built with a diameter of 12.3 mm (the smallest allowable size), then the straightness tolerance would be 0.5 + 0.4 = 0.9 mm.
The virtual size for this case would be 12.3 + 0.9 = 13.2 mm.

## Slide 8: Inspection of External Feature
Parts are inspected with functional gaging at virtual condition that represents the mating part.
here is a part made at MMC
which should have perfect form according to rule 1
but our straightness specification overruled rule 1 so our inspection gage had to be bigger

## Slide 9: Virtual Size of an Internal Feature
The virtual size of an internal feature (hole) is the smallest cross sectional area that will be guaranteed to be free of material.
virtual size =  at MMC minus any position tolerance (discussed in Chap 8) and any straightness type of tolerance

## Slide 10: Guaranteeing Part Mating
The hole in the block will always clear the peg if the virtual size of the hole (the guaranteed free space) is greater than the virtual size of the peg (the largest possible region that may be occupied by the peg).

## Slide 11: Evaluation