## Slide 1: Geometric Dimensioning and Tolerancing
Chapter 8, Tolerances of Location

## Slide 2: Geometric Characteristics
Form, Orientation, Profile, and Runout Tolerances
In Chapter 6, we discussed the geometric characteristics highlighted above.

## Slide 3: Geometric Characteristics
Form, Orientation, Profile, and Runout Tolerances
In Chapter 8, we will now discuss the location tolerances.

## Slide 4: Concentricity
Used to establish a tolerance zone for the median points of a cylindrical feature.
The FCF reads,"relative to datum A, all median points of opposing elements on this cylindrical surface must lie within a cylindrical tolerance zone of 0.5 mm".

## Slide 5: Symmetry
Symmetry is the condition where a feature or part has the same profile on either side of the center plane (median plane) of a datum feature.
The controlled feature is permitted a maximum of .005 inch shift to the side in either direction.

## Slide 6: Position Tolerance
Position is one of the most effective and used controls in GD&T.
Position is defined in terms of feature centers.
The tolerance zone may be modified with the geometric modifiers, i.e. MMC, LMC, or RFS.

## Slide 7: Position Tolerance
The ‘perfect’ location of the center of the hole relative to the datums is defined by basic dimensions.

## Slide 8: Position Tolerance
If the hole is made at MMC ( .528), the center position must lie within a cylindrical tolerance zone of diameter  .010.

## Slide 9: Position Tolerance
If you make the hole diameter at a size different than MMC, you will be given a larger position tolerance size.
hole  (in) | tol zone  (in)
 .528 |  .010
 .530 |  .012
 .532 |  .014
 .534 |  .016
 .536 |  .018
 .538 |  .020

## Slide 10: Position Tolerance
When are the MMC, LMC, and RFS used for position tolerance?
Let’s see ‘How it Works”.