## Slide 2: CHAP 1 Preliminary Concepts and Linear Finite Elements
Instructor: Nam-Ho Kim (nkim@ufl.edu)
Web: http://www2.mae.ufl.edu/nkim/INFEM/

## Slide 3: Table of Contents
1.1. INTRODUCTION
1.2. VECTOR AND TENSOR CALCULUS
1.3. STRESS AND STRAIN
1.4. MECHANICS OF CONTINUOUS BODIES
1.5. FINITE ELEMENT METHOD

## Slide 4: Introduction
1.1

## Slide 5: Background
Finite Element Method (FEM):
  a powerful tool for solving partial differential equations and integro-differential equations
Linear FEM:
  methods of modeling and solution procedure are well established
Nonlinear FEM:
  different modeling and solution procedures based on the characteristics of the problems  complicated
  many textbooks in the nonlinear FEMs emphasize complicated theoretical parts or advanced topics
This book:
  to simply introduce the nonlinear finite element analysis procedure and to clearly explain the solution procedure
  detailed theories, solution procedures, and implementation using MATLAB for only representative problems

## Slide 6: Chapter Outline
Vector and Tensor Calculus
  Preliminary to understand mathematical derivations in other chapters
Stress and Strain
  Review of mechanics of materials and elasticity
Mechanics of Continuous Bodies
  Energy principles for structural equilibrium (principle of minimum potential energy)
  Principle of virtual work for more general non-potential problems
Finite Element Method
  Discretization of continuum equations and approximation of solution using piecewise polynomials
  Introduction to MATLAB program ELAST3D

## Slide 7: Vector and tensor calculus
1.2

## Slide 8: Vector and Tensor
Vector: Collection of scalars
Cartesian vector: Euclidean vector defined using Cartesian coordinates
  2D, 3D Cartesian vectors
  Using basis vectors: e1 = {1, 0, 0}T, e2 = {0, 1, 0}T, e3 = {0, 0, 1}T
u1
u2
u3
x
y
z
e1
e2
e3

## Slide 9: Index Notation and Summation Rule
Index notation: Any vector or matrix can be expressed in terms of its indices
Einstein summation convention
  In this case, k is a dummy variable (can be j or i)
  The same index cannot appear more than twice
Basis representation of a vector
  Let ek be the basis of vector space V
  Then, any vector in V can be represented by
Repeated indices mean summation!!

## Slide 10: Index Notation and Summation Rule cont.
Examples
  Matrix multiplication:
  Trace operator:
  Dot product:
  Cross product:
  Contraction: double dot product
Permutation symbol

## Slide 11: Cartesian Vector
Cartesian Vectors
Dot product
  Kronecker delta function
  Equivalent to change index j to i, or vice versa
How to obtain Cartesian components of a vector
Magnitude of a vector (norm):
X1
X2
X3
e1
e2
e3
u
v
Projection

## Slide 12: Notation Used Here
Direct tensor notation | Tensor component notation | Matrix notation

## Slide 13: Tensor and Rank
Tensor
  A tensor is an extension of scalar, vector, and matrix (multidimensional array in a given basis)
  A tensor is independent of any chosen frame of reference
  Tensor field: a tensor-valued function associated with each point in geometric space
Rank of Tensor
  No. of indices required to write down the components of tensor
  Scalar (rank 0), vector (rank 1), matrix (rank 2), etc
  Every tensor can be expressed as a linear combination of rank 1 tensors
  Rank 1 tensor v: vi
  Rank 2 tensor A: Aij
  Rank 4 tensor C: Cijkl
Rank-2 stress tensor

## Slide 14: Tensor Operations
Basic rules for tensors
  Tensor (dyadic) product: increase rank
Rank-4 tensor:
Different notations
Identity tensor

## Slide 15: Tensor Operations cont.
Symmetric and skew tensors
  Symmetric
  Skew
  Every tensor can be uniquely decomposed by symmetric and skew tensors
  Note: W has zero diagonal components and Wij = - Wji
Properties – Let A be a symmetric tensor

## Slide 16: Example
Displacement gradient can be considered a tensor (rank 2)
Strain tensor
Spin tensor

## Slide 17: Contraction and Trace
Contraction of rank-2 tensors
  contraction operator reduces four ranks from the sum of ranks of two tensors
magnitude (or, norm) of a rank-2 tensor
Constitutive relation between stress and strain
Trace: part of contraction
  In tensor notation

## Slide 18: Orthogonal Tensor
In two different coord.
Direction cosines
Change basis
e1*
e2*
e3*
e1
e2
e3
We can also show
Orthogonal tensor
Rank-2 tensor transformation

## Slide 19: Permutation
The permutation symbol has three indices, but it is not a tensor
the permutation is zero when any of two indices have the same value: e112 = e121 = e111 = 0
Identity
vector product

## Slide 20: Dual Vector
For any skew tensor W and a vector u
  Wu and u are orthogonal
Let
Then,
Dual vector of skew tensor W

## Slide 21: Vector and Tensor Calculus
Gradient
  Gradient is considered a vector
  We will often use a simplified notation:
Laplace operator
Gradient of a scalar field f(X): vector

## Slide 22: Vector and Tensor Calculus
Gradient of a Tensor Field (increase rank by 1)
Divergence (decrease rank by 2)
  Ex)
Curl

## Slide 23: Integral Theorems
Divergence Theorem
Gradient Theorem
Stokes Theorem
Reynolds Transport Theorem
G
c
r
n: unit outward normal vector

## Slide 24: Integration-by-Parts
u(x) and v(x) are continuously differentiable functions
1D
2D, 3D
For a vector field v(x)
Green’s identity

## Slide 25: Example: Divergence Theorem
S: unit sphere (x2 + y2 + z2 = 1), F = 2xi + y2j + z2k
Integrate

## Slide 26: Quiz
A symmetric rank four tensor is defined by where 1 = [dij] is a unit tensor of rank-two and is a symmetric unit tensor of rank-four. When E is an arbitrary symmetric rank-two tensor, calculate S = D:E in terms of E.

## Slide 27: Stress and strain
1.3

## Slide 28: Surface Traction (Stress)
Surface traction (Stress)
  The entire body is in equilibrium with external forces (f1 ~ f6)
  The imaginary cut body is in equilibrium due to external forces (f1, f2, f3) and internal forces
  Internal force acting at a point P on a plane whose unit normal is n:
  The surface traction depends on the unit normal direction n.
  Surface traction will change as n changes.
  unit = force per unit area (pressure)

## Slide 29: Cartesian Stress Components
Surface traction changes according to the direction of the surface.
Impossible to store stress information for all directions.
Let’s store surface traction parallel to the three coordinate directions.
Surface traction in other directions can be calculated from them.
Consider the x-face of an infinitesimal cube
s11
s12
s13
x
y
z
Dx
Dy
Dz
DF
Normal stress
Shear stress

## Slide 30: Stress Tensor
  First index is the face and the second index is its direction
  When two indices are the same, normal stress, otherwise shear stress.
  Continuation for other surfaces.
  Total nine components
  Same stress components are defined for the negative planes.
Rank-2 Stress Tensor
Sign convention
s11
s22
s33
s12
s13
s21
s23
s31
s32
x
y
z
Dx
Dy
Dz

## Slide 31: Symmetry of Stress Tensor
  Stress tensor should be symmetric 9 components 6 components
  Equilibrium of the angular moment
  Similarly for all three directions:
  Let’s use vector notation:
Cartesian components of stress tensor

## Slide 32: Stress in Arbitrary Plane
  If Cartesian stress components are known, it is possible to determine the surface traction acting on any plane.
  Consider a plane whose normal is n.
  Surface area (ABC = A)
  The surface traction
  Force balance
x
y
z
B
A
C
s33
s31
s32
s22
s23
s21
s11
s13
s12
t(n)
n
P

## Slide 33: Cauchy’s Lemma
All three-directions
Tensor notation
  stress tensor; completely characterize the state of stress at a point
Cauchy’s Lemma
  the surface tractions acting on opposite sides of the same surface are equal in magnitude and opposite in direction

## Slide 34: Projected Stresses
Normal stress
Shear stress
Principal stresses
Mean stress (hydrostatic pressure)
Stress deviator
Rank-4 identity tensor
Rank-4 deviatoric identity tensor

## Slide 35: Principal Stresses
Normal & shear stress change as n changes
  Is there a plane on which the normal (or shear)stress becomes the maximum?
There are at least three mutually perpendicular planes on which the normal stress attains an extremum
  Shear stresses are zero on these planes  Principal directions
  Traction t(n) is parallel to surface normal n
Eigenvalue problem
Principal stress
Principal direction

## Slide 36: Eigenvalue Problem for Principal Stresses
The eigenvalue problem has non-trivial solution if and only if the determinant is zero:
The above equation becomes a cubic equation:
Three roots are principal stresses

## Slide 37: Principal Directions
Stress Invariants: I1, I2, I3
  independent of the coordinate system
Principal directions
  Substitute each principal stress to the eigenvalue problem to get n
  Since the determinant is zero, an infinite number of solutions exist
  Among them, choose the one with a unit magnitude
Principal directions are mutually perpendicular

## Slide 38: Principal Directions
There are three cases for principal directions:
  σ1, σ2, and σ3 are distinct  principal directions are three unique mutually orthogonal unit vectors.
  σ1 = σ2 and σ3 are distinct  n3 is a unique principal direction, and any two orthogonal directions on the plane that is perpendicular to n3 are principal directions.
  σ1 = σ2 = σ3  any three orthogonal directions are principal directions. This state of stress corresponds to a hydrostatic pressure.
n3

## Slide 39: Strains (Simple Version)
  Strain is defined as the elongation per unit length
  Tensile (normal) strains in x1- and x2-directions
  Strain is a dimensionless quantity. Positive for elongation and negative for compression
P
P
Dx1
Du1
Dx2
Du2
Textbook has different, but more rigorous derivations

## Slide 40: Shear Strain
  Shear strain is the tangent of the change in angle between two originally perpendicular axes
  Shear strain (change of angle)
  Positive when the angle between two positive (or two negative) faces is reduced and negative when the angle is increased.
  Valid for small deformation
P
Du1
Du2
q2
q1
p/2 – g12
Dx1
Dx2

## Slide 41: Strains (Rigorous Version)
Strain: a measure of deformation
  Normal strain: change in length of a line segment
  Shear strain: change in angle between two perpendicular line segments
Displacement of P = (u1, u2, u3)
Displacement of Q & R
P(x1,x2,x3)
Q
R
P'(x1+u1, x2+u2, x3+u3)
Q'
R'
x1
x2
x3
Dx1
Dx2

## Slide 42: Displacement Field
Coordinates of P, Q, and R before and after deformation
Length of the line segment P'Q'

## Slide 43: Deformation Field
Length of the line segment P'Q'
Linear normal strain
Linear
Nonlinear
Ignore H.O.T. when displacement gradients are small

## Slide 44: Deformation Field
Shear strain gxy
  change in angle between two lines originally parallel to x– and y–axes
Engineering shear strain
Different notations

## Slide 45: Strain Tensor
Strain Tensor
Cartesian Components
Vector notation

## Slide 46: Volumetric and Deviatoric Strain
Volumetric strain (from small strain assumption)
Deviatoric strain
x2
x3
x1
1
e11
e22
e33
1
1
Exercise: Write Idev in matrix-vector notation

## Slide 47: Stress-Strain Relationship
Applied Load shape change (strain) stress
There must be a relation between stress and strain
Linear Elasticity: Simplest and most commonly used
Proportional limit
Yield stress
Ultimate stress
Strain hardening
Necking
Fracture
s
e
Young’s modulus

## Slide 48: Generalized Hooke’s Law
Linear elastic material
  In general, Dijkl has 81 components
  Due to symmetry in sij, Dijkl = Djikl
  Due to symmetry in ekl, Dijkl = Dijlk
  from definition of strain energy, Dijkl = Dklij
Isotropic material (no directional dependence)
  Most general 4-th order isotropic tensor
  Have only two independent coefficients (Lame’s constants: l and m)
21 independent coeff

## Slide 49: Generalized Hooke’s Law cont.
Stress-strain relation
  Volumetric strain:
  Off-diagonal part:
  Bulk modulus K: relation b/w volumetric stress & strain
  Substitute so that we can separate volumetric part
Total deform. = volumetric + deviatoric deform.
m is the shear modulus
Bulk modulus

## Slide 50: Generalized Hooke’s Law cont.
Stress-strain relation cont.
Deviatoric part
Volumetric part
Deviatoric strain
Important for plasticity; plastic deformation only occurs in deviatoric part volumetric part is always elastic
Deviatoric stress

## Slide 51: Generalized Hooke’s Law cont.
Vector notation
  The tensor notation is not convenient for computer implementation
  Thus, we use Voigt notation
  Strain (6×1 vector), Stress (6×1 vector), and C (6×6 matrix)
2nd-order tensor  vector 4th-order tensor  matrix
e12 + e21 = 2e12
You don’t need 2 here

## Slide 52: 3D Solid Element cont.
Elasticity matrix
Relation b/w Lame’s constants and Young’s modulus and Poisson’s ratio
Textbook has a definition of D in terms of E and n

## Slide 53: Plane Stress
Thin plate–like components parallel to the xy–plane
The plate is subjected to forces in its in-plane only
s13 = s23 = s33 = 0
e13 = e23 = 0, but e33 ≠ 0
e33 can be calculated from the condition of s33 = 0:

## Slide 54: Plane Strain
Strains with a z subscript are all zero: e13 = e23 = e33 = 0
Deformation in the z–direction is constrained, (i.e., u3 = 0)
can be used if the structure is infinitely long in the z–direction
s13 = s23 = 0, but s33 ≠ 0
s33 can be calculated from the condition of e33 = 0:

## Slide 55: Mechanics of continuous bodies
1.4

## Slide 56: Governing Equations for Equilibrium
Governing differential equations for structural equilibrium
  Three laws of mechanics: conservation of mass, conservation of linear momentum and conservation of angular momentum
Boundary-valued problem: satisfied at every point in W
  Governing D.E. + Boundary conditions
  Solutions: C2–continuous for truss & solid, C4–continuous for beam
  Unnecessarily requirements for higher-order continuity
Energy-based method
  For conservative system, structural equilibrium when the potential energy has its minimum: Principle of minimum potential energy
  If the solution of BVP exists, then that solution is the minimizing solution of the potential energy
  When no solution exists in BVP, PMPE may have a natural solution
Principle of virtual work
  Equilibrium of the work done by both internal and external forces with small arbitrary virtual displacements

## Slide 57: Balance of Linear Momentum
Balance of linear momentum
Stress tensor (rank 2):
Surface traction
Cauchy’s Lemma
W
G
n
tn
X1
X2
X3
e1
e2
e3
X
fb: body force
tn: surface traction
0 for static problem

## Slide 58: Balance of Linear Momentum cont
Balance of linear momentum
  For a static problem
Balance of angular momentum
Divergence Theorem

## Slide 59: Boundary-Valued Problem
We want to determine the state of a body in equilibrium
The equilibrium state (solution) of the body must satisfy
  local momentum balance equation
  boundary conditions
Strong form of BVP
  Given body force fb, and traction t on the boundary, find u such that and
Solution space
(1)
(2)
(3)
W
G
n
t
X1
X2
X3
e1
e2
e3
X
fb

## Slide 60: Boundary-Valued Problem cont.
How to solve BVP
  To solve the strong form, we want to construct trial solutions that automatically satisfy a part of BVP and find the solution that satisfy remaining conditions.
  Statically admissible stress field: satisfy (1) and (3)
  Kinematically admissible displacement field: satisfy (2) and have piecewise continuous first partial derivative
  Admissible stress field is difficult to construct. Thus, admissible displacement field is used often

## Slide 61: Principle of Minimum Potential Energy (PMPE)
Deformable bodies generate internal forces by deformation against externally applied forces
Equilibrium: balance between internal and external forces
For elastic materials, the concept of force equilibrium can be extended to energy balance
Strain energy: stored energy due to deformation (corresponding to internal force)
For elastic material, U(u) is only a function of total displacement u (independent of path)
Linear elastic material

## Slide 62: PMPE cont.
Work done by applied loads (conservative loads)
U(u) is a quadratic function of u, while W(u) is a linear function of u.
Potential energy
Gh
Gg
W
u1
u2
u3
x1
x2
x3
f s
f b

## Slide 63: PMPE cont.
PMPE: for all displacements that satisfy the boundary conditions, known as kinematically admissible displacements, those which satisfy the boundary-valued problem make the total potential energy stationary on DA
But, the potential energy is well defined in the space of kinematically admissible displacements
No need to satisfy traction BC (it is a part of potential)
Less requirement on continuity
The solution is called a generalized (natural) solution
H1: first-order derivatives are integrable

## Slide 64: Example – Uniaxial Bar
Strong form
Integrate twice:
Apply two BCs:
PMPE with assumed solution u(x) = c1x + c2
To satisfy KAD space, u(0) = 0,  u(x) = c1x
Potential energy:
L
F
x
Solution of BVP

## Slide 65: Virtual Displacement
Virtual displacement is not experienced but only assumed to exist so that various possible equilibrium positions may be compared to determine the correct one
Let mass m and springs are in equilibrium at the current position
Then, a small arbitrary perturbation, dr, can be assumed
  Since dr is so small, the member forces are assumed unchanged
The work done by virtual displacement is
If the current position is in force equilibrium, dW = 0
F1
F2
F3
F4
dr

## Slide 66: Virtual Displacement Field
Virtual displacement (Space Z)
  Small arbitrary perturbation (variation) of real displacement
  Let ū be the virtual displacement, then u + ū must be kinematically admissible, too
  Then, ū must satisfy homogeneous displacement BC
  Space Z only includes homogeneous essential BCs
Property of variation
u
ū
In the literature, du is often used instead of ū

## Slide 67: PMPE As a Variation
Necessary condition for minimum PE
  Stationary condition <--> first variation = 0
Variation of strain energy
Energy bilinear form

## Slide 68: PMPE As a Variation cont.
Variation of work done by applied loads
Thus, PMPE becomes
  Load form is linear with respect to ū
  Energy form a(u, ū) is symmetric, bilinear w.r.t. u and ū
  Different problems have different a(u, ū) and , but they share the same property
How can we satisfy “for all ū  ” requirement? Can we test an infinite number of ū?
Load linear form

## Slide 69: Example – Uniaxial Bar
Assumed displacement u(x) = cx 
  virtual displacement is in the same space with u(x):
Variation of strain energy
Variation of applied load
PMPE
Arbitrary  arbitrary  coefficient of must be zero

## Slide 70: Principle of Virtual Work
Instead of solving the strong form directly, we want to solve the equation with relaxed requirement (weak form)
Virtual work – Work resulting from real forces acting through a virtual displacement
Principle of virtual work – when a system is in equilibrium, the forces applied to the system will not produce any virtual work for arbitrary virtual displacements
  Balance of linear momentum is force equilibrium
  Thus, the virtual work can be obtained by multiplying the force equilibrium equation with a virtual displacement
  If the above virtual work becomes zero for arbitrary ū, then it satisfies the original equilibrium equation in a weak sense

## Slide 71: Principle of Virtual Work cont
PVW
  Integration-by-parts
  Divergence Thm
  The boundary is decomposed by

## Slide 72: Principle of Virtual Work cont
Since sij is symmetric
Weak Form of BVP
  Internal virtual work = external virtual work
  Starting point of FEM
Symbolic expression
  Energy form:
  Load form:
FE equation

## Slide 73: Example – Heat Transfer Problem
Steady-State Differential Equation
Boundary conditions
Space of kinematically admissible temperature
Multiply by virtual temperature, integrate by part, and apply boundary conditions
Q
domain A
Sq
ST
qn
T = T0
n = {nx, ny}T

## Slide 74: Example – Beam Problem
Governing DE
Boundary conditions for cantilevered beam
Space of kinematically admissible displacement
Integrate-by-part twice, and apply BCs
f(x)
x
L

## Slide 75: Difference b/w Strong and Weak Solutions
The solution of the strong form needs to be twice differentiable
The solution of the weak form requires the first-order derivatives are integrable  bigger solution space than that of the strong form
If the strong form has a solution, it is the solution of the weak form
If the strong form does not have a solution, the weak form may have a natural solution
F

## Slide 76: Finite element method
1.5

## Slide 77: Finite Element Approximation
Difficult to solve a variational equation analytically
Approximate solution
  Linear combination of trial functions
  Smoothness & accuracy depend on the choice of trial functions
  If the approximate solution is expressed in the entire domain, it is difficult to satisfy kinematically admissible conditions
Finite element approximation
  Approximate solution in simple sub-domains (elements)
  Simple trial functions (low-order polynomials) within an element
  Kinematically admissible conditions only for elements on the boundary
Exact solution
Approximate solution
x
u(x)
Finite elements
Nodes
Piecewise- linear approximation

## Slide 78: Finite Elements
Types of finite elements
1D 2D 3D
Variational equation is imposed on each element.
One element
Linear
Quadratic

## Slide 79: Trial Solution
  Solution within an element is approximated using simple polynomials.
  i-th element is composed of two nodes: xi and xi+1. Since two unknowns are involved, linear polynomial can be used:
  The unknown coefficients, a0 and a1, will be expressed in terms of nodal solutions u(xi) and u(xi+1).

## Slide 80: Trial Solution cont.
  Substitute two nodal values
  Express a0 and a1 in terms of ui and ui+1. Then, the solution is approximated by
  Solution for Element e:
  N1(x) and N2(x): Shape Function or Interpolation Function

## Slide 81: Trial Solution cont.
Observations
  Solution u(x) is interpolated using its nodal values ui and ui+1.
  N1(x) = 1 at node xi, and =0 at node xi+1.
  The solution is approximated by piecewise linear polynomial and its gradient is constant within an element.
  Stress and strain (derivative) are often averaged at the node.
N1(x)
N2(x)
xi
xi+1

## Slide 82: 1D Finite Elements
1D BVP
Use PVW
Integration-by-parts
  This variational equation also satisfies at individual element level
Space of kinematically admissible displacements
(1)

## Slide 83: 1D Interpolation Functions
Finite element approximation for one element (e) at a time
Satisfies interpolation condition
Interpolation of displacement variation (same with u)
Derivative of u(x): differentiating interpolation functions

## Slide 84: Element-Level Variational Equation
Approximate variational equation (1) for element (e)
  Must satisfied for all
  If element (e) is not on the boundary, can be arbitrary
Element-level variational equation
2x2 matrix
2x1 vector

## Slide 85: Assembly
Need to derive the element-level equation for all elements
Consider Elements 1 and 2 (connected at Node 2)
Assembly
Vanished unknown term

## Slide 86: Assembly cont.
Assembly of NE elements (ND = NE + 1)
Coefficient matrix [K] is singular; it will become non-singular after applying boundary conditions

## Slide 87: Example
Use three equal-length elements
All elements have the same coefficient matrix
RHS (p(x) = x)

## Slide 88: Example cont.
RHS cont.
Assembly
Apply boundary conditions
  Deleting 1st and 4th rows and columns
Element 1
Element 2
Element 3

## Slide 89: EXAMPLE cont.
Approximate solution
Exact solution
  Three element solutions are poor
  Need more elements

## Slide 90: 3D Solid Element
Isoparametric mapping
  Build interpolation functions on the reference element
  Jacobian: mapping relation between physical and reference elem.
Interpolation and mapping
(a) Finite Element
(b) Reference Element
x
h
z
(1,1,–1)
(1,1,1)
(–1,1,1)
(–1,1,–1)
x1
x2
x3
x4
x5
x6
x7
x8
x2
x1
x3
(1, –1,–1)
(1, –1,1)
(–1, –1,1)
Same for mapping and interpolation

## Slide 91: 3D Solid Element cont.
Jacobian matrix
Derivatives of shape functions
  Jacobian should not be zero anywhere in the element
  Zero or negative Jacobian: mapping is invalid (bad element shape)
: Jacobian

## Slide 92: 3D Solid Element cont.
Displacement-strain relation

## Slide 93: 3D Solid Element cont.
Transformation of integration domain
Energy form
Load form
Discrete variational equation

## Slide 94: Numerical Integration
For bar and beam, analytical integration is possible
For plate and solid, analytical integration is difficult, if not impossible
Gauss quadrature is most popular in FEM due to simplicity and accuracy
1D Gauss quadrature
  NG: No. of integ. points; xi: integ. point; wi: integ. weight
  xi and wi are chosen so that the integration is exact for (2*NG – 1)-order polynomial
  Works well for smooth function
  Integration domain is [-1, 1]

## Slide 95: Numerical Integration cont.
Multi-dimensions
NG | Integration Points (xi) | Weights (wi)
1 | 0.0 | 2.0
2 | .5773502692 | 1.0
3 | .7745966692 0.0 | .5555555556 .8888888889
4 | .8611363116 .3399810436 | .3478546451 .6521451549
5 | .9061798459 .5384693101 0.0 | .2369268851 .4786286705 .5688888889
x
h
x
h
x
h
(a) 11
(b) 22
(c) 33

## Slide 96: ELAST3D.m
A module to solve linear elastic problem using NLFEA.m
Input variables for ELAST3D.m
Variable | Array size | Meaning
ETAN | (6,6) | Elastic stiffness matrix Eq. (1.81)
UPDATE | Logical variable | If true, save stress values
LTAN | Logical variable | If true, calculate the global stiffness matrix
NE | Integer | Total number of elements
NDOF | Integer | Dimension of problem (3)
XYZ | (3,NNODE) | Coordinates of all nodes
LE | (8,NE) | Element connectivity

## Slide 97: How to Solve Linear Problem in Nonlinear Code
Linear matrix solver
  Construct stiffness matrix and force vector
  Use LU decomposition to solve for unknown displacement {d}
Nonlinear solver (iterative solver)
  Assume the solution at iteration n is known, and n+1 is unknown
{fint} = {fext}
{f} = {fext} − {fint} = {0}
For linear problem, {dn} = {0}
Only one iteration!!

## Slide 98
function ELAST3D(ETAN, UPDATE, LTAN, NE, NDOF, XYZ, LE)
%***********************************************************************
% MAIN PROGRAM COMPUTING GLOBAL STIFFNESS MATRIX AND RESIDUAL FORCE FOR
% ELASTIC MATERIAL MODELS
%***********************************************************************
%%
global DISPTD FORCE GKF SIGMA
%
% Integration points and weights (2-point integration)
XG=[-0.57735026918963D0, 0.57735026918963D0];
WGT=[1.00000000000000D0, 1.00000000000000D0];
%
% Index for history variables (each integration pt)
INTN=0;
%
%LOOP OVER ELEMENTS, THIS IS MAIN LOOP TO COMPUTE K AND F
for IE=1:NE
% Nodal coordinates and incremental displacements
ELXY=XYZ(LE(IE,:),:);
% Local to global mapping
IDOF=zeros(1,24);
for I=1:8
II=(I-1)*NDOF+1;
IDOF(II:II+2)=(LE(IE,I)-1)*NDOF+1:(LE(IE,I)-1)*NDOF+3;
end
DSP=DISPTD(IDOF);
DSP=reshape(DSP,NDOF,8);
%
%LOOP OVER INTEGRATION POINTS
for LX=1:2, for LY=1:2, for LZ=1:2
E1=XG(LX); E2=XG(LY); E3=XG(LZ);
INTN = INTN + 1;
%
% Determinant and shape function derivatives
[~, SHPD, DET] = SHAPEL([E1 E2 E3], ELXY);
FAC=WGT(LX)*WGT(LY)*WGT(LZ)*DET;

## Slide 99
% Strain
DEPS=DSP*SHPD';
DDEPS=[DEPS(1,1) DEPS(2,2) DEPS(3,3) ...
DEPS(1,2)+DEPS(2,1) DEPS(2,3)+DEPS(3,2) DEPS(1,3)+DEPS(3,1)]';
%
% Stress
STRESS = ETAN*DDEPS;
%
% Update stress
if UPDATE
SIGMA(:,INTN)=STRESS;
continue;
end
%
% Add residual force and stiffness matrix
BM=zeros(6,24);
for I=1:8
COL=(I-1)*3+1:(I-1)*3+3;
BM(:,COL)=[SHPD(1,I) 0 0;
0 SHPD(2,I) 0;
0 0 SHPD(3,I);
SHPD(2,I) SHPD(1,I) 0;
0 SHPD(3,I) SHPD(2,I);
SHPD(3,I) 0 SHPD(1,I)];
end
%
% Residual forces
FORCE(IDOF) = FORCE(IDOF) - FAC*BM'*STRESS;
%
% Tangent stiffness
if LTAN
EKF = BM'*ETAN*BM;
GKF(IDOF,IDOF)=GKF(IDOF,IDOF)+FAC*EKF;
end
end, end, end, end
end

## Slide 100
function [SF, GDSF, DET] = SHAPEL(XI, ELXY)
%*************************************************************************
% Compute shape function, derivatives, and determinant of hexahedral element
%*************************************************************************
%%
XNODE=[-1 1 1 -1 -1 1 1 -1;
-1 -1 1 1 -1 -1 1 1;
-1 -1 -1 -1 1 1 1 1];
QUAR = 0.125;
SF=zeros(8,1);
DSF=zeros(3,8);
for I=1:8
XP = XNODE(1,I);
YP = XNODE(2,I);
ZP = XNODE(3,I);
%
XI0 = [1+XI(1)*XP 1+XI(2)*YP 1+XI(3)*ZP];
%
SF(I) = QUAR*XI0(1)*XI0(2)*XI0(3);
DSF(1,I) = QUAR*XP*XI0(2)*XI0(3);
DSF(2,I) = QUAR*YP*XI0(1)*XI0(3);
DSF(3,I) = QUAR*ZP*XI0(1)*XI0(2);
end
GJ = DSF*ELXY;
DET = det(GJ);
GJINV=inv(GJ);
GDSF=GJINV*DSF;
end
SF(81): shape functions,
GDSF (38): shape functions derivatives
DET: Jacobian of the mapping

## Slide 101: One Element Tension Example
%
% One element example
%
% Nodal coordinates
XYZ=[0 0 0;1 0 0;1 1 0;0 1 0;0 0 1;1 0 1;1 1 1;0 1 1];
%
% Element connectivity
LE=[1 2 3 4 5 6 7 8];
%
% External forces [Node, DOF, Value]
EXTFORCE=[5 3 10.0E3; 6 3 10.0E3; 7 3 10.0E3; 8 3 10.0E3];
%
% Prescribed displacements [Node, DOF, Value]
SDISPT=[1 1 0;1 2 0;1 3 0;2 2 0;2 3 0;3 3 0;4 1 0;4 3 0];
%
% Material properties
% MID:0(Linear elastic) PROP=[LAMBDA NU]
MID=0;
PROP=[110.747E3 80.1938E3];
%
% Load increments [Start End Increment InitialFactor FinalFactor]
TIMS=[0.0 1.0 1.0 0.0 1.0]';
%
% Set program parameters
ITRA=30; ATOL=1.0E5; NTOL=6; TOL=1E-6;
%
% Calling main function
NOUT = fopen('output.txt','w');
NLFEA(ITRA, TOL, ATOL, NTOL, TIMS, NOUT, MID, PROP, EXTFORCE, SDISPT, XYZ, LE);
fclose(NOUT);
10kN
x2
x1
x3
1
2
3
4
5
6
7
8
10kN
10kN
10kN

## Slide 102: One Element Output
Time Time step Iter Residual
1.00000 1.000e+00 2 5.45697e-12
TIME = 1.000e+00
Nodal Displacements
Node U1 U2 U3
1 0.000e+00 0.000e+00 0.000e+00
2 -5.607e-08 0.000e+00 0.000e+00
3 -5.607e-08 -5.607e-08 0.000e+00
4 0.000e+00 -5.607e-08 0.000e+00
5 -5.494e-23 1.830e-23 1.933e-07
6 -5.607e-08 4.061e-23 1.933e-07
7 -5.607e-08 -5.607e-08 1.933e-07
8 -8.032e-23 -5.607e-08 1.933e-07
Element Stress
S11 S22 S33 S12 S23 S13
Element 1
0.000e+00 1.091e-11 4.000e+04 -2.322e-13 6.633e-13 -3.317e-12
0.000e+00 0.000e+00 4.000e+04 -3.980e-13 1.327e-13 -9.287e-13
-3.638e-12 7.276e-12 4.000e+04 -1.592e-12 -2.123e-12 -3.317e-12
0.000e+00 0.000e+00 4.000e+04 2.653e-13 -2.123e-12 5.307e-13
0.000e+00 0.000e+00 4.000e+04 5.638e-13 3.449e-12 -1.327e-12
0.000e+00 0.000e+00 4.000e+04 -1.194e-12 4.776e-12 1.061e-12
0.000e+00 0.000e+00 4.000e+04 -7.960e-13 2.919e-12 -3.449e-12
3.638e-12 3.638e-12 4.000e+04 -5.307e-13 3.715e-12 1.061e-12
*** Successful end of program ***
Command line output
Contents in output.txt