## Slide 1: CHAP 5 Finite Element Analysis of Contact Problem
Nam-Ho Kim

## Slide 2: Introduction
Contact is boundary nonlinearity
  The graph of contact force versus displacement becomes vertical
  Both displacement and contact force are unknown in the interface
Objective of contact analysis
  Whether two or more bodies are in contact
  Where the location or region of contact is
  How much contact force or pressure occurs in the interface
  If there is a relative motion after contact in the interface
Finite element analysis procedure for contact problem
  Find whether a material point in the boundary of a body is in contact with the other body
  If it is in contact, the corresponding contact force must be calculated

## Slide 3: Introduction
Equilibrium of elastic system:
  finding a displacement field that minimizes the potential energy
Contact condition (constrained minimization)
  the potential is minimized while satisfying the contact constraint
Convert to unconstrained optimization
  Can be solved using either the penalty method or Lagrange multiplier method
Contact-target concept for contact implementation
  the nodes on the contact boundary cannot penetrate the surface elements on the target boundary

## Slide 4: Goals
Learn the computational difficulty in boundary nonlinearity
Understand the concept of variational inequality and its relationship with the constrained optimization
Learn how to impose contact constraint and friction constraints using penalty method
Understand difference between Lagrange multiplier method and penalty method
Learn how to integrate contact constraint with the structural variational equation
Learn how to implement the contact constraints in finite element analysis
Understand collocational integration

## Slide 5: 1D Contact Examples
5.2

## Slide 6: Contact Problem – Boundary Nonlinearity
Contact problem is categorized as boundary nonlinearity
Body 1 cannot penetrate Body 2 (impenetrability)
Why nonlinear?
  Both contact boundary and contact stress are unknown!!!
  Abrupt change in contact force (difficult in NR iteration)
Body 1
Body 2
Contact boundary
Contact stress (compressive)
Penetration
Contact force

## Slide 7: Why are contact problems difficult?
Unknown boundary
  Contact boundary is unknown a priori
  It is a part of solution
  Candidate boundary is often given
Abrupt change in force
  Extremely discontinuous force profile
  When contact occurs, contact force cannot be determined from displacement
  Similar to incompressibility (Lagrange multiplier or penalty method)
Discrete boundary
  In continuum, contact boundary varies smoothly
  In numerical model, contact boundary varies node to node
  Very sensitive to boundary discretization
Penetration
Contact force
Body 1
Body 2

## Slide 8: Contact of a Cantilever Beam with a Rigid Block
Trial-and-error solution
  First assume that the deflection is smaller than the gap
  Since , the assumption is wrong, the beam will be in contact

## Slide 9: Cantilever Beam Contact with a Rigid Block cont.
Trial-and-error solution cont.
  Now contact occurs. Contact in one-point (tip).
  Contact force, , to prevent penetration
  Determine the contact force from tip displacement = gap

## Slide 10: Cantilever Beam Contact with a Rigid Block cont.
Solution using contact constraint
  Treat both contact force and gap as unknown and add constraint
  When , no contact. Contact occurs when . impossible
  Gap condition:

## Slide 11: Cantilever Beam Contact with a Rigid Block cont.
Solution using contact constraint cont.
  Contact condition
  No penetration:
  Positive contact force:
  Consistency condition:
  Lagrange multiplier method
  When   violate contact condition
  When   satisfy contact condition
Lagrange multiplier, , is the contact force

## Slide 12: Cantilever Beam Contact with a Rigid Block cont.
Penalty method
  Small penetration is allowed, and contact force is proportional to it
  Penetration function
  Contact force
  From
  Gap depends on penalty parameter
: penalty parameter

## Slide 13: Cantilever Beam Contact with a Rigid Block cont.
Penalty method cont.
  Large penalty allows small penetration
Penalty parameter | Penetration (m) | Contact force (N)
3×105 | 1.25×10−4 | 37.50
3×106 | 2.27×10−5 | 68.18
3×107 | 2.48×10−6 | 74.26
3×108 | 2.50×10−7 | 74.92
3×109 | 2.50×10−8 | 75.00

## Slide 14: Beam Contact with Friction
Sequence: is applied first, followed by the axial load
Assume no friction (, 1D bar deformation)
Frictional constraint ()
  Stick condition:
  Slip condition:
  Consistency condition:
: tangential friction force

## Slide 15: Beam Contact with Friction cont.
Trial-and-error solution
  First assume stick condition (need to satisfy )
  Violate:
  Next, try slip condition (need to satisfy )
  Satisfies , therefore, valid

## Slide 16: Beam Contact with Friction cont.
Solution using frictional constraint (Lagrange multiplier)
  Use consistency condition:
  Choose as a Lagrange multiplier and as a constraint
  When , , and , violate the stick condition
  When
  and the slip condition is satisfied, valid solution

## Slide 17: Beam Contact with Friction cont.
Penalty method
  Penalize when
  Slip displacement and frictional force
  When (stick), (no penalization)
  When (slip), penalize to stay close
  Friction force (in terms of )
: penalty parameter for tangential slip

## Slide 18: Beam Contact with Friction cont.
Penalty method cont.
  Tip displacement
  For large ,
Penalty parameter | Tip displacement (m) | Frictional force (N)
1×10−4 | 5.68×10−4 | 43.18
1×10−3 | 6.19×10−4 | 38.12
1×10−2 | 6.24×10−4 | 37.56
1×10−1 | 6.25×10−4 | 37.50
1×100 | 6.25×10−4 | 37.50
Slip condition

## Slide 19: Observations
Due to unknown contact boundary, contact point should be found using either direct search (trial-and-error) or nonlinear constraint equation
  Both methods requires iterative process to find contact boundary and contact force
  Contact function replace the abrupt change in contact condition with a smooth but highly nonlinear function
Friction force calculation depends on the sequence of load application (Path-dependent)
Friction function regularizes the discontinuous friction behavior to a smooth one

## Slide 20: General Formulation FOR 2D Contact Problems
5.3

## Slide 21: General Contact Formulation
Contact between a flexible body and a rigid body
Point contacts to rigid surface (param )
How to find
  Closest projection onto the rigid surface
Unit tangent vector

## Slide 22: Contact Formulation cont.
Gap function
Impenetrability condition
Tangential slip function
boundary that has a possibility of contact
Parameter at the previous contact point

## Slide 23: Ex) Project to a Parabola
Projection of to
Let
Projection point
Gap

## Slide 24: Variational Inequality
Governing equation
Contact conditions (small deformation)
Contact set (convex)
satisfies all kinematic constraints (displacement conditions)

## Slide 25: Variational Inequality cont.
Variational equation with (i.e., is arbitrary)
Since it is arbitrary, we don’t know the value, but it is non-negative
Variational inequality for contact problem

## Slide 26: Illustration of Projection
If the solution is out of set , it is projected to on
Beam deflection example (rigid block with initial gap of 1mm)
: beam deflection without rigid block
  Contact condition is violated (penetration to the block)
: projection of onto convex set
  by applying the contact force

## Slide 27: Variational Inequality cont.
For large deformation problem
Variational inequality is not easy to solve directly
We will show that V.I. is equivalent to constrained optimization of total potential energy
The constraint will be imposed using either penalty method or Lagrange multiplier method
{ }

## Slide 28: Potential Energy and Directional Derivative
Potential energy
Directional derivative
Directional derivative of potential energy
For variational inequality

## Slide 29: Equivalence
V.I. is equivalent to constrained optimization
  For arbitrary
Thus, is the smallest potential energy in
  Unique solution if and only if is a convex function and set is closed convex
non-negative

## Slide 30: Constrained Optimization
PMPE minimizes the potential energy in the kinematically admissible space
Contact problem minimizes the same potential energy in the contact constraint set
The constrained optimization problem can be converted into unconstrained optimization problem using the penalty method or Lagrange multiplier method
  If , penalize using
penalty parameter

## Slide 31: Constrained Optimization cont.
Penalized unconstrained optimization problem
constrained
unconstrained
Solution space w/o contact 

uNoContact
u
Contact force

## Slide 32: Ex) Beam Deflection with Rigid Block
Assumed deflection:
Penalty function:
Penalized potential energy

## Slide 33: Ex) Beam Deflection with Rigid Block
Stationary condition
Penetration:
Contact force:
Penalty parameter | a1 | a2 | a3 | Penetration (m) | Contact force (N)
3×105 | 2.31×10−3 | -1.60×10−3 | 4.17×10−4 | 1.25×10−4 | 37.50
3×106 | 2.16×10−3 | -1.55×10−3 | 4.17×10−4 | 2.27×10−5 | 68.18
3×107 | 2.13×10−3 | -1.54×10−3 | 4.17×10−4 | 2.48×10−6 | 74.26
3×108 | 2.13×10−3 | -1.54×10−3 | 4.17×10−4 | 2.50×10−7 | 74.92
3×109 | 2.13×10−3 | -1.54×10−3 | 4.17×10−4 | 2.50×10−8 | 75.00
True value | 2.13×10−3 | -1.54×10−3 | 4.17×10−4 | 0.0 | 75.00

## Slide 34: Variational Equation
Structural Equilibrium
Variational equation
need to express in terms of and

## Slide 35: Frictionless Contact Formulation
Variation of the normal gap
Normal contact form
Contact force:
  positive contact force is in the same direction with , that is, a compressive force
Displacement variation:

## Slide 36: Linearization
It is clear that is independent of energy form
  The same can be used for elastic or plastic problem
It is nonlinear with respect to (need linearization)
Increment of gap function
  We assume that the contact boundary is straight line
  This is true for linear finite elements
  Refer to the book for the case when
Rigid surface

## Slide 37: Linearization cont.
Linearization of contact form
N-R iteration

## Slide 38: Ex) Frictionless Contact of a Block
Calculate displacement, penetration and contact force at the contact interface.
Plane strain: ,
Contact boundary:
Gap function:
Contact form:
Penalized potential energy
x
y
q
Rigid body
Elastic body
0
1
Contact boundary

## Slide 39: Ex) Frictionless Contact of a Block cont.
From , becomes a diagonal matrix, decoupled x & y
Since load is only y-direction,
Linear displacement in y-direction
Penalized potential
  Need to satisfy for arbitrary
As increases, penetration decreases but
contact force remains constant

## Slide 40: Ex) Frictionless Contact of a Block cont.
The product of penetration and penalty parameter remains constant
Penalty parameter | Displacement | Penetration (m) | Contact force (N)
True value |  | 0.0 | 
Penalty parameter | Displacement | Penetration (m) | Contact force (N)
True value |  | 0.0 | 

## Slide 41: Frictional Contact Formulation
frictional contact depends on load history
Frictional interface law – regularization of Coulomb law
Friction form

## Slide 42: Friction Force
During stick condition, (: regularization param.)
When slip occurs,
Modified friction form

## Slide 43: Linearization of Stick Form
Increment of slip
Increment of tangential vector
Incremental slip form for the stick condition

## Slide 44: Linearization of Slip Form
Parameter for slip condition:
Friction form:
Linearized slip form (not symmetric!!)

## Slide 45: Linearization
Let contact form
Linearization
N-R iteration
  Let be current load increment and be the current iteration counter
Contact form is independent of structural form
  Can be applied to different material models.

## Slide 46: Ex) Frictional Slip of a Cantilever Beam
Distributed load  axial load ,
Contact force:
Penalized potential energy (axial alone)
P=100N

## Slide 47: Ex) Frictional Slip of a Cantilever Beam
Linear axial displacement field:
Tangential slip in terms of displacement
  Parametric coordinate has an origin at , and it has the same length as the x-coordinate
Assume the stick condition:
The assumption is violated!!

## Slide 48: Ex) Frictional Slip of a Cantilever Beam
Assume the slip condition:
  With contact force ,

## Slide 49: Finite Element Formulation of Contact Problems
5.4

## Slide 50: Flexible-Rigid Body Contact
: a portion of the contact boundary where the contact body penetrates the target body
Contact between a contact node () and a straight target segment ( and )
Contact pair:
Approaches:
  (1) to find if the contact pair is in contact or in separation
  (2) to calculate the contact force and penetration if it is in contact

## Slide 51: Finite Element Formulation
Contact-Target contact
  The rigid body has fixed or prescribed displacement
  Point is projected onto the piecewise linear segments of the rigid body with as the projected point
  Unit normal and tangent vectors
g
et
en
Contact body
Target body
xc
x
x0
x1
x2
xs
L
xc0

## Slide 52: Finite Element Formulation cont.
Parameter at contact point
Gap function
  Contact occurs when and
Contact forces
  : integration weight (length of element)
  Contact force is in the direction of
Impenetrability condition

## Slide 53: Collocation Integral
Contact form is the integral along the boundary
Collocation integral: Numerical integration at node location
Discrete contact form
  Gauss quadrature is difficult because integration point node
  Collocation integral: integration points = node, weights =
  Weight represents the domain that an integration point covers
  calculating integration weight for general elements is difficult
  can be included in the gap by putting for all contact nodes
  can cause confusion interpreting the physical meaning of the gap

## Slide 54: Linearization
Discrete incremental form
  Tangent stiffness:
  Assembled contact stiffness:
N-R iteration
  Residual force

## Slide 55: Ex) Collocation Integration
Single element:
  when integration weight is ignored, i.e., ,
  When
  Analytical solution (slide 40): with :

## Slide 56: Ex) Collocation Integration
Four elements:
  when integration weight is ignored, uniform contact stress contact force is equally distributed two nodes ,
  When : ,
Therefore, including integration weights is correct
If integration weights are not used, gap includes integration weights

## Slide 57: Frictional Slip
Frictional slip
Friction force and tangent stiffness (stick condition)
Friction force and tangent stiffness (slip condition)

## Slide 58: Frictional Slip cont.
Tangential form
Linearized tangential form
N-R iteration
  Contact stiffness:
  Contact force:

## Slide 59: Flexible-Flexible Contact
Both contact and target bodies are deformable
  Equal and opposite contact force is applied at contact node and target segment need interpolate contact force at target segment
  Let contact force at a contact node
  Contact forces at target nodes are
  Contact forces at contact pair
g
et
en
Contact body
Target body
xc
x
x0
x1
x2
xs
L
xc0

## Slide 60: Flexible-Flexible Contact cont.
Variations of normal gap and tangential slip
Contact form and tangential form
Define augmented vectors
Additional term due to deformable target body

## Slide 61: Flexible-Flexible Contact cont.
Contact form
Linearization
  Stick condition
  Slip condition

## Slide 62: MATLAB Code for Contact Analysis
Define contact problem
%******************************************************************************
XYZC=[1.1 2; -0.1 2]; % Rigid body coordinates
CNODE=[5 6]; % Contact nodes
LEC=[7 8]; % Target segments
CDISP=[7 2 -0.2;8 2 -0.2]; % Prescribed displ. of rigid nodes
CONTPARM=[1E8 1E7 0.4]; % Contact parameters [wN, wT, friction coefficient]
CONTACT=struct('XYZC',XYZC,'XYZP',XYZC,'CDISP',CDISP,'CNODE',CNODE,... %
'LEC',LEC,'PARM',CONTPARM); % Contact structure
NLFEA(PARAM,NOUT,MID,PROP,[],SDISPT,XYZ,LE,CONTACT,[]); % Calling NLFEA
%******************************************************************************
  Rigid nodes: defined in XYZC
  Contact nodes: defined in CNODE
  Target segments: defined in LEC
  Prescribed displacements of rigid nodes: defined in CDISP
  Contact parameters: defined in CONTPARM
  Send to NLFEA using a structure: defined in CONTACT

## Slide 63: MATLAB Code for Contact Analysis cont.
Contact pair: defined using contact nodes & target segments
NLFEA calls CNTELM to calculate the global contact stiffness matrix and contact force vector
CNTELM calls CNTELM2D or ENTELM3D to calculate contact force and contact stiffness for each pair

## Slide 64
1 function CNTELM(CNT,XYZ,CDISP,NUMNP,LTAN)
2 %******************************************************************************
3 % COMPUTE CONTACT STIFFNESS & FORCE AND ASSEMBLE TO GLOBAL STIFFNESS & FORCE %
4 %******************************************************************************
5 %% %
6 global DISPTD FORCE GKF % Global variables
7 NCNT=size(CNT.CNODE,2); NTARG=size(CNT.LEC,1); % No. of contact pairs
8 NDOF=size(XYZ,2); NETARG=2^(NDOF-1); % Dimensions
9 ELXY=zeros(NDOF,NTARG+1); % Coordinates of contact pairs
10 ELXYP=zeros(NDOF,NTARG+1); % Coordinates at previous time
11 for ICNT=1:NCNT % Loop for contact nodes
12 IDOF=NDOF*(CNT.CNODE(ICNT)-1)+(1:NDOF); % Contact node DOFs
13 ELXY(:,1)=XYZ(CNT.CNODE(ICNT),:)+DISPTD(IDOF)';% Coordinates of contact nodes
14 ELXYP(:,1)=XYZ(CNT.CNODE(ICNT),:)+CDISP(IDOF)';% Coordinates at previous time
15 for ITARG=1:NTARG % Loop for target segments
16 if CNT.LEC(ITARG,1)>NUMNP % Target nodes are rigid
17 for i=1:NETARG % Loop for all nodes in current target segment
18 ELXY(:,i+1)=XYZ(CNT.LEC(ITARG,i),:); % Coordinates of target nodes
19 ELXYP(:,i+1)=CNT.XYZP(CNT.LEC(ITARG,i)-NUMNP,:); % Coord. at previous time
20 end % End of for i loop
21 else % Target nodes are flexible
22 for i=1:NETARG % Loop for all nodes in current target segment
23 JDOF=NDOF*(CNT.LEC(ITARG,i)-1)+(1:NDOF); % DOF of flexible target nodes
24 ELXY(:,i+1)=XYZ(CNT.LEC(ITARG,i),:)+DISPTD(JDOF)'; % Current coordinates
25 ELXYP(:,i+1)=XYZ(CNT.LEC(ITARG,i),:)+CDISP(JDOF)'; % Previous coordinates
26 IDOF=[IDOF JDOF]; % Accumulated DOFs of flexible nodes
27 end % End of for i loop
28 end % End of if CNT.LEC(ITARG,1)>NUMNP loop
29 NFLEX=size(IDOF,2); % No of flexible DOFs in contact pair
30 if NDOF == 2 % 2D contact branch
31 [F,KC]=CNTELM2D(ELXY,ELXYP,CNT.PARM); % 2D contact force and stiffness
32 else % 3D contact branch
33 [F,KC]=CNTELM3D(ELXY,ELXYP,CNT.PARM); % 3D contact force and stiffness
34 end % End of if NDOF branch
35 if ~isempty(F) % F & KC are non-empty when contact occurs
36 FORCE(IDOF)=FORCE(IDOF)+F(1:NFLEX); % Assemble contact force
37 if LTAN, GKF(IDOF,IDOF)=GKF(IDOF,IDOF)+KC(1:NFLEX,1:NFLEX); end % stiffness
38 break; % Stop checking other target segments. One target per contact node
39 end % End of if ~isempty(F) branch
40 IDOF=NDOF*(CNT.CNODE(ICNT)-1)+(1:NDOF); % Contact node DOFs
41 end % End of target segment loop
42 end % End of contact node loop
43 end % End of function

## Slide 65
45 function [F,KC]=CNTELM2D(ELXY,ELXYP,PARM)
46 %******************************************************************************
47 % COMPUTE CONTACT STIFFNESS AND FORCE FOR 2D CONTACT PAIR %
48 %******************************************************************************
49 %% %
50 F=[]; KC=[]; % Return null when no contact
51 XT=ELXY(:,3)-ELXY(:,2); XLEN=norm(XT); % Tangent target segment
52 if XLEN < 1E-6, return; end % Error in target segment definition
53 XTP=ELXYP(:,3)-ELXYP(:,2); XLENP = norm(XTP); % Tangent at previous time
54 XT=XT/XLEN; % Unit tangent vector
55 XTP=XTP/XLENP; % Unit tangent at previous time
56 XN=[-XT(2); XT(1)]; % Unit normal vector
57 GN=(ELXY(:,1)-ELXY(:,2))'*XN; % Gap b/w contact and target
58 ALPHA=(ELXY(:,1)-ELXY(:,2))'*XT/XLEN; % Parametric coordinate
59 ALPHA0=((ELXYP(:,1)-ELXYP(:,2))'*XTP)/XLENP; % Param. coord. at previous time
60 if (ALPHA>1.05)||(ALPHA<-0.05)||(GN>=0)||(GN<=-XLEN), return; end %
61 XLAMBN=-PARM(1)*GN; % Normal contact force
62 GT=(ALPHA-ALPHA0)*XLENP; % Tangential slip
63 XLAMBT=-PARM(2)*GT; % Tangential force for stick cond.
64 FRTOL=PARM(3)*XLAMBN; % Criterion for stick/slip condition
65 NN=[XN; -(1-ALPHA)*XN; -ALPHA*XN]; % Augmented normal vector
66 TT=[XT; -(1-ALPHA)*XT; -ALPHA*XT]; % Augmented tangential vector
67 if abs(XLAMBT)>FRTOL % Slip condition
68 XLAMBT=-FRTOL*sign(GT); % Tangential force for slip condition
69 KC=PARM(1)*(NN*NN')-PARM(3)*PARM(1)*sign(GT)*(TT*NN'); % Contact stiffness
70 else % Stick condition
71 KC=PARM(1)*(NN*NN')+PARM(2)*(TT*TT'); % Contact stiffness
72 end % End of stick/slip branch
73 F= XLAMBN*NN+XLAMBT*TT; % Contact force
74 end % End of function
Refer to the book for detailed explanations of the codes

## Slide 66: Ex) Contact Compression of Two Elements
Two plane-strain elements are under contact with a rigid wall on the top. The rigid wall moves down by , , , and
%******************************************************************************
% Two-element contact example 2D plane strain %
%******************************************************************************
XYZ=[0 0; 1 0; 0 1; 1 1; 0 2; 1 2]; % Nodal coordinates
LE=[1 2 4 3;3 4 6 5]; % Element connectivity
SDISPT=[1 1 0;1 2 0;2 2 0;3 1 0;5 1 0]; % Prescribed displ. [Node, DOF, Value]
TIMS=[0.0 1.0 0.2 0.0 1.0]'; % Load increments [Start End Increment IF FF]
MID=0; PROP=[2E6 0.3]; % Linear elastic material PROP=[E NU]
XYZC=[-0.1 2; 1.1 2]; % Rigid body coordinates
CNODE=[5 6]; % Contact nodes
LEC=[8 7]; % Target segments
CDISP=[7 2 -0.2;8 2 -0.2]; % Prescribed displ. of rigid nodes
CONTPARM=[1E8 1E7 0.4]; % Contact parameters [wN, wT, friction coefficient]
CONTACT=struct('XYZC',XYZC,'XYZP',XYZC,'CDISP',CDISP,'CNODE',CNODE,... %
'LEC',LEC,'PARM',CONTPARM); % Contact structure
PARAM=struct('ITRA',70,'ATOL',1.0E5,'NTOL',6,'TOL',1E-6,'TIMS',TIMS); % Param.
NOUT=fopen('output.txt','w'); % Output file
NLFEA(PARAM,NOUT,MID,PROP,[],SDISPT,XYZ,LE,CONTACT,[]); % Calling NLFEA
%******************************************************************************

## Slide 67
TIME = 1.000e+00
Nodal Displacements
Node U1 U2
1 0.000e+00 0.000e+00
2 4.522e-02 0.000e+00
3 1.631e-18 -1.066e-01
4 4.508e-02 -9.968e-02
5 0.000e+00 -1.989e-01
6 1.055e-02 -1.988e-01
Element Stresses
S11 S22 S33 S12 S23 S13
Element 1
3.329e+02 -2.310e+05 -6.919e+04 1.107e+03 0.000e+00 0.000e+00
1.199e+02 -2.311e+05 -6.928e+04 4.193e+03 0.000e+00 0.000e+00
4.962e+03 -2.202e+05 -6.456e+04 1.046e+03 0.000e+00 0.000e+00
4.749e+03 -2.203e+05 -6.465e+04 4.132e+03 0.000e+00 0.000e+00
Element 2
-6.453e+03 -2.088e+05 -6.458e+04 -1.375e+03 0.000e+00 0.000e+00
-6.013e+04 -2.318e+05 -8.759e+04 -4.396e+03 0.000e+00 0.000e+00
-1.099e+04 -2.194e+05 -6.911e+04 -1.671e+04 0.000e+00 0.000e+00
-6.466e+04 -2.424e+05 -9.212e+04 -1.973e+04 0.000e+00 0.000e+00
Contact Forces
Node F1 F2
5 0.000e+00 -1.056e+05
6 -3.302e+04 -1.200e+05
*** Successful end of program ***
Nodal displacements
Element stresses
Contact forces

## Slide 68: 3D Contact Analysis
5.5

## Slide 69: 3D Contact Formulation
Two tangent vectors:
  Two parameters:
  Use FE shape functions
Consistency condition (closest projection)
  Need local N-R method to find

## Slide 70: 3D Contact Formulation cont.
Contact search
  Contact occurs in this target element if and
  Gap
Contact force and tangent stiffness only for violated pairs
  Contact force
  Tangent stiffness
Tangential slip with friction
  Tangential slip:
  Tangent vector
Previous contact point
This is not in the parametric direction but the slip direction

## Slide 71: 3D Contact Formulation cont.
Contact force and tangent stiffness
Matlab implementation
  Contact pair (1 contact node, 4 target nodes)
  Augmented arrays

## Slide 72: CNTELM3D
1 function [F,KC]=CNTELM3D(ELXY,ELXYP,PARM)
2 %******************************************************************************
3 % COMPUTE CONTACT STIFFNESS AND FORCE FOR 3D CONTACT PAIR %
4 %******************************************************************************
5 %% %
6 F=[]; KC=[]; % Return null when no contact
7 [T1,T2,XC,XS,~]=CUTL(0,0,ELXY); % Two tangent vectors and contact nodes
8 XN=cross(T1,T2); XN=XN/norm(XN); % Unit normal vector at the center
9 XI=(XS'*T1)/(norm(T1)^2); % Parametric coord. along T1 dir.
10 ETA=(XS'*T2)/(norm(T2)^2); % Parametric coord. along T2 dir.
11 GN=XN'*XS; % Gap in the normal dir.
12 XX=(ELXY(:,1)-ELXY(:,2)+ELXY(:,3)-ELXY(:,4))/4; % 2nd-derivative of Xc
13 if((abs(XI)>1.2)||(abs(ETA)>1.2)||GN>0.1), return; end % No contact occurs
14 for ICOUNT=1:20 % NR iteration to find contact point
15 [T1,T2,XC,XS,AN] = CUTL(XI,ETA,ELXY); % Two tangent vectors and contact nodes
16 A=[-T1'*T1, XS'*XX-T2'*T1; XS'*XX-T2'*T1, -T2'*T2]; % Jacobian of NR
17 B=[-XS'*T1; -XS'*T2]; % Residual of NR
18 DXI=A\B; % Incremental parametric coordinates
19 XI=XI+DXI(1); ETA=ETA+DXI(2); % Update parametric coordinates
20 if(norm(DXI)<1.E-6), break; end % Converged NR iteration
21 end % End of local N-R loop
22 XN=cross(T1,T2); XN=XN/norm(XN); % Unit normal vector at contact point
23 GN=XN'*XS; % Gap in the normal dir.
24 if((abs(XI)>1.05)||(abs(ETA)>1.05)||GN>0), return; end % No contact occurs
25 XX=(ELXYP(:,1)-ELXYP(:,2)+ELXYP(:,3)-ELXYP(:,4))/4; % 2nd-derivative of Xc
26 XIP=XI; ETAP=ETA; % Previous parametric coordinates
27 for ICOUNT=1:20 % NR iteration to find contact point
28 [T1P,T2P,~,XSP,~] = CUTL(XIP,ETAP,ELXYP); % Tangent vectors & contact nodes
29 A=[-T1P'*T1P, XSP'*XX-T2P'*T1P; XSP'*XX-T2P'*T1P, -T2P'*T2P];% Jacobian of NR
30 B=[-XSP'*T1P; -XSP'*T2P]; % Residual of NR
31 DXIP=A\B; % Incremental parametric coordinates
32 XIP=XIP+DXIP(1); ETAP=ETAP+DXIP(2); % Update parametric coordinates
33 if(norm(DXIP)<1.E-6), break; end % Converged NR iteration
34 end % End of local N-R loop

## Slide 73: CNTELM3D cont.
35 [~,~,XCP,~,~] = CUTL(XIP,ETAP,ELXY); % Previous contact point
36 GT=XC-XCP; XT=GT/norm(GT); % Tangential slip & unit vector
37 if norm(GT)<1E-10, XT=(T1+T2)/norm(T1+T2); end % Tangent vector with zero slip
38 NN=XN*AN; NN=reshape(NN,[],1); % Augmented normal vector
39 TT=XT*AN; TT=reshape(TT,[],1); % Augmented tangential vector
40 TT1=T1/norm(T1)*AN; TT1=reshape(TT1,[],1); % Augmented tangent 1 vector
41 TT2=T2/norm(T2)*AN; TT2=reshape(TT2,[],1); % Augmented tangent 2 vector
42 XLAMBN=-PARM(1)*GN; % Normal contact force
43 XLAMBT=-PARM(2)*norm(GT); % Tangential force for stick cond.
44 if abs(XLAMBT)>PARM(3)*XLAMBN % Slip condition
45 XLAMBT=-PARM(3)*XLAMBN; % Tangential force for slip condition
46 KC=PARM(1)*(NN*NN')-PARM(3)*PARM(1)*(TT*NN'); % Contact stiffness
47 else % Stick condition
48 KC=PARM(1)*(NN*NN')+PARM(2)*(TT1*TT1'+TT2*TT2'); % Contact stiffness
49 end % End of if abs(XLAMBT)>PARM(3)*XLAMBN
50 F= XLAMBN*NN+XLAMBT*TT; % Contact force
51 end %
52 %
53 function [T1,T2,XC,XS,AN] = CUTL(XI,ETA,ELXY)
54 %******************************************************************************
55 % COMPUTE COORD. OF CENTEROID AND TWO TANGENT VECTORS %
56 %******************************************************************************
57 %% %
58 XN=[-1 1 1 -1; -1 -1 1 1]; % Parametric coordinates of 4 nodes
59 T1=zeros(3,1); T2=T1; XC=T1; XS=T1; % Definition of vectors
60 for J = 1:3 % Loop for coord. dir.
61 T1(J)=sum(XN(1,:).*(1+ETA*XN(2,:)).*ELXY(J,2:5)./4); % Tangent 1 vector
62 T2(J)=sum(XN(2,:).*(1+XI *XN(1,:)).*ELXY(J,2:5)./4); % Tangent 2 vector
63 XC(J)=sum((1+XI*XN(1,:)).*(1+ETA*XN(2,:)).*ELXY(J,2:5)./4); % Contact point
64 XS(J)=ELXY(J,1)-XC(J); % Relative contact node location
65 end % End of coord. dir. loop
66 AN=[1 -(1+XI*XN(1,:)).*(1+ETA*XN(2,:))/4]; % Augmented shape function vector
67 end %

## Slide 74: Ex) Contact Compression of Two 3D Elements
Rigid wall moves down by , , , , and
%******************************************************************************
% Two-element contact example 3D %
%******************************************************************************
XYZ=[0 0 0; 1 0 0; 0 1 0; 1 1 0; 0 2 0; 1 2 0; % Nodal coordinates
0 0 1; 1 0 1; 0 1 1; 1 1 1; 0 2 1; 1 2 1]; %
LE=[1 2 4 3 7 8 10 9; % Element connectivity
3 4 6 5 9 10 12 11]; %
SDISPT=[1 1 0;1 2 0;1 3 0;2 2 0;2 3 0;3 1 0;3 3 0; % Prescribed displacements
4 3 0;5 1 0;5 3 0;6 3 0;7 1 0;7 2 0;7 3 0; %
8 2 0;8 3 0;9 1 0;9 3 0;10 3 0;11 1 0;11 3 0;12 3 0]; %
TIMS=[0.0 1.0 0.2 0.0 1.0]'; % Load increments [Start End Increment IF FF]
MID=0; PROP=[2E6, 0.3]; % Linear elastic material PROP=[E NU]
XYZC=[-0.1 2 -0.1; 1.1 2 -0.1; -0.1 2 1.1; 1.1 2 1.1]; % Rigid body coordinates
CNODE=[5 6 11 12]; % Contact nodes
CDISP=[13 2 -0.2;14 2 -0.2;15 2 -0.2;16 2 -0.2]; % Displacementd of rigid nodes
LEC=[13 14 16 15]; % Target element
CONTPARM=[0.5E8 0.5E7 0.4]; % Contact parameters [wN, wT, friction coeff.]
CONTACT=struct('XYZC',XYZC,'XYZP',XYZC,'CDISP',CDISP,'CNODE',CNODE,... %
'LEC',LEC,'PARM',CONTPARM); % Contact structure
PARAM=struct('ITRA',70,'ATOL',1.0E5,'NTOL',6,'TOL',1E-6,'TIMS',TIMS); % Param.
NOUT=fopen('output.txt','w'); % Output file
NLFEA(PARAM,NOUT,MID,PROP,[],SDISPT,XYZ,LE,CONTACT,[]); % Calling NLFEA
%******************************************************************************

## Slide 75: Contact Analysis Procedure and Modeling Issues
5.6

## Slide 76: Types of Contact Interface
Weld contact
  A contact node is bonded to the target segment (no relative motion)
  Conceptually same with rigid-link or MPC
  For contact purpose, it allows a slight elastic deformation
  Decompose forces in normal and tangential directions
Rough contact
  Similar to weld, but the contact can be separated
Stick contact
  The relative motion is within an elastic deformation
  Tangent stiffness is symmetric,
Slip contact
  The relative motion is governed by Coulomb friction model
  Tangent stiffness become unsymmetric

## Slide 77: Contact Search
Easiest case
  User can specify which contact node will contact with which target segment
  This is only possible when deformation is small and no relative motion exists in the contact surface
  Contact and target nodes are often located at the same position and connected by a compression-only spring (node-to-node contact)
  Works for very limited cases
General case
  User does not know which contact node will contact with which target segment
  But, user can specify candidates
  Then, the contact algorithm searches for contacting target segment for each contact node
  Time consuming process, because this needs to be done at every iteration

## Slide 78: Contact Search cont.
Node-to-surface contact search
Surface-to-surface contact search

## Slide 79: Contact-Target Contact
Theoretically, there is no need to distinguish Body 1 from Body 2
However, the distinction is often made for numerical convenience
One body is called a contact body, while the other body is called a target body
Contact condition: the contact body cannot penetrate into the target body
The target body can penetrate into the contact body (physically not possible, but numerically it’s not checked)
Slave
Master

## Slide 80: Contact-Target Contact cont.
Contact condition between a contact node and a target segment
In 2D, contact pair is often given in terms of
Contact node is projected onto the piecewise linear segments of the target segment with as the projected point
Gap:
: no contact
: contact
xs
g
et
en
Contact
Target
xc
x
x0
x1
x2
L
xc0

## Slide 81: Contact Formulation (Two-Step Procedure)
Search nodes/segments that violate contact constraint
Apply contact force for the violated nodes/segments (contact force)
Contact force
Violated nodes
Body 1
Body 2
Contact candidates

## Slide 82: Contact Tolerance and Load Increment
Contact tolerance
  Minimum distance to search for contact (1% of element length)
Load increment and contact detection
  Too large load increment may miss contact detection
Out of contact
Within tolerance
Out of contact

## Slide 83: Contact Force
For those contacting pairs, penetration needs to be corrected by applying a force (contact force)
More penetration needs more force
Penalty-based contact force (compression-only spring)
Penalty parameter (): Contact stiffness
  It allows a small penetration ()
  It depends on material stiffness
  The bigger , the less allowed penetration
x
xc
x1
x2
g < 0
FC

## Slide 84: Contact Stiffness
Contact stiffness depends on the material stiffness of contacting two bodies
Large contact stiffness reduces penetration, but can cause problem in convergence
Proper contact stiffness can be determined from allowed penetration (need experience)
Normally expressed as a scalar multiple of material’s elastic modulus
Start with small initial SF and increase it gradually until reasonable penetration

## Slide 85: Lagrange Multiplier Method
In penalty method, the contact force is calculated from penetration
  Contact force is a function of deformation
Lagrange multiplier method can impose contact condition exactly
  Contact force is a Lagrange multiplier to impose impenetrability condition
  Contact force is an independent variable
Complimentary condition
Stiffness matrix is positive semi-definite
Contact force is applied in the normal direction to the master segment

## Slide 86: Observations
Contact force is an internal force at the interface
  Newton’s 3rd law: equal and opposite forces act on interface
Due to discretization, force distribution can be different, but the resultants should be the same
pC1
pC2
F
qC1
qC2
qC2
F

## Slide 87: Contact Formulation
Add contact force as an external force
Ex) Linear elastic materials
Contact force depends on displacement (nonlinear, unknown)
pC1
pC2
F
qC1
qC2
qC2
F
Contact force
Internal force
External force
Contact stiffness
Tangent stiffness
Residual

## Slide 88: Friction Force
So far, contact force is applied to the normal direction
  It is independent of load history (potential problem)
Friction force is produced by a relative motion in the interface
  Friction force is applied to the parallel direction
  It depends on load history (path dependent)
Coulomb friction model
Body 1
Contact force
Friction force
Relative motion
Friction force

## Slide 89: Friction Force cont.
Coulomb friction force is indeterminate when two bodies are stick (no unique determination of friction force)
In reality, there is a small elastic deformation before slip
Regularized friction model
  Similar to elasto-perfectly-plastic model
Relative motion
Friction force
: tangential stiffness

## Slide 90: Tangential Stiffness
Tangential stiffness determines the stick case
It is related to shear strength of the material
Contact surface with a large behaves like a rigid body
Small elongate elastic stick condition too much (inaccurate)
Relative motion
Friction force

## Slide 91: Selection of Target and Contact Surfaces
Contact constraint
  A contact node CANNOT penetrate the target segment
  A target node CAN penetrate the contact segment
  There is not much difference in a fine mesh, but the results can be quite different in a coarse mesh
How to choose target and contact
  Rigid surface to a target
  Convex surface to a contact
  Fine mesh to a contact
Slave
Master
Master
Slave

## Slide 92: Selection of Target and Contact Surfaces
How to prevent penetration?
  Can define contact-target pair twice by changing the role
  Some surface-to-surface contact algorithms use this
  Careful in defining contact-target pairs
Contact-target pair 1
Contact-target pair 2

## Slide 93: Flexible or Rigid Bodies?
Flexible-Flexible Contact
  Body1 and Body2 have a similar stiffness and both can deform
Flexible-Rigid Contact
  Stiffness of Body2 is significantly larger than that of Body1
  Body2 can be assumed to be a rigid body (no deformation but can move)
  Rubber contacting to steel
Why not flexible-flexible?
  When two bodies have a large difference in stiffness, the matrix becomes ill-conditioned
  Enough to model contacting surface only for Body2
Friction in the interface
  Friction makes the contact analysis path-dependent
  Careful in the order of load application

## Slide 94: Effect of discretization
Contact stress (pressure) is high on the edge
Contact stress is sensitive to discretization
Contact body
Uniform pressure
Non-uniform contact stress

## Slide 95: Rigid-Body Motion
Contact constraint is different from displacement BC
  Contact force is proportional to the penetration amount
  A contact body between two rigid-bodies can either fly out or oscillate between two surfaces
  Always better to remove rigid-body motion without contact
Rigid target
Rigid target
Rigid target
Rigid target

## Slide 96: Rigid-Body Motion
When a body has rigid-body motion, an initial gap can cause singular matrix (infinite/very large displacements)
Same is true for initial overlap
Rigid target
Rigid target

## Slide 97: Rigid-Body Motion
Removing rigid-body motion
  A small, artificial bar elements can be used to remove rigid-body motion without affecting analysis results much
Contact stress at bushing due to shaft bending

## Slide 98: Convergence Difficulty at a Corner
Convergence iteration is stable when a variable (force) varies smoothly
The slope of finite elements are discontinuous along the curved surface
This can cause oscillation in residual force (not converging)
Need to make the corner smooth using either higher-order elements or many linear elements
  About 10 elements in 90 degrees, or use higher-order elements

## Slide 99: Curved Contact Surface
Curved surface
  Contact pressure is VERY sensitive to the curvature
  Linear elements often yield unsmooth contact pressure distribution
  Less quadratic elements is better than many linear elements
Linear elements
Quadratic elements

## Slide 100: Summary
Contact condition is a rough boundary nonlinearity due to discontinuous contact force and unknown contact region
  Both force and displacement on the contact boundary are unknown
  Contact search is necessary at each iteration
Penalty method or Lagrange multiplier method can be used to represent the contact constraint
  Penalty method allows a small penetration, but easy to implement
  Lagrange multiplier method can impose contact condition accurately, but requires additional variables and the matrix become positive semi-definite
Numerically, contact-target concept is used along with collocation integration (at contact nodes)
Friction makes the contact problem path-dependent
Discrete boundary and rigid-body motion makes the contact problem difficult to solve