## Slide 1: Finite Element Analysis Using Abaqus
Instructor: Nam-Ho Kim (nkim@ufl.edu)

## Slide 2: Abaqus Basics
Simulation
Abaqus/Standard
Output file:
Job.odb, job.dat
Postprocessing
Abaqus/CAE
Preprocessing
Abaqus/CAE
Interactive Mode
Analysis Input file
Input file (text):
Job.inp
FEM Solver

## Slide 3: Methods of Analysis in ABAQUS
Interactive mode
  Create an FE model and analysis using GUI
  Advantage: Automatic discretization and no need to remember commands
  Disadvantage: No automatic procedures for changing model or parameters
Python script
  All GUI user actions will be saved as Python script
  Advantage: Users can repeat the same command procedure
  Disadvantage: Need to learn Python script language

## Slide 4: Methods of Analysis in ABAQUS
Analysis input file
  ABAQUS solver reads an analysis input file
  Possible to manually create an analysis input file
  Advantage: Users can change model directly without GUI
  Disadvantage: Users have to discretize model and learn ABAQUS input file grammar

## Slide 5: Components in ABAQUS Model
Geometry modeling (define geometry)
Creating nodes and elements (discretization)
Element section properties (area, moment of inertia, etc)
Material data (linear/nonlinear, elastic/plastic, isotropic/orthotropic, etc)
Loads and boundary conditions (nodal force, pressure, gravity, fixed displacement, joint, relation, etc)
Analysis type (linear/nonlinear, static/dynamic, etc)
Output requests

## Slide 6: FEM Modeling

## Slide 7: FEM Modeling
Pressure
Which analysis type?
Which element type?
  Section properties
  Material properties
  Loads and boundary conditions
  Output requests
Beam element
Solid element

## Slide 8: FEM Modeling
Line (Beam element)
- Assign section properties (area, moment of inertia)
- Assign material properties
Volume (Solid element)
- Assign section properties
- Assign material properties

## Slide 9: FEM Modeling
Line (Beam element)
- Apply distributed load “on the line”
- Apply fixed BC “at the point”
Volume (Solid element)
- Apply distribution load “on the surface”
- Apply fixed BC “on the surface”
fixed BC
fixed BC

## Slide 10: FEM Modeling
Line (Beam element)
- Discretized geometry with beam element
- Discretized BC and load on nodes
Volume (Solid element)
- Discretized geometry with solid element
- Discretized BC and load on nodes

## Slide 11: Start Abaqus/CAE
Startup window

## Slide 12: Example: Overhead Hoist

## Slide 13: Units
Quantity | SI | SI (mm) | US Unit (ft) | US Unit (inch)
Length | m | mm | ft | in
Force | N | N | lbf | lbf
Mass | kg | tonne (103 kg) | slug | lbf s2/in
Time | s | s | s | s
Stress | Pa (N/m2) | MPa (N/mm2) | lbf/ft2 | psi (lbf/in2)
Energy | J | mJ (10–3 J) | ft lbf | in lbf
Density | kg/m3 | tonne/mm3 | slug/ft3 | lbf s2/in4
Abaqus does not have built-in units
Users must use consistent units

## Slide 14: Create Part
Parts
  Create 2D Planar, Deformable, Wire, Approx size = 4.0
  Provide complete constrains and dimensions
  Merge duplicate points

## Slide 15: Geometry Constraint
Define exact geometry
  Add constraints
  Add dimension
  Over constraint warning

## Slide 16: Geometry Modification
Modify geometry modeling
  1. Go back to the sketch
  2. Update geometry

## Slide 17: Define Material Properties
Materials
  Name: Steel
  Mechanical Elasticity Elastic

## Slide 18: Define Section Properties
Calculate cross-sectional area using CLI (diameter = 5mm)
Sections
  Name: Circular_Section
  Beam, Truss
  Choose material (Steel)
  Write area

## Slide 19: Define Section Properties
Assign the section to the part
  Section Assignments
  Select all wires
  Assign Circular_Section

## Slide 20: Assembly and Analysis Step
Different parts can be assembled in a model
Single assembly per model
Assembly
  Instances: Choose the frame wireframe
Analysis Step
  Configuring analysis procedure
Steps
  Name: Apply Load
  Type: Linear perturbation
  Choose Static, Linear perturbation

## Slide 21: Assembly and Analysis Step
Examine Field Output Request (automatically requested)
User can change the request

## Slide 22: Boundary Conditions
Boundary conditions: Displacements or rotations are known
BCs
  Name: Fixed
  Step: Initial
  Category: Mechanical
  Type: Displacement/Rotation
  Choose lower-left point
  Select U1 and U2
Repeat for lower-right corner
  Fix U2 only

## Slide 23: Applied Loads
Loads
  Name: Force
  Step: Applied Load
  Category: Mechanical
  Type: Concentrated force
Choose lower-center point
CF2 = -10000.0

## Slide 24: Meshing the Model
Parts
  Part-1, Mesh
Menu Mesh, Element Types (side menu )
Select all wireframes
Library: Standard
Order: Linear
Family: Truss
T2D2: 2-node linear 2-D truss

## Slide 25: Meshing the Model
Seed a mesh
  Control how to mesh (element size, etc)
Menu Seed, Part (side menu )
  Global size = 1.0
Menu Mesh, Part, Yes (side menu )
Menu View, Part Display Option
  Label on

## Slide 26: Mesh Modification
Menu Seed, Part (side menu )
  Change the seed size (Global size) 1.0 to 0.5
  Delete the previous mesh
Menu Mesh, Part, Yes (side menu )

## Slide 27: Creating an Analysis Job
Jobs
Jobs, Truss
  Data Check
  Monitor
  Continue (or, submit)

## Slide 28: Postprocessing
Change “Model” tab to “Results” tab
Menu File, Open Job.odb file
Common Plot Option (side menu ), click on the Labels tab
(Show element labels, Show node labels)
Set Font for All Model Labels…

## Slide 29: Postprocessing
Deformation scale
Common Plot Option (side menu ), click on the Basic tab, Deformation Scale Factor area

## Slide 30: Postprocessing
Tools, XY Data, Manager
  Position: Integration Point
  Stress components, S11 (Try with displacements and reaction)

## Slide 31: Postprocessing
  Click on the Elements/Nodes tab
  Select Element/Nodes you want to see result and save
  Click Edit… to see the result

## Slide 32: Postprocessing
Report, Field Output
  Position: Integration Point
  Stress components, S11 (Try with displacements and reaction)
  Default report file name is “abaqus.rpt”
  The report file is generated in “C:\temp” folder

## Slide 33: Save
Save job.cae file
Menu, File, Save As…
- job.cae file is saved
- job.jnl file is saved as well (user action history, python code)