## Slide 1: Tutorial 2: Abaqus with Analysis Input File

## Slide 2: Abaqus Basics
Simulation
Abaqus/Standard
Output file:
Job.odb, job.dat
Postprocessing
Abaqus/CAE
Preprocessing
Abaqus/CAE
Interactive Mode
Analysis Input file
Input file (text):
Job.inp
FEM Solver

## Slide 3: Why do I go with input files?
Analysis with input files
  ABAQUS solver reads the analysis input file
  Advantage:
    User can change model directly without GUI
    FASTER than analysis using GUI
    Useful for minor modification (GUI automatically create an input file)
  Disadvantage:
    No visual information (should use GUI to check model layout)
    User has to discretize model

## Slide 4: Input File: frame.inp
*HEADING
Two-dimensional overhead hoist frame
SI units (kg, m, s, N)
1-axis horizontal, 2-axis vertical
*PREPRINT, ECHO=YES, MODEL=YES, HISTORY=YES
**
** Model definition
**
*NODE, NSET=NALL
101, 0., 0., 0.
102, 1., 0., 0.
103, 2., 0., 0.
104, 0.5, 0.866, 0.
105, 1.5, 0.866, 0.
*ELEMENT, TYPE=T2D2, ELSET=FRAME
11, 101, 102
12, 102, 103
13, 101, 104
14, 102, 104
15, 102, 105
16, 103, 105
17, 104, 105
*SOLID SECTION, ELSET=FRAME, MATERIAL=STEEL
** diameter = 5mm --> area = 1.963E-5 m^2
1.963E-5,
*MATERIAL, NAME=STEEL
*ELASTIC
200.E9, 0.3
Truss element
Solid section
Elastic material

## Slide 5: Input File: frame.inp
**
** History data
**
*STEP, PERTURBATION
10kN central load
*STATIC
*BOUNDARY
101, ENCASTRE
103, 2
*CLOAD
102, 2, -10.E3
*NODE PRINT
U,
RF,
*EL PRINT
S,
**********************************
** OUTPUT FOR ABAQUS QA PURPOSES
**********************************
*EL FILE
S,
*NODE FILE
U, RF
*END STEP
Truss element
Solid section
Elastic material
CLOAD
PERTURBATION STATIC

## Slide 6: Input File: frame.inp
*HEADING
Two-dimensional overhead hoist frame
SI units (kg, m, s, N)
1-axis horizontal, 2-axis vertical
*PREPRINT, ECHO=YES, MODEL=YES, HISTORY=YES
**
** Model definition
**
*NODE, NSET=NALL
101, 0., 0., 0.
102, 1., 0., 0.
103, 2., 0., 0.
104, 0.5, 0.866, 0.
105, 1.5, 0.866, 0.
*ELEMENT, TYPE=T2D2, ELSET=FRAME
11, 101, 102
12, 102, 103
13, 101, 104
14, 102, 104
15, 102, 105
16, 103, 105
17, 104, 105
*SOLID SECTION, ELSET=FRAME, MATERIAL=STEEL
** diameter = 5mm --> area = 1.963E-5 m^2
1.963E-5,
*MATERIAL, NAME=STEEL
*ELASTIC
200.E9, 0.3
**
** History data
**
*STEP, PERTURBATION
10kN central load
*STATIC
*BOUNDARY
101, ENCASTRE
103, 2
*CLOAD
102, 2, -10.E3
*NODE PRINT
U,
RF,
*EL PRINT
S,
**********************************
** OUTPUT FOR ABAQUS QA PURPOSES
**********************************
*EL FILE
S,
*NODE FILE
U, RF
*END STEP

## Slide 7: Format of Input File
Model data section
  Information required to define the structure being analyzed
History data section
  Type of simulation (static, dynamics, etc)
  The sequence of loading or events for which the response of the structure is required
  Divided into a sequence of steps
  Output request
Input file
  Composed of a number of option blocks (describing a part of the model)
  Each option block begins with a keyword line (starting with *), which is usually followed by one or more data lines.
  Description for the data lines (starting with **)

## Slide 8: Format of Input File cont.
Keyword line
  *ELEMENT, TYPE = T2D2, ELSET = FRAME
    Element set FRAME is 2-dimensional truss element
  *NODE, NSET=PART1
    All nodes below belong to a set PART1
  *ELEMENT, TYPE = T2D2,
  ELSET = FRAME
    Maximum 256 characters per line

## Slide 9: Format of Input File cont.
    Data line - Keyword line usually followed by data lines
    *NODE
    101, 0., 0., 0.
    102, 1., 0., 0.
    103, 2., 0., 0.
    104, 0.5, 0.866, 0.
    105, 1.5, 0.866, 0.
101
102
103
104
105

## Slide 10: Format of Input File cont.
*ELEMENT
11, 101, 102
12, 102, 103
13, 101, 104
14, 102, 104
15, 102, 105
16, 103, 105
17, 104, 105
101
102
103
104
105
12
11
13
14
15
16
17

## Slide 11: Format of Input File cont.
Model data
Heading
  The first option in any Abaqus input file must be *HEADING
  Description of the problem
    *HEADING
    Two-dimensional overhead hoist frame
    SI units (kg, m, s, N)
    1-axis horizontal, 2-axis vertical
Data file printing options
  Input file echo
    *PREPRINT, ECHO=YES, MODEL=YES, HISTORY=YES
Comments
  **
  ** Model definition
  **

## Slide 12: Format of Input File cont.
Element connectivity
  Keyword *ELEMENT specifies element type, element set
    *ELEMENT, TYPE=T2D2, ELSET=FRAME
    11, 101, 102
    12, 102, 103
    13, 101, 104
    14, 102, 104
    15, 102, 105
    16, 103, 105
    17, 104, 105
Section properties
  Keyword *SOLID SECTION specifies area, I, etc
    *SOLID SECTION, ELSET=FRAME, MATERIAL=STEEL
    ** diameter = 5mm --> area = 1.963E-5 m^2
    1.963E-5,

## Slide 13: Format of Input File cont.
Material properties
  Keyword *MATERIAL followed by various suboptions
    *MATERIAL, NAME=STEEL
    *ELASTIC
    200.E9, 0.3
History data
  Starts with keyword *STEP, followed by the title of the step
    *STEP, PERTURBATION
    10kN central load
Analysis procedure
  Use *STATIC immediately after *STEP
Boundary conditions
  Keyword *BOUNDARY
  (UX, UY, UZ, UR1, UR2, URS) = (1, 2, 3, 4, 5, 6)

## Slide 14: Format of Input File cont.
Boundary conditions cont.
  Format: Node number, first dof, last dof, displ value
    103, 2,2, 0.0
    103, 2,2
    103, 2
    101, 1
    101, 2
  Built in constraints
    ENCASTRE: Constraint on all displacements and rotations at a node
    PINNED: Constraint on all translational degrees of freedom
    XSYMM: Symmetry constraint about a plane of constant
    YSYMM: Symmetry constraint about a plane of constant
    ZSYMM: Symmetry constraint about a plane of constant
    XASYMM: Antisymmetry constraint about a plane of constant
    YASYMM: Antisymmetry constraint about a plane of constant
    ZASYMM: Antisymmetry constraint about a plane of constant

## Slide 15: Format of Input File cont.
Applied loads
  concentrated loads, pressure loads, distributed traction loads, distributed edge loads and moment on shells, nonzero boundary conditions, body loads, and temperature
    *CLOAD
    102, 2, -10.E3
Output request
  neutral binary file (.odb), printed text file (.dat), restart file (.res), binary result file (.fil)
    *EL PRINT
    S, E
    *NODE PRINT
    U,
    RF,
End of step
    *END STEP

## Slide 16: Modifying Input File
Multiple Sections (FRAME1 and FRAME2)
  Assign new section to element 6
    *ELEMENT, TYPE=T2D2, ELSET=FRAME1
    11, 101, 102
    12, 102, 103
    13, 101, 104
    14, 102, 104
    15, 102, 105
    16, 103, 105
    *ELEMENT, TYPE=T2D2, ELSET=FRAME2
    17, 104, 105
    *SOLID SECTION, ELSET=FRAME1, MATERIAL=STEEL
    ** diameter = 5mm --> area = 1.963E-5 m^2
    1.963E-5,
    *SOLID SECTION, ELSET=FRAME2, MATERIAL=STEEL
    2.0E-5,

## Slide 17: Modifying Input File (Made by ABAQUS)
Input files made by GUI
  Find the files in the work directory (to check where the directory is: Files > Set Work Directory)
  Automatically made by GUI when users submit a model (ex: [Jobname].inp)
  Edit the existing input file

## Slide 18: Run ABAQUS
Using Abaqus/CAE
  Import the input model
  Advantage: visually check FEM model
  Disadvantage: A couple of commands do not work (ex: text out request commands)

## Slide 19: Run ABAQUS
Using Command Prompt
Data check
  abaqus job=frame datacheck interactive
  Check for **ERROR or **WARNING
Solving the problem
  abaqus job=frame continue interactive
    Show frame.dat file

## Slide 20: Run ABAQUS
Basic commands in command prompt
  cd [directory name] : change directory to new directory
  (ex: cd test)
  cd / : change directory to root at once
  dir : see available files in current directory

## Slide 21: Batch Test
Running many jobs
  Useful to run many jobs at the same time
  Create a batch file (ex: multirun.bat)
Making a batch file
  Make an empty text file and write a list of files
  Change the file name and extension (ex: newname.txt -> multirun.bat)
(
abaqus job=frame-1 interactive
abaqus job=frame-2 interactive
abaqus job=frame-3 interactive
abaqus job=frame-4 interactive )