## Slide 1: Tutorial 3: Plane Beam

## Slide 2: CLAMPED-CLAMPED BEAM
E = 100 MPa,
Circular section with r = 20mm
Plot bending moment and shear force diagrams
q = 30 N/m
y
x
1
2
1 m
3
1 m

## Slide 3: CLAMPED-CLAMPED BEAM
Classification of Beam Elements
  Dimension (2D / 3D)
  Formulation type (Mindlin-2node / Mindlin-3node / Euler)
  Additional information (OS (open section) / H (hybrid) / OSH)
  B23H
2D
Cubic polynomial
Hybrid formulation

## Slide 4: CLAMPED-CLAMPED BEAM
Degree of freedoms for a beam element
  2D/3D (2D beam is a special case of the 3D beam)
  With translation (from the truss element)
  Do not confuse sign convention for displacements and forces
u11
u21
u31
θ11
u12
u22
u32
θ12
θ21
θ31
θ22
θ32
u11
u31
u12
u32
θ21
θ22
3D Beam
2D Beam

## Slide 5: CLAMPED-CLAMPED BEAM
Parts
  2D Planar, Deformable, Wire, App Size = 4
  Create lines: (-1, 0), (1, 0)
Materials
  Mechanical, Elasticity, Elastic
  Young’s modulus = 100E6, Poisson’s ratio = 0.3
Profiles
  Circular, r = 0.02
Sections
  Beam
Assign the section “Beam” to the part

## Slide 6: CLAMPED-CLAMPED BEAM
Beam cross section needs orientation (ex. Second moment of inertia)
n1 vector is (0, 0, -1) for plane beam (may not be modified for plane beam)
Tangent direction vector t is dependent to the direction of wire geometry

## Slide 7: CLAMPED-CLAMPED BEAM
Direction of wire geometry (t)
Direction of wire geometry (t)
Assigned beam orientation
Assigned beam orientation
CASE 1
CASE 2
M
M
V
V
M
M
V
V
2 (n2)
1 (t)
(n1)
2 (n2)
1 (t)
(n1)

## Slide 8: CLAMPED-CLAMPED BEAM
Assembly, Instance
Steps
  Linear perturbation, Static
Field output request
  Check SF, Section forces and moments
BCs
  Initial, Encastre (clamped)
Loads
  Mechanical, Pressure (force/length for beam) or Line load (force/length), select upward, Uniform, 30
Mesh
  Element type, “Classical beam theory” or Euler beam theory, Cubic polynomial, (B23), Global element size = 0.2

## Slide 9: CLAMPED-CLAMPED BEAM
Analysis, Create Job, Data Check, Submit
Results
Deformed plot, Stress plots
  Field output, Section points, Top or Bottom
Paths, Node list (first node #, last node #, inc)

## Slide 10: CLAMPED-CLAMPED BEAM
XYData, path, X Values = Sequence ID
  Field output, SM1
To adjust font size of the XYData plot
  Double click object to open a dialog box to adjust its properties (ex: double click the legend box to enlarge its font size)

## Slide 11: CLAMPED-CLAMPED BEAM
Sign Convention for force and moment
  Must not be confused with sign convention for displacements
  Users must make sure which sign convention is used in a FEA software
  Shear force and bending moment sign convention of ABAQUS for beam diagram
M
M
V
V
x
y
q = 30 N/m
y
x
1
2
2 m
3

## Slide 12: CLAMPED-CLAMPED BEAM
Common Plot Options
  Normals, check “Show normals”, “On element”
Module part, View, Part Display Options
  check “Render Beam Profile”

## Slide 13: CLAMPED-CLAMPED BEAM
Result
  Field output, SM1
  Shear force output (SF2) is not available for B23 element
Contour Plot Options
  Check “Show tick masks for line elements”

## Slide 14: CLAMPED-CLAMPED BEAM
Change element type
  Element type, “Timoshenko beam theory” or Mindling beam theory, Shear flexible, (B21), Global element size = 0.2
Field Output
  Shear force output (SF2) is available