## Slide 1: Tutorial 6-1: 3D Modeling

## Slide 2: CANTILEVER BEAM
3D cantilever beam
  E=210 Gpa, Poison ratio 0.3
  Thickness t = 0.5 m
1m
5m
100 kN-m

## Slide 3: CANTILEVER BEAM
Parts
  3D Planar, Deformable, Solid, Extrusion, App Size = 10
  Create lines (rectangle): (0, 0), (5, 1)
  Depth = 0.01
Materials
  Mechanical, Elasticity, Elastic
  Young’s modulus = 200E9, Poisson’s ratio = 0.3
Sections
  Solid, Homogeneous
Assign the section to the part

## Slide 4: CANTILEVER BEAM
Assembly, Instance
Steps
  Linear perturbation, Static
BCs
  Initial, Encastre + Displacement/Rotation, U2
Encastre
U1

## Slide 5: CANTILEVER BEAM
Loads
  Mechanical, Pressure, select upward, Uniform, 30
Mesh
  Hexa - structured mesh is default setting as it is possible
  Global element size = 1
Cantilever beam with 8-node solid
  Max v = 1.872 × 10-4 (Exact 1.5 × 10-4)
100 kN-m
1m
-50 kN-m
1m
50 kN-m
50 kN-m
-50 kN-m
0.5m

## Slide 6: BRACKET ANALYSIS
A bracket with a shaft hole
  E=210 Gpa, Poison ratio 0.3
  3D geometry modeling
  8-node hexa element with structure mesh

## Slide 7: PART MODULE
Parts
  Create Part-1
  3D, Extrude, Depth 0.1
0.15
R0.1
R0.05
0.25
0.05
Fillet
R0.02

## Slide 8: PART MODULE
Parts
  Create Cut / Circular Hole
  Dist. from Edge1 = 0.05 , Dist. from Edge2 = 0.05, Diameter 0.035
  Do it again for the opposite side
Tip
  Create a hole then edit those parameters (the cut circular hole is categorized as a feature of a part)
0.05
0.05
R0.035

## Slide 9: PART MODULE
Parts
  Create Cut / Extrude
  Select a planar, select an edge
  Make a circle and three edges, click “done” button
  Do it again for the opposite side

## Slide 10: PROPERTY / ASSEMBLY / STEPS MODULES
Materials
  Mechanical, Elasticity, Elastic
  Young’s modulus = 210E9, Poisson’s ratio = 0.3
Sections
  Solid, Homogeneous
Assign the section to the part
Assembly, Instance
Steps
  Linear perturbation, Static

## Slide 11: INTERACTION MODULE (MPC)
How to apply loads at the center of shaft hole?
  Side tool bar/Create a reference point (RP-3) at the center of the shaft hole (RP-1 and RP-2 are the center of circles) Note: We need only one reference point RP-1 and RP-2 were made to show where they are
  Menu/Constraint/Create/MPC Constraint MPC (Multiple point constraints)
  Select the RP-3 as the MPC control point (master node)
  Select the surface (magenta area) of the hole shaft as the slave nodes
  MPC type select as of Beam
Reference Points
Applied Beam type MPCs

## Slide 12: LOADS MODULE
BCs
  Step1, ENCASTRE
  Step1, Displacement/Rotation, y-dir
Loads
  Step1, CF1 = 1000 N, CF2 = -1000 N on the master node of the MPC
1000 N
-1000 N

## Slide 13: MESH MODULE
Mesh (Partitioning)
  Partition Cell
  Select Point & Normal, Click “Done”
Tip
  A color of a volume indicates the best meshing method
  If a color of a volume is dark orange, the volume can not be meshed that partitioning is needed
  If the structured mesh is applicable for a volume, the color will be green

## Slide 14: MESH MODULE
Mesh
  Hexa - structured mesh is default setting as it is possible
  Global element size = 0.08
Tip
  Mesh shape can be distorted by geometric modeling: The rectangle represents start/end point of the circle
Analysis, Create Job, Data Check, Submit
Results

## Slide 15: Tutorial 6-2: Heat Transfer

## Slide 16: HEAT CONDUCTION
Fire in the subway tunnel (Heat Deterioration)
  Aluminum alloy
  Thermal conductivity Concrete: k=1.7 W/(m·K) Soil: k=1.5 W/(m·K)
1m
1m
Concrete
Soil
Heat flux
250 W/m2
Temperature
5 °C (41 °F)

## Slide 17: HEAT CONDUCTION
Parts
  Create Part-1
  3D, Extrude, Depth 1 m
Materials
  Thermal, Conductivity
  Concrete: 1.7 W/(m·K), Soil: 1.5 W/(m·K)
Sections
  Solid, Homogeneous
  Concrete section, Soil section
Assign the section to the part
Assembly, Instance

## Slide 18: HEAT CONDUCTION
Steps
  General, Heat transfer
Loads
  Surface heat flux
BCs
  Temperature
Temperature: 5 °C (41 °F)
Heat flux
250 W/m2

## Slide 19: HEAT CONDUCTION
Mesh
  Assign Element Type, Heat Transfer
  Global seed, 1 m
Analysis, Create Job, Data Check, Submit
Results
  HFL: Heat flux
  NT: Nodal temperature
  RFL: Residual flux