## Slide 1: Chapter 4 Physics-based Prognostics

## Slide 2: 1. Introduction to Physics-based Prognostics

## Slide 3: Parameter Estimation in Prognostics
Physics-based prognostics: there exists a physical model that describes the evolution of damage or degradation (degradation model)
Key issues: how to improve the accuracy of degradation model and how to incorporate uncertainty in the future
Sources of uncertainty
  Uncertainty in model parameters
  Uncertainty in loading conditions
  Error in the model form
Decision-making process of prognostics should include these sources of uncertainty and should be based on conservative estimate of damage degradation

## Slide 4: Illustration of Physics-based Prognostics
Degradation model
  Assume loading conditions and time are given
  This chapter focuses on identifying model parameters and predicting the future behavior of degradation

## Slide 5: Uncertainty in Model Parameters
Generic materials have a large uncertainty
  This information is included in the material handbook
  Actual material parameters that are used in a system might be different from the model parameters that are obtained from laboratory test
However, a particular batch of a material may have a small uncertainty
Uncertainty in model parameters can significantly affect the performance of prognostics
  Ex) Paris model parameter (16% variability) may lead to 500% difference in the lifecycle
  The conservative estimate may request maintenance only after 20% of actual life has been consumed
it is important to reduce the uncertainty in model parameters to predict more accurate remaining useful life

## Slide 6: Effect of Model Parameter Uncertainty
N=0:100:4000;sig=70;a0=0.001; m=3.6:0.1:4.2; C=5E-10; figure; hold on;
for i=1:7
a(i,:)=(N.*C*(1-m(i)/2)*(sig*sqrt(pi))^m(i)+a0^(1-m(i)/2)).^(2/(2-m(i)));
plot(N,a(i,:));
end
N
m=3.6
m=4.2

## Slide 7: Epistemic Uncertainty in Model Parameters
uncertainty in model parameters is mostly from epistemic uncertainty
The fundamental concept of physics-based prognostics is to use measurement data to reduce the uncertainty in model parameters
  measurement data can be used to reduce the uncertainty in degradation model parameters using the Bayesian framework
  most physics-based prognostics methods have their foundation on Bayesian inference
Once model parameters are identified, the future behavior of degradation can be predicted by propagating the model to the future
  substitute the identified parameters to the degradation model with future time and loadings
  the RUL is predicted by propagating the degradation state until it reaches a threshold

## Slide 8: Physics-based Prognostics Methods
Physics-based prognostics methods are based on parameter estimation algorithms
Nonlinear least squares (NLS): nonlinear version of least squares method
Bayesian method (BM): Overall Bayesian inference
Kalman filter (KF): exact posterior distribution in the case of a linear system with Gaussian noise
Extended/unscented Kalman filter: for nonlinear systems
Particle filter (PF): represent the posterior distribution using particles

## Slide 9: Demonstration Problem: Battery Degradation
the capacity of a secondary cell degrades over cycles in use
  Failure threshold is defined when the capacity fades by 30%
Empirical degradation model
  Performance : capacity (capacity at nominally rated current of 1A)
  Model parameters: and , time or cycles:
Relative degradation model
  is the initial capacity. If the measurement is relative to the initial value,

## Slide 10: Degradation Data
Measured capacity at every 5 charging-discharging cycles
True parameter
Added Gaussian noise
True parameter is only used for data generation
EOL=118 cycles
time step, | initial, 1 | 2 | 3 | 4 | 5 | 6 | 7 | 8 | 9 | 10
time (cycles) | 0 | 5 | 10 | 15 | 20 | 25 | 30 | 35 | 40 | 45
data, (C/1 (Ahr)) | 1.00 | 0.99 | 0.99 | 0.94 | 0.95 | 0.94 | 0.91 | 0.91 | 0.87 | 0.86
 | initial, 1 | 2 | 3 | 4 | 5 | 6 | 7 | 8 | 9 | 10
time (cycles) | 0 | 5 | 10 | 15 | 20 | 25 | 30 | 35 | 40 | 45
 | 1.00 | 0.99 | 0.99 | 0.94 | 0.95 | 0.94 | 0.91 | 0.91 | 0.87 | 0.86

## Slide 11: 2. Nonlinear Least Squares (NLS)

## Slide 12: Nonlinear Least Squares Method
We used least squares method in Chapter 2
  Regression: when unknown model parameters are linear in the model
Nonlinear least squares (NLS)
  When the model parameters are nonlinear relationship in the model
How do you know a model is nonlinear?
  Derivatives depends on parameters
Ex) Battery degradation
NLS finds the best parameters using the weighted sum of square errors
Weights at measurement point

## Slide 13: Nonlinear Least Squares Method cont.
: Diagonal matrix
  When all weights are the same, becomes constant and can be ignored
  We will assume that is constant
Linear least squares:
  is a quadratic form and global minimum can be found using zero gradient
  Zero gradient yields a linear system of equation:
Nonlinear least squares:
  cannot be expressed as a linear system of equations
  Iterative process based on optimization methods is required
  Levenberg-Marquardt (LM) method is a popular method, which combines the gradient descent method and the Gauss-Newton method
  Look at Matlab function lsqnonlin

## Slide 14: Uncertainty in NLS
Parameter estimation depends on measurement data
  Uncertainty in data (noise) can cause uncertainty in model parameters
Variance of estimated model parameters
  : Jacobian matrix (similar to design matrix ), can be calculated numerically (finite difference)
  Assume the weights are the same
  Then,
Samples of model parameters can be drawn from multivariate t-random numbers

## Slide 15: NLS: Matlab code for Nonlinear Least Squares
function [thetaHat,rul]=NLS(theta0)
clear global; global DegraUnit TimeUnit ...
time y thres ParamName thetaTrue signiLevel ns ny nt np
%=== PROBLEM DEFINITION 1 (Required Variables) ==============
WorkName=' '; % work results are saved by WorkName
DegraUnit=' '; % degradation unit
TimeUnit=' '; % time unit (Cycles, Weeks, etc.)
time=[ ]'; % time at both measurement and prediction
y=[ ]'; %[nyx1]: measured data
thres= ; % threshold (critical value)
ParamName=[ ]; %[npx1]: parameters' name to be estimated
thetaTrue=[ ]; %[npx1]: true values of parameters
signiLevel= ; % significance level for C.I. and P.I.
ns= ; % number of particles/samples

## Slide 16: NLS Matlab Code cont.
%============================================================
% % % PROGNOSIS using NLS
ny=length(y); nt=ny;
np=size(ParamName,1); %% Deterministic Estimation
Optio=optimset('algorithm',{'levenberg-marquardt',0.01});
[thetaH,~,resid,~,~,~,J]=lsqnonlin(@FUNC,theta0,[],[],Optio);
sse=resid'*resid; %% Distribution of Theta
dof=ny-np+1;
sigmaH=sqrt(sse/dof); % Estimated std of data
W=eye(ny)*1/sigmaH^2; thetaCov=inv(J'*W*J);
sigTheta=sqrt(diag(thetaCov)); % Estimated std of Theta
mvt=mvtrnd(thetaCov,dof,ns)'; % Generate t-dist
thetaHat=repmat(thetaH,1,ns)+mvt.*repmat(sigTheta,1,ns);
thetaHat(np,:)=sigmaH*ones(1,ns); %% Final Sampling Results
for k=1:length(time(ny:end)); %% Degradation Prediction
zHat(k,:)=MODEL(thetaHat,time(ny-1+k));
degraPredi(k,:)=zHat(k,:)+trnd(dof,1,ns)*sigmaH;
end;

## Slide 17: NLS Matlab Code cont.
% % % POST-PROCESSING
degraTrue=[]; %% True Degradation
if ~isempty(thetaTrue); degraTrue=MODEL(thetaTrue,time); end
rul=POST(thetaHat,degraPredi,degraTrue); %% RUL & Result Disp
Name=[WorkName ' at ' num2str(time(ny)) '.mat']; save(Name);
end
function objec=FUNC(theta)
global time y ny
z=MODEL(theta,time(1:ny));
objec=(y-z);
end
function z=MODEL(theta,t)
global ParamName np
for j=1:np-1; eval([ParamName(j,:) '=theta(j,:);']); end
%===== PROBLEM DEFINITION 2 (model equation) ===============
%===========================================================
end

## Slide 18: NLS Code Explanation
Matlab code NLS is a template
  Users can define their own degradation model with unknown model parameters
Problem definition for user-specific applications
  Variable definition
  Model definition
Prognostics using NLS
Post-processing for displaying results

## Slide 19: Problem Definitions (lines 5-14, 48)
WorkName: model name
DegraUnit & TimeUnit: the units that are used in measurement data
time: first times are for measurement times, remaining times are for prediction
y: measurement data at first times
thres: the value of failure threshold for degradation
ParamName: name of model parameters + measurement noise ‘s’
  The actual variable name ‘b’ and ‘s’ will be used in the model definition in line 48 (eval function in Matlab)
thetaTrue: true values of parameters (optional)
signiLevel: significance level for the confidence interval
  5 (90%), 2.5 (95%), or 0.5 (99%)
ns: number of samples

## Slide 20: Problem Definition for Battery Degradation
Lines 5-14
Line 48
WorkName='Battery_NLS';
DegraUnit='C/1 Capacity';
TimeUnit='Cycles';
time=[0:5:200]';
y=[1.00 0.99 0.99 0.94 0.95 0.94 0.91 0.91 0.87 0.86]';
thres=0.7;
ParamName=['b'; 's'];
thetaTrue=[0.003; 0.02];
signiLevel=5;
ns=5e3;
z=exp(-b.*t);

## Slide 21: Prognostics Using NLS (lines 17-32)
Use LM algorithm with more dominant use of Gauss-Newton update
Minimize FUNC starting from theta0 using lsqnonlin
Optio=optimset('algorithm',{'levenberg-marquardt',0.01});
[thetaH,~,resid,~,~,~,J]=lsqnonlin(@FUNC,theta0,[],[],Optio);
function objec=FUNC(theta)
global time y ny
z=MODEL(theta,time(1:ny));
objec=(y-z);
end
Calculate residual vector
function z=MODEL(theta,t)
global ParamName np
for j=1:np-1; eval([ParamName(j,:) '=theta(j,:);']); end
%===== PROBLEM DEFINITION 2 (model equation) ===============
%===========================================================
end

## Slide 22: Prognostics Using NLS
STD of data, (np includes s, but s is not model parameters)
Covariance of parameters,
Generate samples of parameters using t-distribution
Propagate parameter samples to degradation samples
W=eye(ny)*1/sigmaH^2; thetaCov=inv(J'*W*J);
sigTheta=sqrt(diag(thetaCov)); % Estimated std of Theta
sse=resid'*resid; %% Distribution of Theta
dof=ny-np+1;
sigmaH=sqrt(sse/dof); % Estimated std of data
mvt=mvtrnd(thetaCov,dof,ns)'; % Generate t-dist
thetaHat=repmat(thetaH,1,ns)+mvt.*repmat(sigTheta,1,ns);
thetaHat(np,:)=sigmaH*ones(1,ns); %% Final Sampling Results
for k=1:length(time(ny:end)); %% Degradation Prediction
zHat(k,:)=MODEL(thetaHat,time(ny-1+k));
degraPredi(k,:)=zHat(k,:)+trnd(dof,1,ns)*sigmaH;
end;

## Slide 23: Post-processing (lines 34-37)
Plots of model parameters and RUL using Matlab code POST
Save database to the disk
How to use NLS
  LM algorithm in lsqnonlin finds a local optimum (depending on initial)
%%% POST-PROCESSING
degraTrue=[]; %% True Degradation
if ~isempty(thetaTrue); degraTrue=MODEL(thetaTrue,time); end
rul=POST(thetaHat,degraPredi,degraTrue); %% RUL & Result Disp
Name=[WorkName ' at ' num2str(time(ny)) '.mat']; save(Name);
[thetaHat,rul]=NLS(0.01);

## Slide 24: Matlab Code POST
Histogram of all parameters
Plotting degradation
  Percentile value [50% (median), ]
function rul=POST(thetaHat,degraPredi,degraTrue)
for j=1:np; subplot(1,np,j);
[frq,val]=hist(thetaHat(j,:),30);
bar(val,frq/ns/(val(2)-val(1)));
xlabel(ParamName(j,:));
end;
degraPI=prctile(degraPredi',perceValue)';
f1(1,:)=plot(time(1:ny),y(:,1),'.k'); hold on;
f1(2,:)=plot(time(ny:end),degraPI(:,1),'--r');
f1(3:4,:)=plot(time(ny:end),degraPI(:,2:3),':r');
f2=plot([0 time(end)],[thres thres],'g');

## Slide 25: Matlab Code POST
RUL calculation
  coeff =1 (increasing) or -1 (decreasing) degradation
  loca: location when degradation reaches the threshold
  i0: number of samples that did not reach the threshold (never failed)
i0=0; %% RUL Prediction
if y(nt(1))-y(1)<0; coeff=-1; else coeff=1;end;
for i=1:ns;
loca=find(degraPredi(:,i)*coeff>=thres*coeff,1);
if isempty(loca); i0=i0+1;
disp([num2str(i) 'th not reaching thres']);
elseif loca==1; rul(i-i0)=0;
else rul(i-i0)=...
interp1([degraPredi(loca,i) degraPredi(loca-1,i)], ...
[time(ny-1+loca) time(ny-2+loca)],thres)-time(ny);
end
end;
rulPrct=prctile(rul,perceValue);

## Slide 26: Matlab Code POST cont.
Plotting the histogram of RUL
figure(3); %% RUL Results Display
[frq,val]=hist(rul,30);
bar(val,frq/ns/(val(2)-val(1))); hold on;
xlabel(['RUL' ' (' TimeUnit ')']);
titleName=['at ' num2str(time(ny)) ' ' TimeUnit];
title(titleName)
fprintf(['\n Percentiles of RUL at %g ' TimeUnit], time(ny))
fprintf('\n %gth: %g, 50th (median): %g, %gth: %g \n', ...
perceValue(2),rulPrct(2),rulPrct(1),perceValue(3),rulPrct(3))

## Slide 27: 3. Bayesian Method (BM)

## Slide 28: Bayesian Method (BM)
In terms of Chapter 3, BM corresponds to overall Bayesian method
  All training data (up to the current time) are used together to build the likelihood function
  The posterior distribution is obtained by multiplying the likelihood function with the prior distribution
For conjugate distribution, it is possible to generate samples from standard distributions
For single parameter estimation, the inverse CDF method can be used to generate samples
For general cases, Markov-chain Monte-Carly (MCMC) method will be used to generate samples
Using generated samples of model parameters, samples of RUL can be generated

## Slide 29: Ex) MCMC Method: One Parameter
Draw 5000 samples from
Uniformly distributed proposal distribution
  STD of uniform distribution
para0=5; weigh=5;
for i=1:5000
u=rand;
para1=unifrnd(para0-weigh, para0+weigh);
pdf1=normpdf(para1,5,2.9);
pdf0=normpdf(para0,5,2.9);
Q=min(1, pdf1/pdf0);
u=rand;
if u<Q; sampl(:,i)=para1; else sampl(:,i)=para0; end
para0=sampl(:,i);
end
plot(sampl); xlabel('Iteration (samples)'); ylabel('A')
figure; [frq,val]=hist(sampl,30);
bar(val,frq/5000/(val(2)-val(1))); hold on;
a=-10:0.1:20; plot(a,normpdf(a,5,2.9),'k')
xlabel('A'); legend('Sampling','Exact')

## Slide 30: Ex) MCMC Method: One Parameter cont.
The quality of proposal distribution can be assessed using the trace of samples
Ex) para0=0.5, weigh=0.5
Trace does not show fluctuation with respect to the mean
The histogram does not agree with the analytical PDF

## Slide 31: Ex) Multidimensional Correlated Sampling
Posterior PDF of
Model and data
para0=[0; 1]; weigh=[0.05; 0.05]; s=2.9;
t = [0 1 2 3 4];
y=[6.99 2.28 1.91 11.94 14.60];
f0=5+para0(1)*t.^2+para0(2)*t.^3;
pdf0=(s*sqrt(2*pi))^-5*exp(-(f0-y)*(f0-y)'/(2*s^2));
para1=unifrnd(para0-weigh, para0+weigh);
f1=5+para1(1)*t.^2+para1(2)*t.^3;
pdf1=(s*sqrt(2*pi))^-5*exp(-(f1-y)*(f1-y)'/(2*s^2));

## Slide 32: Ex) Multidimensional Correlated Sampling cont.
Due to a wrong initial point, first 200 samples are disregarded (burn-in)
Sample trace show that the weight is too small
para0=[0; 0], weigh=[0.3; 0.3],

## Slide 33: Bayesian Method Matlab Code (BM)
Problem definition
function [thetaHat,rul]=BM(para0,weigh)
clear global; global DegraUnit initDisPar TimeUnit ...
time y thres ParamName thetaTrue signiLevel ns ny nt np
%=== PROBLEM DEFINITION 1 (Required Variables) ==============
WorkName=' '; % work results are saved by WorkName
DegraUnit=' '; % degradation unit
TimeUnit=' '; % time unit (Cycles, Weeks, etc.)
time=[ ]'; % time at both measurement and prediction
y=[ ]'; %[nyx1]: measured data
thres= ; % threshold (critical value)
ParamName=[ ]; %[npx1]: parameters' name to be estimated
initDisPar=[ ]; %[npx2]: prob. parameters of init./prior dist
thetaTrue=[ ]; %[npx1]: true values of parameters
signiLevel= ; % significance level for C.I. and P.I.
ns= ; % number of particles/samples
burnIn= ; % ratio for burn-in

## Slide 34: BM Matlab Code cont.
%============================================================
% % % PROGNOSIS using BM with MCMC
ny=length(y); nt=ny;
np=size(ParamName,1);
sampl(:,1)=para0; %% Initial Samples
[~,jPdf0]=MODEL(para0,time(1:ny)); %% Initial (joint) PDF
for i=2:ns/(1-burnIn); %% MCMC Process
% proposal distribution (uniform)
para1(:,1)=unifrnd(para0-weigh,para0+weigh);
% (joint) PDF at new samples
[~,jPdf1]=MODEL(para1,time(1:ny));
% acceptance/rejection criterion
if rand<min(1,jPdf1/jPdf0)
para0=para1; jPdf0=jPdf1;
end;
sampl(:,i)=para0;
end;
nBurn=ns/(1-burnIn)-ns; %% Sampling Trace
figure(4);for j=1:np;subplot(np,1,j);plot(sampl(j,:));hold on
plot([nBurn nBurn],[min(sampl(j,:)) max(sampl(j,:))],'r');end
thetaHat=sampl(:,nBurn+1:end); %% Final Sampling Results
for k=1:length(time(ny:end)); %% Degradation Prediction
[zHat(k,:),~]=MODEL(thetaHat,time(ny-1+k));
degraPredi(k,:)=normrnd(zHat(k,:),thetaHat(end,:));
end;

## Slide 35: BM Matlab Code cont.
% % % POST-PROCESSING
degraTrue=[]; %% True Degradation
if ~isempty(thetaTrue); degraTrue=MODEL(thetaTrue,time); end
rul=POST(thetaHat,degraPredi,degraTrue); %% RUL & Result Disp
Name=[WorkName ' at ' num2str(time(ny)) '.mat']; save(Name);
end
function [z,poste]=MODEL(param,t)
global y ParamName initDisPar ny np
for j=1:np; eval([ParamName(j,:) '=param(j,:);']); end
%===== PROBLEM DEFINITION 2 (model equation) ===============
%===========================================================
if length(y)~=length(t); poste=[];
else
prior= ... %% Prior
prod(unifpdf(param,initDisPar(:,1),initDisPar(:,2)));
likel=(1./(sqrt(2.*pi).*s)).^ny.* ... %% Likelihood
exp(-0.5./s.^2.*(y-z)'*(y-z));
poste=likel.*prior; %% Posterior
end
end

## Slide 36: BM Implementation for Battery Prognostics
Normal likelihood
Prior distribution:
Problem definition (lines 5-16, 52)
  initDisPar: initial distribution parameters
  burnIn=0.2: initial 20% of samples will be discarded
All other problem definitions are the same as NLS
initDisPar=[0 0.02; 1e-5 0.1];
burnIn=0.2;

## Slide 37: BM Implementation for Battery Prognostics cont.
Calling BM:
  Initial parameters param0 = [0.01 0.05]’
  Weight of proposal distribution = [0.0005 0.01]’
  thetaHat: samples of estimated model parameters
  rul: samples of RUL
Two usages of MODEL
  MODEL returns degradation prediction z, and posterior PDF
  During model parameter estimation, posterior PDF poste is calculated using ny data
  During prognostics, MODEL is used to generate future degradation samples with future time
[thetaHat,rul]=BM([0.01 0.05]',[0.0005 0.01]');
function [z,poste]=MODEL(param,t)

## Slide 38: Overall BM Posterior PDF
Do not calculate PDF in the prediction stage
Prior : Independent distribution
Likelihood
Posterior
if length(y)~=length(t); poste=[];
else
prior= ... %% Prior
prod(unifpdf(param,initDisPar(:,1),initDisPar(:,2)));
likel=(1./(sqrt(2.*pi).*s)).^ny.* ... %% Likelihood
exp(-0.5./s.^2.*(y-z)'*(y-z));
poste=likel.*prior; %% Posterior
end

## Slide 39: Prognostics using BM
Parameter estimation = generating samples from posterior distribution
  Using MCMC sampling
sampl(:,1)=para0; %% Initial Samples
[~,jPdf0]=MODEL(para0,time(1:ny)); %% Initial (joint) PDF
for i=2:ns/(1-burnIn); %% MCMC Process
% proposal distribution (uniform)
para1(:,1)=unifrnd(para0-weigh,para0+weigh);
% (joint) PDF at new samples
[~,jPdf1]=MODEL(para1,time(1:ny));
% acceptance/rejection criterion
if rand<min(1,jPdf1/jPdf0)
para0=para1; jPdf0=jPdf1;
end;
sampl(:,i)=para0;
end;

## Slide 40: Sampling Trace
Remove the first nBurn samples
  Remaining number of samples = ns
nBurn=ns/(1-burnIn)-ns; %% Sampling Trace
figure(4);for j=1:np;subplot(np,1,j);plot(sampl(j,:));hold on
plot([nBurn nBurn],[min(sampl(j,:)) max(sampl(j,:))],'r');end

## Slide 41: Post-processing (lines 43-46)
Basically the same with NLS
  Use POST with samples of parameters and degradations
Percentiles of RUL at 45 Cycles
5th: 54.3859,
50th (median): 68.3619,
95th: 82.8892

## Slide 42: 4. Particle Filter (PF)

## Slide 43: Particle Filter
the most popular method in the physics-based prognostics
  fundamental concept is the same as the recursive Bayesian update
the prior and posterior PDF of parameters are represented by particles (samples)
the posterior at the previous step is used as the prior at the current step, and the parameters are updated by multiplying it with the likelihood from the new measurement
also known as the sequential Monte Carlo method

## Slide 44: Review of Importance Sampling (IS)
IS assigns a weight to each sample (or particle) in proportion to an arbitrarily chosen importance distribution
  the quality of estimation depends on the selected importance distribution
The weight of particle
  : arbitrary importance distribution
  : posterior distribution value at th particle
possible to use the prior distribution as an importance distribution
  because it is already available and close to the posterior distribution
Condensation (CONditional DENSity propagATION) algorithm
  Weight = likelihood:

## Slide 45: Sequential IS
PF can be considered as a sequential importance sampling method
  weights are continuously updated whenever a new observation is available
Degeneracy phenomenon
  happens when weights are updated with the same initial samples
  decreases the accuracy in the posterior distribution with a large variance
sequential importance resampling (SIR)
  Small weight particles are removed
  High weight particles are duplicated

## Slide 46: General Process of PF
Conventionally, PF has been used to estimate the system state using measured data
  model parameters are obtained from laboratory tests
PF can also be used to estimate both the system state and model parameters
General process of PF
  We do not consider processing noise as we use physical model
  Measurement function
: degradation model (state transition)
: measurement function
: measurement noise
: system state (degradation level)
: model parameters

## Slide 47: Application to Battery Degradation
Rewrite the battery degradation model in terms of PF process
Ratio
PF form:

## Slide 48: SIR Process
Initial step
  Generate samples (particles) of degradation and model parameters based on the prior distribution
  Same initial weight for all particles:

## Slide 49: SIR Process: Prediction
Use step as a prior distribution
  available in the form of samples
degradation state at is propagated to in the form of samples
  No transition for model parameters:
  Draw samples of based on
Ex) Battery degradation

## Slide 50: SIR Process: Update
Model parameters and degradation state are updated (corrected) based on the likelihood function from measured data at the current step
  Likelihood: the probability of obtaining conditional on each sample
Weight calculation as a normalized likelihood

## Slide 51: SIR Process: Update cont.
Posterior distribution = sample weight
  After update, some samples have a high weight, some samples have a low weight
Cause degeneracy problem
  decreases the accuracy in the posterior distribution
  causes the lack of reducing the range of distribution by keeping samples with low weights

## Slide 52: SIR Process: Resampling
Resampling: all samples have the same weight so that samples, not weight, can represent the posterior distribution of model parameters and degradation state
CDF method
  (a) Construct CDF of from the likelihood function
  (b) Find samples of that make the CDF of be the same as the randomly chosen
By repeating the CDF method times, samples of with a constant weights are obtained (approximate posterior distribution)
  After resampling, every sample has the same weight

## Slide 53: SIR Process: Resampling cont.
in BM, posterior = likelihood prior
In PF, prior = samples, likelihood = weights
resampling process is equivalent to generating a new set of samples that follow the posterior distribution
  Particles with a large weight are likely duplicated, and particles with a small weight are likely removed
Recursive Bayesian updating: the posterior distribution at the current step is used as a prior distribution at the next -th step

## Slide 54: Ex) PF of Battery Degradation with 10 Samples
initial distributions:
At
  Generate 10 samples from the initial distributions
time step, | initial, 1 | 2 | 3
time (cycles) | 0 | 5 | 10
data, (C/1 (Ahr)) | 1.00 | 0.99 | 0.99
 | initial, 1 | 2 | 3
time (cycles) | 0 | 5 | 10
 | 1.00 | 0.99 | 0.99
k=1; ns=10;
b(k,:)=unifrnd(0,0.005,ns,1);
z(k,:)=unifrnd(0.9,1.1,ns,1);
figure; subplot(1,2,1);
plot(b(k,:),zeros(1,ns),'ok'); xlabel('b (parameter)')
subplot(1,2,2);
plot(z(k,:),zeros(1,ns),'ok'); xlabel('z (degradation)')

## Slide 55: Ex) PF of Battery Degradation with 10 Samples
At : Prediction
  Same parameter, propagating model prediction
k=2; dt=5;
b(k,:)=b(k-1,:);
z(k,:)=exp(-b(k,:).*dt).*z(k-1,:);
% for figure plot, use the same code given in k=1

## Slide 56: Ex) PF of Battery Degradation with 10 Samples
At : Update
  Calculate likelihood
  Weights are normalized (sum = 1)
  Scaled weights = weights : weights are the number of samples to be duplicated
likel=normpdf(y(k,:),z(k,:),0.02);
weigh=round(likel/sum(likel)*ns);
figure; subplot(1,2,1); stem(b(k,:),weigh,'r');
xlabel('b (parameter)'); ylabel('Weight')
subplot(1,2,2); stem(z(k,:),weigh,'r');
xlabel('z (degradation)'); ylabel('Weight')

## Slide 57: Ex) PF of Battery Degradation with 10 Samples
At : Resampling
  Inverse CDF can be used
  We will simply remove samples with zero weights, other samples are duplicated as many as the weight
sampl=[b(k,:); z(k,:)];
loca=find(weigh>0); ns0=1;
for i=1:length(loca);
ns1=sum(weigh(loca(1:i)));
b(k,ns0:ns1)=sampl(1,loca(i))*ones(1,weigh(loca(i)));
z(k,ns0:ns1)=sampl(2,loca(i))*ones(1,weigh(loca(i)));
ns0=ns1+1;
end
Several samples are overlapped: particle depletion

## Slide 58: Ex) PF of Battery Degradation with 10 Samples
At : Prediction, Update, and Resampling

## Slide 59: Ex) PF of Battery Degradation with 10 Samples
Future degradation prediction
  Model parameters are not updated anymore
  The degradation state is continuously propagated until reaching the threshold
Ex) In the case of
  At ,
  At ,
  At 0,
  Therefore, predicted RULcycles

## Slide 60: Particle Filter (PF) Matlab Code
function [thetaHat,rul]=PF
clear global; global DegraUnit initDisPar TimeUnit ...
time y thres ParamName thetaTrue signiLevel ns ny nt np
%=== PROBLEM DEFINITION 1 (Required Variables) ==============
WorkName=' '; % work results are saved by WorkName
DegraUnit=' '; % degradation unit
TimeUnit=' '; % time unit (Cycles, Weeks, etc.)
time=[ ]'; % time at both measurement and prediction
dt= ; % time interval for degradation propagation
y=[ ]'; %[nyx1]: measured data
thres= ; % threshold (critical value)
ParamName=[ ]; %[npx1]: parameters' name to be estimated
initDisPar=[ ]; %[npx2]: prob. parameters of init./prior dist
thetaTrue=[ ]; %[npx1]: true values of parameters
signiLevel= ; % significance level for C.I. and P.I.
ns= ; % number of particles/samples

## Slide 61: PF Matlab Code cont.
% % % PROGNOSIS using PF
ny=length(y); nt=ny;
np=size(ParamName,1);
for j=1:np; %% Initial Distribution
param(j,:,1)=unifrnd(initDisPar(j,1),initDisPar(j,2),1,ns);
end;
for k=2:length(time); %% Update Process or Prognosis
paramPredi=param(:,:,k-1); % step1. prediction (prior)
nk=(time(k)-time(k-1))/dt;
for k0=1:nk; paramPredi(np,:)=MODEL(paramPredi,dt); end
if k<=ny % (Update Process)
% step2. update (likelihood)
likel=normpdf(y(k),paramPredi(np,:),paramPredi(np-1,:));
cdf=cumsum(likel)./sum(likel); % step3. resampling
for i=1:ns;
u=rand;
loca=find(cdf>=u,1); param(:,i,k)=paramPredi(:,loca);
end;
else % (Prognosis)
param(:,:,k)=paramPredi;
end
end
thetaHat=param(1:np-1,:,ny); %% Final Sampling Results
paramRearr=permute(param,[3 2 1]); %% Degradation Prediction
zHat=paramRearr(:,:,np);
degraPredi=normrnd(zHat(ny:end,:),paramRearr(ny:end,:,np-1));

## Slide 62: PF Matlab Code cont.
% % % POST-PROCESSING
degraTrue=[]; %% True Degradation
if ~isempty(thetaTrue); k=1;
degraTrue0(1)=thetaTrue(np); degraTrue(1)=thetaTrue(np);
for k0=2:max(time)/dt+1;
degraTrue0(k0,1)= ...
MODEL([thetaTrue(1:np-1); degraTrue0(k0-1)],dt);
loca=find((k0-1)*dt==time,1);
if ~isempty(loca); k=k+1; degraTrue(k)=degraTrue0(k0);end
end
end
rul=POST(thetaHat,degraPredi,degraTrue); %% RUL & Result Disp
Name=[WorkName ' at ' num2str(time(ny)) '.mat']; save(Name);
end
function z1=MODEL(param,dt)
global ParamName np
for j=1:np; eval([ParamName(j,:) '=param(j,:);']); end
%===== PROBLEM DEFINITION 2 (model equation) ===============
%===========================================================
end

## Slide 63: Matlab Implementation for Battery Prognostics
No uncertainty in initial prediction
Problem definition (lines 5-16)
  For simplicity, we assume constant time interval: (can be varied)
  Smaller can improve integration accuracy (forward Euler method)
  In PF, the degradation state is the last parameter
Degradation model (line 64)
  Degradation model is given in the form of transition function
dt=5;
ParamName=['b'; 's'; 'z'];
initDisPar=[0 0.02; 1e-5 0.1; 1 1];
thetaTrue=[0.003; 0.02; 1];
z1=exp(-b.*dt).*z;

## Slide 64: Matlab Implementation for Battery Prognostics
Calling PF
  Similar to BM, PF returns samples of model parameters and RULs
Model definition
  Same as NLS
Initial stage
  Generate samples of parameters and degradation
  Note: no uncertainty for the initial degradation
[thetaHat,rul]=PF;
for j=1:np; %% Initial Distribution
param(j,:,1)=unifrnd(initDisPar(j,1),initDisPar(j,2),1,ns);
end;

## Slide 65: Matlab Implementation for Battery Prognostics
Step 1: Prediction (prior)
  No change in model parameters (same values from the previous time)
  Propagate degradation using the model
  If , multiple steps are used to integration the degradation
Step 2: Update
  Based on every sample of degradation and measurement
% step1. prediction (prior)
paramPredi=param(:,:,k-1);
nk=(time(k)-time(k-1))/dt;
for k0=1:nk; paramPredi(np,:)=MODEL(paramPredi,dt); end
if k<=ny % (Update Process)
% step2. update (likelihood)
likel=normpdf(y(k),paramPredi(np,:),paramPredi(np-1,:));

## Slide 66: Matlab Implementation for Battery Prognostics
Step 3: Resampling
  cdf: cumulative CDF of likelihood samples
  Using a random sample , find the new sample location that corresponds to approximately
  a sample with a large likelihood (weight) has more probability to be duplicated, while a sample with a small likelihood may not be reproduced
% step3. resampling
cdf=cumsum(likel)./sum(likel);
for i=1:ns;
u=rand;
loca=find(cdf>=u,1);
param(:,i,k)=paramPredi(:,loca);
end;
else % (Prognosis)
param(:,:,k)=paramPredi;
end

## Slide 67: Matlab Implementation for Battery Prognostics
Post-processing
  Basically identical to NLS and BM
  Since degradation is a part of param, rearrange arrayes
thetaHat=param(1:np-1,:,ny); %% Final Sampling Results
paramRearr=permute(param,[3 2 1]); %% Degradation Prediction
zHat=paramRearr(:,:,np);
degraPredi=normrnd(zHat(ny:end,:),paramRearr(ny:end,:,np-1));

## Slide 68: 5. Practical Application of Physics-based Prognostics

## Slide 69: Crack Growth Model Definition
Paris crack growth model:
  NLS and BM require the degradation model as a function of time/cycle
  PF requires the model as a transition function (incremental form)
Assume , cycles
time step, | initial, 1 | 2 | 3 | 4 | 5 | 6 | 7 | 8
time (cycles) | 0 | 100 | 200 | 300 | 400 | 500 | 600 | 700
crack size (m) | 0.0100 | 0.0109 | 0.0101 | 0.0107 | 0.0110 | 0.0123 | 0.0099 | 0.0113
time step, | 9 | 10 | 11 | 12 | 13 | 14 | 15 | 16
time (cycles) | 800 | 900 | 1000 | 1100 | 1200 | 1300 | 1400 | 1500
crack size (m) | 0.0132 | 0.0138 | 0.0148 | 0.0156 | 0.0155 | 0.0141 | 0.0169 | 0.0168
 | initial, 1 | 2 | 3 | 4 | 5 | 6 | 7 | 8
time (cycles) | 0 | 100 | 200 | 300 | 400 | 500 | 600 | 700
crack size (m) | 0.0100 | 0.0109 | 0.0101 | 0.0107 | 0.0110 | 0.0123 | 0.0099 | 0.0113
 | 9 | 10 | 11 | 12 | 13 | 14 | 15 | 16
time (cycles) | 800 | 900 | 1000 | 1100 | 1200 | 1300 | 1400 | 1500
crack size (m) | 0.0132 | 0.0138 | 0.0148 | 0.0156 | 0.0155 | 0.0141 | 0.0169 | 0.0168

## Slide 70: Crack Growth Model Definition
Measurement data generation process
  True model parameters are used only to generating measurement data
  Use to generate true crack growth
  Add random Gaussian noise to the crack size
The generated data are used to identify two model parameters
  Assume and are known
The threshold (critical crack size),

## Slide 71: Likelihood and Prior Distribution
In order to study the effect of different distribution type, we assume likelihood is from a lognormal distribution
  This means that random measurement noise is lognormally distributed
  Standard deviation:
  Mean:
Prior distribution
: model prediction (crack size)

## Slide 72: Modifying NLS Matlab Code
Problem definition part
  is not a parameter, but it is calculated based on the identified parameters
WorkName='Crack_NLS';
DegraUnit='Crack size (m)';
TimeUnit='Cycles';
time=[0:100:3500]';
y=[0.0100 0.0109 0.0101 0.0107 0.0110 0.0123 0.0099 0.0113...
0.0132 0.0138 0.0148 0.0156 0.0155 0.0141 0.0169 0.0168]';
thres=0.05;
ParamName=['m'; 'C'; 's'];
thetaTrue=[3.8; log(1.5e-10); 0.001];
signiLevel=5;
ns=5e3;

## Slide 73: Modifying NLS Matlab Code cont.
Model definition
  is used instead of
  When the crack size grows too large, becomes a complex number
  We replace complex crack size with an arbitrary large value
a0=0.01; dsig=75;
z=(t.*exp(C).*(1-m./2).*(dsig*sqrt(pi)).^m ...
+a0.^(1-m./2)).^(2./(2-m));
loca=imag(z)~=0; z(loca)=1;

## Slide 74: Modifying NLS Matlab Code cont.
Likelihood
  Likelihood is unnecessary for NLS, but it is used to predict degradation
Calling NLS
mu=zHat(k,:);
C=chi2rnd(ny-1,1,ns);
s=sqrt((ny-1)*thetaHat(np,:).^2./C);
zeta=sqrt(log(1+(s./mu).^2)); eta=log(mu)-0.5*zeta.^2;
degraPredi(k,:)=lognrnd(eta,zeta);
[thetaHat,rul]=NLS([4; -23]);

## Slide 75: Modifying BM Matlab Code
Problem definition
  In addition to NLS problem definition, add the following information
  If noise is given, put STD of s = 0 (1E-5 for preventing numerical error)
Model definition
Calling BM
WorkName='Crack_BM';
initDisPar=[4.0 0.2; -23 1.1; 0.001 1e-5];
burnIn=0.2;
prior=prod(normpdf(param,initDisPar(:,1),initDisPar(:,2)));
likel=1;
for k=1:ny;
zeta=sqrt(log(1+(s./z(k)).^2)); eta=log(z(k))-0.5*zeta.^2;
likel=lognpdf(y(k),eta,zeta).*likel;
end
[thetaHat]=BM([4 -23 0.001]',[0.1 0.2 0]');

## Slide 76: Modifying PF Matlab Code
Problem definition
  PF includes state ‘a’ as the last parameter
Model definition
WorkName='Crack_PF';
dt=20;
ParamName=['m'; 'C'; 's'; 'a'];
initDisPar=[4.0 0.2; -23 1.1; 0.001 0; 0.01 0];
thetaTrue=[3.8;log(1.5e-10); 0.001; 0.01];
dsig=75;
z1=exp(C).*(dsig.*sqrt(pi*a)).^m.*dt+a;

## Slide 77: Modifying PF Matlab Code cont.
Predicting degradation (logarithmic distribution)
Initial distribution
Likelihood (weight)
Calling PF
mu=zHat(ny:end,:); s=paramRearr(ny:end,:,np-1);
zeta=sqrt(log(1+(s./mu).^2)); eta=log(mu)-0.5*zeta.^2;
degraPredi=lognrnd(eta,zeta);
param(j,:,1)=normrnd(initDisPar(j,1),initDisPar(j,2),1,ns);
mu=paramPredi(np,:); s=paramPredi(np-1,:);
zeta=sqrt(log(1+(s./mu).^2)); eta=log(mu)-0.5*zeta.^2;
likel=lognpdf(y(k),eta,zeta);
[thetaHat,rul]=PF;

## Slide 78: Comparison of Results
Correlation plot
  A large uncertainty in the results from NLS compared to the others (because no prior information is employed)
  Large uncertainty in parameters leads to large uncertainty in degradation prediction
  PF is still not showing smooth distribution of particles
plot(thetaHat(1,:),thetaHat(2,:),'.').

## Slide 79: Comparison of Results
Degradation prediction plot
  Median prediction follows the true degradation for all three methods
  Much larger uncertainty in NLS
  PF has a model error in integrating the incremental equation with .

## Slide 80: 6. Issues in Physics-based Prognostics

## Slide 81: Advantages of Physics-base Prognostics
Can make a long-term prediction
  Possible to predict the RUL by propagating the degradation model to future time
Require relatively a small number of data
  Theoretically, require the # of data same as that of model parameters
  In reality, a greater number of data are required due to noise in data and due to insensitivity of degradation behavior to parameters
  But the required number of data is much less than that of data-driven methods.

## Slide 82: Model Adequacy
Question: Is the physical model good enough to predict the future behavior of degradation?
  In particular, is the model good in the extrapolation region?
An adequate model in the interpolation region can be inadequate in the extrapolation region
  Important to validate the physical model for the purpose of prognostics
Under-estimation of degradation
Training data
Validation data
Fitted model

## Slide 83: Parameter Estimation
Estimation accuracy is related to characteristics of different algorithms, such as NLS, BM and PF
Correlations between model parameters and also between model parameters and loading conditions hinders identifying accurate parameters
A good prognostics algorithm can identify accurate model parameters with a smaller number of data
Correlation: even if the accurate identification of parameters might be difficult, it is possible that accurate prediction in degradation and RUL are still possible

## Slide 84: Quality of Degradation Data
Data could include a high level of noise and bias due to the sensor equipment and measurement environment
  Noise is a random fluctuation in measured data or signal due to interference or unwanted electromagnetic fields in electronic devices
  Bias is static deviation of signals from correct ones, which can happen due to calibration error
Noise makes it difficult to identify signals related to degradation, while bias in-duces error in prediction