## Slide 1: Chapter 7 Applications of Prognostics

## Slide 2: 1. Introduction

## Slide 3: Challenges in Physics-based Approaches
Difficult to accurately identify model parameters due to the correlation between them and a large level of noise and bias in data
Even if accurate values of individual parameters may not be found, the prediction of RUL can still be accurate
Under model-form error, prognostics algorithms can identify equivalent parameters that can compensate for the model-form error
A good prior information can help to reduce uncertainty in the estimated parameters, but inaccurate prior can prevent from converging accurate values

## Slide 4: Challenges in Data-driven Approaches
Data-driven approaches are also affected by the level of noise, but obtaining a large number of training data is a challenge
it is possible to utilize the data obtained from accelerated life test during the development of the current system design
Since accelerated life tests are performed much severe operating conditions, it is necessary to convert them corresponding to the nominal operating conditions in order to be used as training data

## Slide 5: Indirect CM Data
In many cases, the damage data cannot be measured directly, but system responses that are affected by damage are measured instead
  vibration data are often measured to monitor any cracks on bearings and gears, from which the level of damage in bearings is to be predicted
difficult to extract degradation features from indirectly measured data
  important to separate signals from noise
  signal-to-noise ratio (SNR) becomes an important issue

## Slide 6: 2. In-situ Monitoring and Prediction of Joint Wear

## Slide 7: Prognostics of Wear Volume in a Revolute Joint
Most mechanical joints are under sliding motion, which causes wear
Wear is the gradual removal of material from contacting surfaces in relative motion, which eventually causes failure of the system
important to predict its effects and estimate the service life of the system before failure
Common approaches
  (a) estimating wear coefficient from tribometer tests
  (b) calculating contact pressure and sliding distance
  (c) using a wear model to calculate wear depth as well as wear volume
Challenges
  Wear coefficient is a function of contact pressure and surface condition
  Variability of wear coefficient is significant even for the same material
In-situ measurement of wear coefficient is preferable

## Slide 8: Prognostics of Wear Volume in a Revolute Joint
In-situ measurement
  Kinematic information: wear volume and sliding distance
  Kinetic information: contact force/pressure
  We will use an instrumented slider-crank mechanism
Since in-situ measurements inherently include uncertainty, the statistical distribution of wear coefficient are updated based on the Bayesian method
This application shows how difficult to measure the direct CM data

## Slide 9: Wear Model and Wear Coefficient
Archard wear model
  plastic deformation is a dominant mechanism of material removal
  assumes that the volume of material removed is linearly proportional to the product of the sliding distance and the normal load
  wear coefficient: slope between the wear volume and sliding distance
: worn volume
: slip distance
: dimensionless wear coefficient
: Brinell hardness
: applied contact force

## Slide 10: Wear Model and Wear Coefficient cont.
Dimensioned wear coefficient
  Objective: identify the wear coefficient for given normal load and slip distance
Variable normal forces
  Assumption: wear coefficient is independent of normal force
The wear coefficient is not an intrinsic material property
  depends on operating conditions, such as the normal force and slip speed
  experimentation does not often represent the real conditions of a machine
Unit of wear coefficient:
Wear volume in
Slip distance in

## Slide 11: In-Situ Measurement for a Slider-Crank
porous carbon air bearings for the revolute joint between the follower link and the slide stage, as well as the prismatic joint for the linear slide
Revolute joint: steel pin + polymer (PTFE) bushing
  No wear at steel pin, but considerable wear at bushing
  Debris groove to remove worn materials
Debris groove

## Slide 12: Measurement Instrument
added mass and springs affect the joint force and accelerate wear
Factors to affect wear process
  (1) wear coefficient
  (2) joint force
  (3) relative motion in the interface
Force at joint: load cell measurement
  Two full-bridge arrays of strain gages mounted to a necked-down portion of the pin monitor transverse loads while cancelling out bending stresses
Joint of interest

## Slide 13: Measurement Instrument cont.
Steel pin load cell
  Two full-bridge arrays of strain gages mounted to a necked-down portion of the pin monitor transverse loads while cancelling out bending stresses

## Slide 14: Measurement Instrument cont.
two orthogonally-mounted capacitance probes monitor the position of the pin relative to bushing

## Slide 15: Joint Force Measurement
measured joint force agrees well with the multibody dynamic simulation with the coupled evolution wear model
High frequency oscillation is observed when the slider changes its velocity direction
No significant variation of joint forces between different cycles
  the profile of joint forces is fixed throughout all cycles

## Slide 16: Capacitance Probe Displacement Measurement
measured displacements of the pin center using the capacitance probe
Wear volume can be calculated using and
Springs make the contact points located at only one side of the bushing

## Slide 17: Wear Coefficients
Calculate wear coefficients at different angle positions
  Showing convergence but the converged results do not match
  because the joint force is not constant with angle and the measured wear volume includes uncertainty
Goal: estimate the wear coefficient using the first five sets and then predict the wear volume in the sixth cycle
Cycles | Force (N) | Volume (mm3) | Slip distance (m) | (mm3/Nm)
1 | 64.41 | 1.59 | 0.06 | 4134.80
100 | 62.80 | 2.57 | 5.99 | 68.25
1000 | 63.17 | 8.10 | 59.85 | 21.44
5000 | 64.77 | 24.48 | 299.24 | 12.63
10000 | 62.65 | 46.21 | 598.47 | 12.32
20585 | 59.96 | 93.90 | 1232.00 | 12.71
Cycles | Force (N) | Volume (mm3) | Slip distance (m) | 
1 | 64.41 | 1.59 | 0.06 | 4134.80
100 | 62.80 | 2.57 | 5.99 | 68.25
1000 | 63.17 | 8.10 | 59.85 | 21.44
5000 | 64.77 | 24.48 | 299.24 | 12.63
10000 | 62.65 | 46.21 | 598.47 | 12.32
20585 | 59.96 | 93.90 | 1232.00 | 12.71
Cycles | Force (N) | Volume (mm3) | Slip distance (m) | (mm3/Nm)
1 | 103.87 | 7.29 | 0.06 | 11731.00
100 | 106.90 | 7.64 | 5.99 | 119.43
1000 | 114.04 | 9.55 | 59.85 | 13.99
5000 | 138.77 | 23.87 | 299.24 | 5.75
10000 | 143.50 | 44.41 | 598.47 | 5.17
20585 | 147.85 | 91.56 | 1232.00 | 5.03
Cycles | Force (N) | Volume (mm3) | Slip distance (m) | 
1 | 103.87 | 7.29 | 0.06 | 11731.00
100 | 106.90 | 7.64 | 5.99 | 119.43
1000 | 114.04 | 9.55 | 59.85 | 13.99
5000 | 138.77 | 23.87 | 299.24 | 5.75
10000 | 143.50 | 44.41 | 598.47 | 5.17
20585 | 147.85 | 91.56 | 1232.00 | 5.03
Angle location = 0 radian
Angle location = radian

## Slide 18: Bayesian Inference
Model parameter: wear coefficient and STD of noise
Measured data: averaged wear volume between 0 and radians
Likelihood: normal and lognormal
Mean wear volume
Use the average normal force
For lognormal distribution,
Prior distribution
  Non-informative prior for
: # of cycles
: # of intervals

## Slide 19: MCMC Simulation
Posterior distribution (non-informative prior)
  Measurement model
MCMC sampling results
Burn-in

## Slide 20: MCMC Simulation cont.
Statistical moments of parameters
MCMC | 7.82x10-4 | 5.61 | 0.93x10-4 | 2.59 | 0
Exact Sol. | 7.76x10-4 | 5.63 | 0.92x10-4 | 2.51 | 0
Error (%) | 0.79 | 0.47 | 1.09 | 3.13 | 0
MCMC | 7.82x10-4 | 5.61 | 0.93x10-4 | 2.59 | 0
Exact Sol. | 7.76x10-4 | 5.63 | 0.92x10-4 | 2.51 | 0
Error (%) | 0.79 | 0.47 | 1.09 | 3.13 | 0

## Slide 21: Identification of Wear Coefficient
Posterior distribution (normal likelihood)

## Slide 22: Identification of Wear Coefficient cont.
Posterior distribution (lognormal likelihood)

## Slide 23: Identification of Wear Coefficient cont.
Using the first 5 data
  STD from lognormal likelihood (0.51) is better than that of normal likelihood (0.90), but the means are nearly identical
  Maybe because wear coefficient is non-negative
Likelihood | Prior | Data set No. | 3 | 4 | 5 | 6
normal | non-inform | mean | 17.49 | 8.28 | 7.89 | 7.57
 |  | std. | 10.02 | 2.32 | 0.90 | 0.40
 | prior | mean | 5.11 | 5.42 | 5.93 | 6.89
 |  | std. | 0.73 | 0.73 | 0.76 | 0.57
lognormal | non-inform | mean | 20.81 | 8.89 | 7.88 | 7.64
 |  | std. | 5.82 | 1.17 | 0.51 | 0.25
 | prior | mean | 5.46 | 5.67 | 6.29 | 7.41
 |  | std. | 0.72 | 0.75 | 0.77 | 0.25

## Slide 24: Identification of Wear Coefficient cont.
the use of a normal prior leads to underestimation of the mean for k
  Due to the inaccurate prior distribution
it can be concluded that the prior contributes significantly to the posterior distribution
  the prior information is not consistent with observed data
  Non-informative cases are close to Laplace distribution
Normal prior failed to include the target value
  Due to erroneous prior
Normal likelihood
Lognormal likelihood

## Slide 25: Prediction of Wear Volume
Use the identified wear coefficient, predict wear volume
  Predict wear volume at 6th data (20,585 cycles)
the use of selected prior does not predict the wear volume well
the size of the interval of the lognormal likelihood is smaller than that of the normal likelihood
Normal likelihood
Lognormal likelihood

## Slide 26: Predicted Distribution of Wear Volume

## Slide 27: CI and PI of Wear Volume
CI and PI have a tendency to gradually decrease from 1,000 cycles as the cycles increase
CI and PI are small at first stage
  Large uncertainty in wear volume, but wear volume itself is very small

## Slide 28: CI and PI of Wear Volume cont.
The CIs and PIs of the lognormal case are smaller than that of the normal case, which demonstrates improved accuracy
Data set No. |  |  | 1 | 2 | 3 | 4 | 5 | 6
measured wear V |  |  | 4.44 | 5.105 | 8.825 | 24.175 | 45.31 | 92.73
C.I. | N | 95% | 6.61 | 12.13 | 22.14 | 35.75 | 56.25 | 100.38
 |  | 5% | 0.75 | 0.35 | 2.03 | 12.78 | 38.87 | 85.09
 |  | inter | 5.86 | 11.77 | 20.11 | 22.97 | 17.38 | 15.28
 | LN | 95% | 6.61 | 7.06 | 18.73 | 32.88 | 52.27 | 99.04
 |  | 5% | 2.50 | 3.60 | 7.66 | 21.52 | 42.31 | 88.78
 |  | inter | 4.11 | 3.46 | 11.07 | 11.36 | 9.96 | 10.26
P.I. | N | 95% | 9.19 | 20.32 | 30.96 | 40.34 | 60.64 | 104.04
 |  | 5% | -2.84 | -9.18 | -7.01 | 7.56 | 33.78 | 81.22
 |  | inter | 12.03 | 29.50 | 37.97 | 32.78 | 26.87 | 22.82
 | LN | 95% | 9.90 | 12.22 | 23.72 | 36.06 | 55.18 | 101.86
 |  | 5% | 0.24 | 1.23 | 5.18 | 19.36 | 39.87 | 86.70
 |  | inter | 9.66 | 10.99 | 18.53 | 16.70 | 15.30 | 15.15

## Slide 29: 3. Correlated Damage Parameters under Noise and Bias

## Slide 30: Motivation
Maintenance is essential to keep Airplanes safe
  Preventive Maintenance (PM)
    manual inspection with equipment
    accurate but can miss large damage
    cost and time inefficient
    detecting current damage
  Condition-based Maintenance (CBM)
    Structural Health Monitoring (SHM)
    cost and time efficient
    predicting the future status and RUL
Damage
Sensors/actuators
prognostics

## Slide 31: Introduction
Prognostics methods
  data-driven approach
  model-based approach
  hybrid approach
Crack growth
in an aircraft panel
  physics model: Paris model
  measurement data
  identifying model parameters
  predicting future status and RUL

## Slide 32: Damage growth and measurement uncertainty models
Damage growth model
  Paris model:
    : half crack size
    : number of cycles
    : range of stress intensity factor
    : stress range
    : damage parameters
  half crack size, after cycles
  critical crack size
[ Through-the-thickness crack in a fuselage panel ]
σ
σ

## Slide 33: Damage growth and measurement uncertainty models
Measurement uncertainty model
  synthetic measurement data
    not exist real SHM data
    larger noise than lab measurement
    useful for parameter study
  synthetic data generation
    assume:
    bias:
    noise:
    three different levels of loading
      for estimating: =86.5 and 78.6 MPa
      for validation: =70.8 MPa
[ bias = +2mm and noise = 0mm ]
[ bias = +2mm and noise = 5mm ]

## Slide 34: Damage growth parameters estimation
Bayesian inference for identifying parameters
  Bayes’ theorem:
  likelihood function
  prior PDF:
    : unknown parameters
    : observed crack sizes
    : likelihood
    : prior PDF of
    : posterior PDF
    : STD of noise
    : deterministic bias

## Slide 35: Damage growth parameters estimation
Posterior distributions of correlated parameters with zero noise and bias 2mm
[ n =13 ]
[ n =17 ]

## Slide 36: Damage growth parameters estimation
Posterior distributions of correlated parameters with zero noise
 |  | n = 13 |  |  |  | n = 15 |  |  |  | n = 17 |  |  | 
 |  | m | log(C) | a0 | b | m | log(C) | a0 | b | m | log(C) | a0 | b
true values |  | 3.8 | -22.6 | 10 | ±2 | 3.8 | -22.6 | 10 | ±2 | 3.8 | -22.6 | 10 | ±2
b=+2mm | median | 3.82 | -22.8 | 10.6 | 1.37 | 3.81 | -22.7 | 10.4 | 1.53 | 3.82 | -22.7 | 10.4 | 1.52
 | error (%) | 0.49 | 0.57 | 5.67 | 31.7 | 0.32 | 0.37 | 4.00 | 23.6 | 0.47 | 0.44 | 3.84 | 24.2
b=-2mm | median | 3.78 | -22.5 | 9.50 | -1.44 | 3.78 | -22.5 | 9.51 | -1.41 | 3.78 | -22.5 | 9.49 | -1.35
 | error (%) | 0.40 | 0.50 | 4.96 | 28.0 | 0.40 | 0.48 | 4.94 | 29.5 | 0.55 | 0.55 | 5.11 | 32.7
[ The median of identified parameters and the errors with the true values ]

## Slide 37: Damage growth parameters estimation
Handling correlated parameters
  two sets of correlated parameters
    and
    and
  and : easy to estimate the correlation
    constant
    constant
    the number of parameters and correlation sets decreases:
[ Two sets of correlated parameters ]
 


## Slide 38: Damage growth parameters estimation
Posterior distributions of correlated parameters with three different levels of noise
[ b = +2mm ]
[ b = -2mm ]

## Slide 39: Damage propagation and RUL prediction
Prediction of crack growth with bias=+2mm
[ n = 13 ]
[ noise = 1mm ]
[ n = 17 ]
[ noise = 5mm ]
[ n = 13 ]
[ n = 17 ]

## Slide 40: Damage propagation and RUL prediction
Prediction of RUL:
[ noise = 0.1mm ]
[ bias = +2mm ]
[ bias =- 2mm ]
[ noise = 1mm ]
[ noise = 5mm ]

## Slide 41: Conclusions
Identification of the Paris model parameters that govern the crack growth in an aircraft panel and to predict RUL.
  The Bayesian inference was employed for identifying correlated parameters.
  The synthetic data including deferent levels of noise and bias were utilized as measured data from SHM systems.
The correlated parameter identification is sensitive to the level of noise.
However, the predicted RUL is relatively accurate

## Slide 42: Identification of Model Parameters
Correlated distribution can be reasonably accurate for RUL prediction
However, we still want to identify model parameters
  The operating condition may change in the future
  It can be used fleet prognostics
Question: How can we identify accurate model parameters under correlation?

## Slide 43: Statistical distribution of crack propagation and RUL

## Slide 44: Correlation between two Paris model parameters
Posterior joint PDF of m and C
log(C)

## Slide 45: Correlation between Model Parameters
Same crack growth rate with different combinations of parameters

## Slide 46: Evolving correlation relationship with respect to cycles

## Slide 47: Correlation between load condition & model parameters
Illustration of equivalent parameters to different loadings

## Slide 48: Correlation between initial crack size and bias in data

## Slide 49: Identifying model parameters using two different stages
Crack propagation on 7075-T651 plate
From fatigue crack growth database for damage tolerance analysis

## Slide 50: Relationship between model parameters
In terms of crack growth rate
In terms of crack size
Relationship between m and C
(17)
(18)

## Slide 51: Evolution of correlation at different stages

## Slide 52: Identifying model parameters using two different stages
Posterior joint distributions of m and log(C) around N4 and N9 cycles
Combined posterior distribution
True model parameters:
m = 2.81
log(C) = -17.77
Identified parameters:
m ~ N(2.81, 0.032)
log(C) ~N(-17.77, 0.022)

## Slide 53: Identifying model parameters using two different loading conditions

## Slide 54: Identification of correlated model parameters using two different loading conditions
Posterior joint distributions of m and log(C) under nominal and maximum operating conditions
Combined posterior distribution
True model parameters:
m = 2.81
log(C) = -17.77
Identified parameters:
m ~ N(2.81, 0.052)
log(C) ~N(-17.77, 0.022)

## Slide 55: Conclusions
1. Many model parameters and loading conditions are often correlated and their correlation structures change over the damage growth or loading conditions.
2. We used the evolved correlation structures to identify accurate model parameters
  Using two different damage stages
  Using two different loading conditions
3. The identified model parameters can be used at similar systems or at different loading conditions.

## Slide 56: 4. Usage of Accelerated Life Test Data for Prediction RUL at Field Operating Conditions

## Slide 57: Motivation
Prognostics is to predict future damage and RUL of in-service systems based on the damage data.
It is expensive to obtain damage data in-service systems.
Instead, it is easy to obtain accelerated test data since companies frequently use them for the purpose of design.

## Slide 58: Accelerated Life Test (ALT)
Most companies conduct ALT in the development stage
  Using much severe loading/usage conditions
  Many sensors are used to monitor degradation over time
  So far, accelerated life test (ALT) data are mostly used to estimate the average life of a fleet
Challenges of ALT for prognostics
  difficult to use for prognostics because in-service usage conditions are not reflected
  too conservative life prediction if the ALT data are directly used
  ALT data has been used to build a degradation model when physical models are not available, but the model may not be good for normal loading cond.
ALT data must be converted to the nominal loading conditions

## Slide 59: Assumptions
During ALT, sensors are placed in the system or periodic inspections are performed such that the history of damage growth is measured until the damage grows up to a threshold
  The threshold is determined at which the system cannot be operated further without maintenance
  The time when the damage grows to the threshold is called the end of life (EOL).
The current system in the field has a similar damage data up to the current time
The objective is to predict the EOL of the current system so that maintenance can be ordered before the system reaches inoperable situation
Four different scenarios are considered based on available information, such as physical models and field loading conditions.

## Slide 60: Introduction
Prognostics methods can be categorized into three approaches based on the usage of information
Prognostics
Approaches
Data-driven
Physics-based
Hybrid approach
data-driven
physics-based
= +
damage data
damage data
+loading
model
para.
Extrapolation with
Mathematical model
Physics with
Physical model
Particle filter,
Bayesian method,
Kalman filter.
Algorithms
parameter
estimation
methods
Neural network,
Gaussian process regression,
Least square regression.
Algorithms
co-efficient

## Slide 61: Physics-based approaches
damage
model para.
loading
cycle
=
Paris model
Archard’s wear model
Anand model
Physical model
(unknown parameters)
θ=[m, C]
update

## Slide 62: Data-driven approaches
polynomial,
transfer function,
covariance function.
Mathematical model
y=β0+β1x+β2x2
damage
coefficient
(unknown parameters)
w=[β]
Possible input, x
damage data
loading conditions
time

## Slide 63: Crack growth example
Crack growth in a fuselage panel
  Paris model:
    : half crack size
    : number of cycles
    : range of stress intensity factor
    : stress range
    : damage parameters
  Synthetic data generation
    assume:
    noise:
    different levels of loading
      accelerated operating:
      field operating conditions:
[ Through-the-thickness crack
in a fuselage panel ]
σ
σ

## Slide 64: Crack growth example
Generated data & different scenarios
[ accelerated operating conditions ]
[ field operating conditions ]
 | Case 1 | Case 2 | Case 3 | Case 4
Physical model | O | O | X | X
Future loading | O | X | O | X
Available method | Physics-based approaches (Particle Filter) |  | Data-driven approaches (Neural Network) | 
[ four scenarios ]

## Slide 65: Case 1: Physics model + loading conditions
the conventional case of physics-based prognostics
  accelerated life test data are unnecessary for prognosis
The accelerated test data can be used to provide a better prior
  to improve prognostics accuracy and to reduce uncertainty in the early stage
Ex) Paris model for crack growth (Al 7075-T651)
  Use material handbook data as a prior: and
5,000 samples from initial distribution
Initial distribution is so large that crack growth prediction is not useful
Incorporate ALT data to reduce the uncertainty in the initial distribution

## Slide 66: Case 1: Physics model + loading conditions
Improving the prior distribution using 3 ALT data
Much narrower distribution
Correlation is captured

## Slide 67: Case 1: Physics model + loading conditions
Damage & RUL prediction (with priors from literature)
[ 4000 cycles ]
[ 19000 cycles ]
[ 11000 cycles ]
parameters update
RUL
RUL
RUL

## Slide 68: Case 1: Physics model + loading conditions
Comparison of RUL prediction results
  Utilizing ALT for prior provides fairly accurate and precise results even from an early stage
 | PH ( α=10%) | α-λ accuracy (α=10%, λ=0.5) | RA (λ=0.5) | CRA
prior from literature | 11000 | false (0.2504) | 0.9161 | 0.8479
prior from ALT data | 22000 | True (0.6046) | 0.9240 | 0.9285
[ priors from literature ]
[ prior from accelerated test data ]
[ prognostics metrics ]

## Slide 69: Case 2: Physics model, no loading conditions
During ALT, loading conditions are well characterized
In the field, loading conditions are variable and difficult to measure
When future loading is uncertain, it will make sense to assume its range roughly
  True loading condition: 68 MPa
  Uncertain loading condition: U~(50, 90) MPa
Two ways to predict RUL
  Bothe parameters and loading condition are updated
  Only loading condition is updated
  (Only model parameters are updated)

## Slide 70: Case 2: Physics model, no loading conditions
Both parameters and loading conditions updated
  ALT data to update the prior distribution of model parameters
  Field data to update both the loading and model parameters
 | PH ( α=10%) | α-λ accuracy (α=10%, λ=0.5) | RA (λ=0.5) | CRA
prior from literature | 11000 | false (0.3246) | 0.8739 | 0.8116
prior from test data | 13000 | false (0.4728) | 0.9704 | 0.8643
[ prognostics metrics ]
[ priors from literature ]
[ prior from accelerated test data ]

## Slide 71: Case 2: Physics model, no loading conditions
Only loading condition updated
  prior information from accelerated life test data are significantly better than ones using the prior information from the literature
[ priors from literature ]
[ prior from accelerated test data ]
 | PH ( α=10%) | α-λ accuracy (α=10%, λ=0.5) | RA (λ=0.5) | CRA
prior from literature | 2000 | false (0.0578) | 0.4627 | 0.4450
prior from test data | 11000 | True (0.5182) | 0.9727 | 0.8751
[ prognostics metrics ]

## Slide 72: Case 3: No Physical model + loading conditions
Data-driven method (NN)
Adding loading conditions to input variable
Damage growth prediction at 13,000 and 19,000 cycles
Not using ALT data (only current system’s data)
  Long term predictions diverge

## Slide 73: Case 3: No Physical model + loading conditions
Use ALT data as training data
  Good short term predictions as early as 2,000 cycles
  Long term predictions after 19,000 cycles are also close to the true
Even if ALT loading conditions are different from the field loading, ALT data can be used for training data

## Slide 74: Case 4: No Physical model, no loading conditions
Data-driven prognostics
  Loading cannot be updated as no physical model
  Many data similar to the field loading conditions are required
damage data at ALT conditions are mapped into the damage data at the field operating condition so that they can be used as training data
Inverse power method
  a linear relation between the logarithm of life and load
  , : can be found using life data at 2 different loading conditions

## Slide 75: Case 4: No Physical model, no loading conditions
Use crack size = as a threshold
  Life = 1,735 (145 MPa), 1,947 (140 MPa), 2,241 (135 MPa)
  Plot in log(Load) vs. log(Life) and fit a straight line: = slope, =y-intercept
  Life span for other loading conditions can be predicted using
Repeat with different threshold to obtain degradation curve
  Uncertain load range is reduced to [65, 75]MPa based on these curves
[ accelerated test data ]
[ inverse power model ]
[ mapping with estimated life ]

## Slide 76: Case 4: No Physical model, no loading conditions
Sources of uncertainty
  (1) Uncertainty in regression of accelerated life test data: Approximation of lifespan at given threshold
  (2) Uncertainty in the inverse power model: Uncertainty in coefficients
  (3) Uncertainty in inverse regression: to estimate the uncertainty in damage size for a given cycle
[ mapping into half-loads ]
[ mapping uncertainty ]
Median + 1mm noise
We can use mapping data for training

## Slide 77: Case 4: No Physical model, no loading conditions
Damage growth prediction results at 10000 cycles
  using mapped data is much better than not using mapped data in both short-term and long-term predictions
[ only in-service damage data ]
[ with mapping results ]

## Slide 78: Conclusions
Practical use of accelerated test data is presented for the prognostics methods to overcome limited number of (in-service) damage data.
Four different cases are considered according to the availability of physical model and future loading conditions.
  Using accelerated test data increases prediction accuracy in early stage of physics-based prognostics.
  It covers insufficient data problem of data-driven prognostics.

## Slide 79: 5. Bearing Prognostics Method Based on Entropy Decrease at Specific Frequencies

## Slide 80: Bearing Failure
Spall failure in bearing is a common failure in rotating machineries
  80~90% of aircraft engine failures
Difficult to measure degradation
  Difficult to disassemble, difficult to put sensors in moving parts
vibration signals are used for damage evaluation for several decades
  These signals can be used to find the relationship between bearings’ failure mechanism and signal strength at a specific frequency
  since the damage grows rapidly in spall, it is difficult to detect the damage early enough to prepare for maintenance

## Slide 81: Motivation
Vibration signal are generally measured for bearing fault diagnosis and prognosis.
  Red line: threshold of 20g
Unfortunately, it is very challenge to extract damage feature.
  Raw data (acceleration) are not consistent in a pattern of signal, life span, and threshold even if they are from the same systems and usage conditions.
  There are many efforts to tackle this problem, e.g. methods based on frequency domain and entropy, but not mature yet.
We propose an improved method for bearing prognosis.
  based on entropy change in the frequency domain
Notes: Accelerometers were used to measure the vibration

## Slide 82: FEMTO Bearing Data
FEMTO bearing*
  Vibration signals are monitored during 0.1 second with a sampling rate of 25.6 kHz every 10 seconds
  0.1 second in every 10 seconds is considered as one cycle, and there are 2560 samples in each cycle
[ Experimentation platform: PRONOSTIA ]
*P. Nectoux, R. Gouriveau, K. Medjaher, E. Ramasso, B. Morello, N. Zerhouni, C. Varnier. PRONOSTIA: An Experimental Platform for Bearings Accelerated Life Test. IEEE International Conference on Prognostics and Health Management, Denver, CO, USA, 2012.
Notes: FEMTO-ST institute: Franche-Comte Electronics, Mechanics, Thermal Processing, Optics - Science and Technology

## Slide 83: FEMTO Bearing Data cont.
Data acquisition (Acceleration)
  Sampling frequency: 25.6 kHz
  2560 samples (during 1/10 secs.) are recorded every 10 secs.
Three different operating conditions
  Condition 1: 7 Sets
  Condition 2: 7 Sets
  Condition 3: 3 Sets
Threshold: 20g
One cycle,
2560 samples

## Slide 84: Information Entropy
Entropy: a measure of disorder and randomness of the system
  When a system absorbs energy from others, its entropy increases and the counterpart decreases
  The total entropy of an isolated system, however, never decreases
Information entropy (Shannon entropy)
  entropy increases when uncertainty increases by missing information contained in data
  For the bearing problem, the total energy in bearing increases as the work done by external force is consumed by damage initiation/propagation
  For bearing degradation, we use vibration signals rather than the total thermodynamic energy

## Slide 85: Information Entropy cont.
Entropy
  : information source (bins of acceleration data), normalized, 255 intervals
  : number of possible outcomes
  : probability of each outcome, # of data in the bin/total # of data

## Slide 86: Information entropy calculation for bearing data
Assume vibration amplitude linearly increases with cycles
  Probability remains constant
  As increases, entropy increases
  Entropy is always calculated from the start to the current cycle (accumulation)
Assume vibration amplitude linearly decreases with cycles
  From to cycles, # of bins are the same, but data at cycles are more located in the middle bins
  Entropy decreases
Entropy increase
Entropy decrease

## Slide 87: Time Domain Vibration Signals
Raw data for Sets 1 and 2 of Condition 1
  entropy increases as the vibration energy increases
  it seems that the entropy can be used as a degradation feature
  entropy change cannot be observed unless there is a change in vibration signals
  many vibration signals from bearing test do not show a significant change until just before failure under large noise (Set 2)
Set 1 of Condition 1
Set 2 of Condition 1

## Slide 88: Entropy Change in Frequency Domain
FFT with Nf frequencies: Nf curves of entropy vs cycles
Idea: Among Nf curves, use those frequencies that show a consistent behavior (increase of decrease) for all bearing tests

## Slide 89: Entropy May Increase or Decrease
the amplitude increases as the level of damage increases
  True for time domain. True for frequency domain with localized damage
  vibration characteristics continue to change as degradation progresses
The behavior is more complicated in the frequency domain
  The natural frequency changes as the stiffness decreases due to damage
  the periodic nature of localized defects can diminish since the motion of rolling elements becomes irregular and disturbed as damage progresses
Ex) frequency changes from 2.4 Hz to 2.2 Hz due to damage growth
  Amplitude increases at 2.0 Hz, while decreases at 2.5 Hz

## Slide 90: Degradation Feature
amplitude increases at some frequencies, while decreases at other frequencies
After examining 14 FEMTO data sets, it is found that the decreasing trends in entropy are consistent for all data sets
  decreasing amplitudes are more stable and consistent than increasing ones
frequencies showing decreasing entropy are around 4 kHz for all data sets
the decreasing entropy in the frequency domain is used as a degradation feature

## Slide 91: Summary of feature extraction method
The idea of this method is based on:
  In most case, raw data don’t give degradation information.
    Multiple/complex damage modes exist in a bearing system.
  Certain changes in specific frequencies may contain degradation information.
    It is a kind of decomposed signal.
    Some of them represent noise part, and some of them catch a damage change.
Procedure
  Step 1: Reshape FFT results in frequency-wise
  Step 2: Select specific frequencies having degradation information based on entropy decrease

## Slide 92: Step 1: Frequency-wise plot
Raw data
…
…
1 Cycle
k Cycle
…
FFT
Fast Fourier
Transform
Cycles
Amplitude
Frq: 2
.
.
.
Frq: 2560/2
Frq: 1
There are 2560 different frequency from 0 Hz to 25.6 kHz.
Take one frequency (Frq: 1).
That frequency has different amplitude value in terms of cycle.
Frequency-wise
Re-plot

## Slide 93: Step 2: Select specific frequencies
Entropy (information theory), H
  Equation:
  Nature
    The entropy of an isolated system never decreases.
    The entropy of a system (A) decreases only when it interacts with some other system (B) whose entropy increases in the process.
  System A
    Bearing test system
  System B
    Microscopic damage in bearing
  Without B, entropy of A does not decrease.
  After B, entropy of A decreases.
Notes: The definition of the information entropy is, however, quite general, and is expressed in terms of a discrete set of probabilities pi so that
Irreversible / commonly understood as a measure of disorder
http://electron6.phys.utk.edu/101/CH8/entropy.htm
  고립계: 열, 일, 에너지 이동 차단 (교환x)
  Entropy ↑: 무질서도 ↑, 에너지는 보존 but 무용에너지 ↑
  Entropy ↓: 생물의 생장, 광합성 (유용 에너지가 증가하기 때문에?)

## Slide 94: Step 2: Select specific frequencies
Some frequencies show much more clear entropy decrease than raw data.
Frq: 1
Frq: 2
.
.
.
Frq: 2560/2
Cycles
Amplitude
Cycles
Entropy
Frq: 1
Frq: 2
.
.
.
Frq: 2560/2
Those specific frequencies are selected.
Taking a median
Cycles
Entropy
n frequencies

## Slide 95: Results of all test sets
[ Condition 1 ]
[ Condition 3 ]
[ Condition 2 ]

## Slide 96: Model selection and threshold
Model:
  Estimate beta 1 and beta 2 based on entropy data given up to current time.
Cycles
Entropy
Threshold
  Degradation rate:
Max.
Min.
  There are two groups for threshold.
    Faded by 20% and 45%
[ Degradation rate
of all sets ]
Notes: Ratio min. entropy to max. entropy

## Slide 97: Prediction results of degradation
Threshold: 20%
Threshold: 45%
What if
current cycle
is here?
[ Condition 1 ]
[ Condition 3 ]
[ Condition 2 ]
EOL
Max. Entropy
Max. Entropy is proportional to EOL.
But, several training data are required.

## Slide 98: Prediction results RUL
 |  | Set 1 | Set 2 | Set 3 | Set 4 | Set 5 | Set 6 | Set 7
Cond#1 | Current cycle | 2101 | 652 | 1801 | 1138 | 2301 | 2301 | 1501
 | RUL_True | 701 | 218 | 573 | 34 | 161 | 146 | 757
 | RUL_Prediction | 87 | 475 | 460 | 34 | 133 | 976 | 442
 | Error (%) | 87.65 | -117.97 | 19.64 | -0.38 | 17.34 | -568.54 | 41.61
Cond#2 | Current Cycle | 682 | 597 | 1201 | 611 | 2001 | 571 | 171
 | RUL_True | 228 | 199 | 753 | 139 | 309 | 129 | 58
 | RUL_Prediction | 98 | 109 | 627 | 21 | 201 | 90 | 44
 | Error (%) | 57.17 | 45.20 | 16.75 | 84.75 | 34.91 | 29.94 | 24.83
Cond#3 | Current cycle | 385 | 1227 | 351 |  |  |  | 
 | RUL_True | 129 | 409 | 82 |  |  |  | 
 | RUL_Prediction | 84 | 388 | 5 |  |  |  | 
 | Error (%) | 34.87 | 5.11 | 94.20 |  |  |  | 
Score based on the competition criterion: 0.3605
(When all prediction results of RUL is the exactly same as true ones, the score=1.)
Current cycle
  For set 1 and 2: 75% of lifespan
  For set 3~set 7: given in challenge problem (IEEE PHM 2012)
Notes: Winner’s sore: 0.1977
Total sets: 0.3440
Test sets: 0.3605

## Slide 99: True EOL is unknown
True EOL is unknown in real problems because it should be repaired before failure.
[ FEMTO Bearing failure ]
unit (%) | Set 1 | Set 2 | Set 3 | Set 4 | Set 5 | Set 6 | Set 7
Cond#1 | 84 | 4 | 16 | 6 | 11 | 50 | 5
Cond#2 | 80 | 15 | 64 | 7 | 63 | 29 | 52
Cond#3 | 76 | 84 | 8 |  |  |  | 
Wasted life by fixing a threshold to 20%
  Ratio of wasted life and true EOL
Half of bearings represent below 16% waste rate.

## Slide 100: Threshold 20% is not an absolute value
IMS bearing*
*J. Lee, H. Qiu, G. Yu, J. Lin, and Rexnord Technical Services (2007). 'Bearing Data Set', IMS, University of Cincinnati. NASA Ames Prognostics Data Repository, [http://ti.arc.nasa.gov/project/prognostic-data-repository], NASA Ames, Moffett Field, CA.
Four double row bearings (16 rollers) were installed on a shaft.
Three sets of test data are available.
  Degradation feature
But, the level of threshold is different.
Faded by around 70%
FEMTO: accelerated test
IMS: nominal conditions
By applying the same method,
Damage feature is found.
Max. Entropy is proportional to EOL.

## Slide 101: Conclusions
Future work
  Apply this method to other bearing problems under different level of (accelerated) loading conditions.
  Hope there is a relation between threshold (degradation rate) and level of loading conditions.
  Uncertainty caused by taking median of entropy from different frequencies, model parameter estimation, and threshold will be considered.
This method can be widely applicable if certain relation (threshold-loading) is found or if several training data sets are available in each bearing problem.
  Procedure summary of the method
    Reshape FFT results in frequency-wise
    Select specific frequencies showing entropy decrease
    Take a median of those entropies as a damage feature
    Model selection for prognosis, and estimate model parameters
    Setting a threshold (degradation rate based on the max. entropy)