## Slide 2: Chap 1 Introduction to Surrogate Models
Overview of surrogate modeling and issues

## Slide 3: What Is A Surrogate Model?
An engineering method used when a quantity of interest (QoI) cannot be easily directly measured (calculated) so an approximate (surrogate) of the QoI is used instead
Engineering design problems require experiments and/or simulations to evaluate design objective and constraints as a function of design variables
  Ex) To find the optimal airfoil shape, an engineer simulates the airflow around the wing for different shape variables (length, curvature, material, ..)
Single simulation is expensive, and yet, design optimization, design space exploration, sensitivity analysis and what-if analysis require thousands or millions of simulations
Use surrogate!

## Slide 4: Example of Expensive Computer Simulation
Dispersed multiphase flow, where numerous particles interact with shock waves generated from explosives
Simulation of shock interaction with distributed particles took 15,000 seconds with 2,400 clusters in a high-performance computing facility

## Slide 5: What Is A Surrogate Model? cont.
Surrogate models, response surface models, metamodels or emulators
  mimic (approximate) the behavior of the simulation model as closely as possible while being computationally cheap(er) to evaluate
  Surrogate models does not concern physics or theory in the simulation. It only concerns input-output behavior
  A simple mathematical model is constructed based on limited number of input-output pair of data (samples)
  This approach is also known as behavioral modeling or black-box modeling
  When only a single design variable is involved, the process is known as curve-fitting

## Slide 6: Relationship b/w QoI and Input Variables
Normally QoI is governed by complicated physics and numerical simulation
Relationship b/w QoI and input variables can be simplified
Surrogate model:
L
F
h
b

## Slide 7: 1.2 Surrogate Models
Different surrogates start with different concepts

## Slide 8: Illustration of Surrogate Approximation
Surrogate modeling: to represent the relationship between the QoI and input parameters using known functional forms with unknown coefficients
Generate samples in the input domain (Design of experiments)
  Sample location:
  QoI at sample location :
  th sample pair:
Run simulations with input samples  output samples
Fit a surrogate model
Simulation using surrogate
g
x1
x2

## Slide 9: Example of Surrogate Modeling
Notes: A full-frontal or side impact simulation for estimation of a response function (e.g., peak acceleration, intrusion distance) could take several hours on a computer cluster. Through surrogate modeling, a smooth and computationally efficient representation of each response function can be generated. Such models can be extremely helpful in both trade space exploration and design optimization pursuits.

## Slide 10: Cost of Surrogate Modeling
Surrogate model can be simple polynomials or complicated statistical functions
  Cost of constructing the surrogate model and evaluating the output QoI using the surrogate model is assumed to be negligible compared to that of evaluating the output QoI samples
  Cost of a surrogate model is determined based on the number of samples to construct it
Accuracy of a surrogate model is proportional to the number of samples
Trade-off between the accuracy of a surrogate model and the cost of constructing it

## Slide 11: Polynomial Response Surface (PRS)
Early surrogate based on experimental data
  Linear or quadratic polynomials
  Data include noise surrogate filters out noise
Functional form: linear combination of monomial bases
  Unknown coefficients are determined to minimize error
  PRS does not pass through samples (regression)
Assumption: the surrogate model form is accurate, but the data have random noise
Chapter 2 for PRS
0
0.2
0.4
0.6
0.8
1
-5
0
5
10
15
20
C.I.
Samples
PRS

## Slide 12: Kriging (Gaussian Process) Surrogate
Surrogate based on computer simulations
  Not much random noise (numerical error), but bias-like predictions
  To approximate simulation results, samples are assumed to be exact
  Difference b/w surrogate prediction and simulation data is considered prediction error
Assumption: data are exact, but the model form has uncertainty
  predicts the simulation data exactly, but the uncertainty increases as a prediction point is farther away from data points
Chapter 7 for Kriging surrogate
0
0.2
0.4
0.6
0.8
1
0
5
10
15
20
C.I.
Samples
Kriging

## Slide 13: Which Surrogate Is the Best?
Polynomial response surfaces (PRS), Kriging, Radial basis function, Support vector machines, Space mapping, Artificial neural networks, and Bayesian networks
Different surrogates have different assumptions
  When the nature of true function is not known a priori so it is not clear which surrogate model is the most accurate
  When the nature of true function is known, physics-based surrogates such as space-mapping based models are the most efficient
  There is no consensus on how to obtain the most reliable estimates of the accuracy of a given surrogate
Ensemble of multiple surrogates can be used to reduce the risk of using a bad surrogate

## Slide 14: 1.3 Design of Experiments: Sampling
Surrogate strongly depends on the number and location of samples

## Slide 15: Goals of Surrogate Modeling
To Approximate a QoI as accurate as possible, using as few simulation evaluations as possible
  Sample selection (sequential design, optimal experimental design (OED), design of experiments (DOE), or active learning)
  Construction of the surrogate model and optimizing the model parameters (bias-variance trade-off)
  Appraisal of the accuracy of the surrogate.
The accuracy of the surrogate depends on the number and location of samples (experiments or simulations).
Various design of experiments (DOE) techniques cater to different sources of errors, in particular, errors due to noise in the data or errors due to an improper surrogate model.
DOE in Chapter 3

## Slide 16: Design of Experiments (DOE)
Adaptive sampling, sequential design, or active learning
  starting from a small number of samples, additional samples can be added sequentially to improve the accuracy of surrogate prediction
  require a criterion to determine the next sample locations, such as D-optimal design and minimum bias design
  based on a trade-off between minimizing bias (i.e., error) and/or minimizing variance (i.e., uncertainty)
Space-filling design
  a better surrogate can be obtained with more samples
  locate samples more or less uniformly distributed to the entire sampling space
  minimize the maximum distance between samples

## Slide 17: 1.4 Interpolation vs. Extrapolation
Major challenge of surrogate model is prediction at unsampled region

## Slide 18: Curse of Dimensionality
Important to distribute sample to the entire design space
  often impossible to generate enough samples in high dimensions
The range of each variable is halved, put a sample at the center of each sub-domain (one sample at each orthant)
  No. of samples increases exponentially: ,
Samples
Extrapolation region
Interpolation region

## Slide 19: Interpolation vs. Extrapolation
Interpolation domain is the convex hull of samples
  2D: interpolation (25%) vs. extrapolation (75%)
  Mostly extrapolation in high-dimensions (10D, extrapolation = 99.9%)
If samples are located at corners, distances b/w samples become too large
Major challenge in surrogate modeling is how to guarantee the accuracy of prediction in the extrapolation region!
Samples
Extrapolation region
Interpolation region

## Slide 20: Prediction Accuracy at Interpolation & Extrapolation Regions
21 equal-interval samples at from true function
Use radial-basis function surrogate
  Exact at the interpolation region
  Huge error at the extrapolation region and
A surrogate with a good fit in the interpolation region can fail miserably in predicting the extrapolation region!

## Slide 21: Can We Make the Entire Domain an Interpolation Region?
Difficult to make the entire domain the interpolation region
  samples need to be located in all vertices of the input domain (curse of dimensionality)
  possible that an interpolation region may have significant error if the distance between samples is large
Maximum distance b/w samples
  Assume domain range is normalized to be
  2D: , 10D:
As the distance between the samples increases, the prediction accuracy decreases
  similar to the behavior seen in the extrapolation region

## Slide 22: 1.5 Flowchart of Surrogate Modeling
Surrogate needs to be improved based on prediction accuracy

## Slide 23: Flowchart of Surrogate Modeling
Four-step surrogate modeling
Design of experiment
Numerical simulations at selected locations
Construction of surrogate models (model selection and identification)
Model validation
If necessary

## Slide 24: Flowchart of Surrogate Modeling cont.
Design of experiments (DOE):
  Sampling plan in design variable space
  The number and location of samples are determined
  Usually input variables are normalized: hyper-cube input space
  How to assess the goodness of different designs
  The number of samples is severely limited by computational cost
Numerical simulations at selected locations
  Expensive numerical simulation or experiments
  Data may include random noise or error

## Slide 25: Flowchart of Surrogate Modeling cont.
Construction of surrogate model
  Surrogate model selection
    closely related to the number and location of samples
    Flexible model comes with more coefficients need more samples
    start with a simple model and progressively increase its complexity
  Model identification (determining unknown parameters)
    minimizing the errors between the surrogate predictions and samples
Model validation
  evaluates the accuracy of the constructed surrogate model
  Predictive capabilities of the surrogate model at unsampled points

## Slide 26: Fitting Accuracy vs. Prediction Accuracy
Samples are used to fit the surrogate model
  Errors are minimum at sample locations
But surrogate needs to be a good predictor at un-sampled locations
Blue surrogate passes all sample points but has poor prediction capability
Accuracy needs additional samples that were not used in the fitting process
-2
-1
0
1
2
-5
0
5
5th-order polynomial
true function
data

## Slide 27: Cross-Validation
We can save some samples for the purpose of validation
  samples for fitting and samples for validation
  Matlab: 70% for fitting the network and 30% for testing and validation
  But one may get a better surrogate using samples than using samples
Cross-validation
  use samples for fitting and the other sample to assess the prediction error
  repeated the process times by dropping one sample at a time to obtain prediction errors
  RMS error of these errors can represent the prediction capability of the surrogate
  no samples are wasted for the purpose of validation

## Slide 28: 1.6 Overview of Surrogate Modeling
How to prevent overfitting and how to estimate prediction uncertainty?

## Slide 29: Overview of Surrogate Modeling
Simulation-based model
Samples
Estimated model
Analysis problem
Estimation problem
Appraisal problem

## Slide 30: Overview of Surrogate Modeling cont.
Analysis problem
  evaluate at sample location ,
Estimation problem
  samples are used to build the surrogate model
  Nonlinear inverse process: determine continuous from a limited amount of data,
  determined by minimizing the error between the data and prediction
Loss function

## Slide 31: Overview of Surrogate Modeling cont.
Estimation problem cont.
  samples may be exact or may include noise
  estimation problem usually does not have a unique solution
  Prediction uncertainty: multiple estimated models
Multiple possibilities of surrogates with given samples

## Slide 32: Overview of Surrogate Modeling cont.
Appraisal problem
  different definitions of error to assess goodness of against
  if the appraisal error is not satisfactory, additional samples are added, or the model form is changed to improve the prediction accuracy
Introductory level of accuracy
  check if the surrogate is accurate or not at sample locations
Prediction capability of the surrogate
  accuracy at un-sampled points (i.e., prediction points).
Consider interpolating surrogate with 5 samples
  Predictions might have error at unsampled locations

## Slide 33: Prediction Uncertainty
Surrogate prediction
  : surrogate
  : prediction error
Prediction error is often represented by a normal distribution
  : prediction variance
  Prediction has expected value and variance
  Surrogate quality: Accuracy of mean prediction and prediction uncertainty
)
), ))

## Slide 34: 1.7 Smoothness and Loss Function
A smoother surrogate is better than a complex one

## Slide 35: Quality of Surrogate Fitting
surrogate modeling determines a continuous function using a finite number of samples (nonlinear inverse problem)
  Infinitely many surrogates may satisfy the inverse problem
If multiple surrogates have the same fitting error, a smoother one is considered a better one
blue surrogate changes the sign of the slope less than that of the red one
a polynomial function with a smaller number of inflection points is considered smoother
-2
-1
0
1
2
-5
0
5
5th-order polynomial
2nd-order polynomial

## Slide 36: Regularization
Goodness is measured by not only error but also smoothness
Minimize error (loss function) + smoothness
  : family of surrogate models under consideration
  : loss of cost function used to quantify the empirical error
  : regularization parameter
  : th derivative of , a penalty term on smoothness
Closeness to the data
Smoothness of model

## Slide 37: Loss function
Loss function to determine the closeness of the model to the data
Quadratic loss function (-norm):
  Most commonly used (easy estimation of the parameters)
  Sensitive to outliers
Linear loss function (-norm):
  Also called Laplace loss function
  Use absolute value of the difference
Error
Error
Loss function
Loss function

## Slide 38: Loss functions cont.
Huber loss function:
  Quadratic for small values of its argument and linear otherwise
-loss function:
  Popular in support vector regression surrogate
  Error is considered to be zero when the difference is less than
Error
Error
Loss function
Loss function