## Slide 2: Chap 7 Kriging Surrogate Model

## Slide 3: Introduction
Polynomial response surface (Chapter 2)
  model form = known basis functions + unknown coefficients
  linear regression to determine coefficients
  surrogate converges to the mean of the trend of samples
  works well when samples are obtained from experiments with random measurement noise
Computer simulations to generate samples
  build surrogate using expensive high-fidelity simulations
  ignorable noise, handle bias separately
  interpolate samples from simulations, not regress them
  complex model form is often unknown, but continuous and smooth

## Slide 4: Introduction to Kriging Surrogate
Kriging assumes that samples are correct, but the model form is unknown or uncertain
Daniel Krige (1950s), a South African geologist
  predicting the distribution of minerals on the basis of samples
  formalized by a French engineer Georges Matheron (1960s)
Kriging is known as Gaussian process for statisticians
  samples are assumed to be multivariate Gaussian random variables
Kriging is expensive surrogate in terms of computation
  became popular after computing power is enhanced
  Still it is assumed that the cost of building a Kriging surrogate is ignorable compared to that of calculating samples
Notes: Kriging was invented in the 1950s by Daniel Krige (Professor at University of the Witwatersrand, Republic of South Africa), a South African geologist , for the purpose of predicting the distribution of minerals on the basis of samples. It became very popular for fitting surrogates to expensive computer simulations only about 40-50 years later. This is at least partly because it is an expensive surrogate in terms of computation, and it had to wait until computers became fast enough.
My experience is that of all currently popular surrogates, it has the highest chance of being the most accurate for a given problem. However, from my experience that chance is still less than 50%.
Krige, D. G. (1951). "A statistical approach to some basic mine valuation problems on the Witwatersrand". J. of the Chem., Metal. and Mining Soc. of South Africa 52 (6): 119–139.
Matheron, G., "Principles of geostatistics", Economic Geology, 58, pp 1246–1266, 1963

## Slide 5: Kriging and Cost of Surrogates
In linear regression, the process of fitting involves solving a set of linear equations once.
Moving least squares performs the fit for each function evaluation, using only nearby points.
Radial basis surrogates use shape functions that are based around data points and decay away from them, so that nearby data have more influence on prediction.
Kriging, is even more expensive, we have a spread constant in every direction, and we have to perform optimization to calculate the best set of constants (hyperparameters).
  With many hundreds of data points this can become significant computational burden.
Notes: Linear regression was invented at a time where fitting a surrogate was onerous computationally even though it only involves solving a system of linear equations. As computer resources have become cheaper, more expensive surrogates have been proposed and adopted.
For moving least squares, we need to form and solve the system at every prediction point. What we get is a surrogate that models better local effects because nearby points have more influence than points that are far away.
Radial basis surrogates create the same effect of nearby points having a larger effects by using shape functions that decay away from data points. Matlab’s radial basis neural networks do optimization to decide which of the data points should serve as shape functions and which should not. However, the spread of the shape functions (how fast they decay from the data points) is input by the user.
Kriging goes one step further in that it uses optimization to calculate the spread, and it allows the spread to be different in different directions. This requires doing an optimization problems to find these spreads, and in addition each surrogate evaluation is not cheap, especially when there is a large number of data points.

## Slide 6: 7.2 Kriging Philosophy
Samples are accurate but correlated, model form has uncertainty

## Slide 7: Kriging philosophy
We assume that the data is sampled from an unknown function that obeys simple correlation rules.
The value of the function at a point is correlated to the values at neighboring points based on their separation in different directions.
The correlation is strong to nearby points and weak with far away points, but strength does not change based on location, only separation between points.
  valid assumption if the function is continuous (smooth predictor)
  a local surrogate with shape functions
  Correlation assumption can be strength and weakness of Kriging
Normally Kriging is used for noise free data so that it interpolates exactly the function values.
Notes: For linear regression we normally assume that we know the functional shape (e.g. a polynomial) and the data is to be used to find the coefficients that will minimize the root mean square errors at the data points. Kriging takes a very different approach. It assumes that we don’t know much about the function, except for the form of correlation between the value of the function at nearby points. In particular, the correlation depends only on the separation between points and decays as they are further apart.
Kriging is a smooth predictor. If two points are close, then their Kriging estimates are close.
Kriging is usually used as an interpolator, so that if fits exactly the data, and we could not use the rms error as a way to find its parameters. That is, we assume that there is no noise in the data. There is a version of kriging with noise (often called kriging with a nugget).
Because of the correlation decay, kriging is a local surrogate with shape functions that are similar to those used for radial basis surrogates, except that the decay can be different in different directions.

## Slide 8: Reminder: Covariance and Correlation
Covariance of two random variables and
The covariance of a random variable with itself is the square of the standard deviation:
Covariance matrix
Correlation
The correlation matrix has 1 on the diagonal.
  correlation measures their propensity to move together
  when
Notes: This is a reminder of the basic statistical quantities of covariance of pair of random variables and the important concept of correlation. Remember that the variance of a random variable, is the first moment around its mean, or the square of the standard deviation. The covariance of a pair of random variables is the mixed moment of the two variables.
Correlation measures their propensity to move together. So a correlation of 1 means that they increase and decrease in perfect synchrony. The most common case is when X=cY, where c is a positive constant.
Similarly a correlation of -1 also means perfect synchrony, but in the opposite direction, and X=cY, with c a negative constant is a common case. Finally, a correlation of 0 means that they are not related. The common case is when the random variables are independent, but not all uncorrelated variables are independent. Zero correlation relates to the first moment, but there may be dependence through higher order effects.
The correlation matrix is the matrix of correlation of the components of a vector. It has 1 on the diagonal, because each variable is perfectly correlated with itself.

## Slide 9: Ex7.1) Correlation between functions at near and far points
Generate 10 random samples, translate them by a bit (0.1), and by more (1.0)
  x=10*rand(1,10);
  xnear=x+0.1; xfar=x+1;
  ynear=sin(xnear);
  y=sin(x);
  yfar=sin(xfar);
Compare corelations:
  r=corrcoef(y,ynear) 0.9894; High correlation
  rfar=corrcoef(y,yfar) 0.4229; Low correlation
Decay to about 0.4 over one sixth of the wavelength.
  Wavelength on sine function is 2~6
Notes: The fitting process in kriging needs to estimate how fast the correlation between function values decays with distance. This depends on the wavelength of the function, with short wavelength corresponding to fast decay. In the example here, we check how fast the correlation decays for sin(x) that has a wave length of 2p.
To illustrate the values of correlations that are expected between function values, we generate random numbers between 0 and 10 and evaluate the sine function at these points. We also translate the points by a small amount compared to the wavelength (0.1) and a larger amount (1.0) and calculate the correlation coefficients between the function values in the original and translated sets.
The correlation coefficient is about 0.99 with the nearby points and 0.42 with the set further away. This reflects the change in function values, as illustrated by the pair of points marked in red.
In kriging, finding the rate of correlation decay is part of the fitting process. This example shows us that with a wavy function we can expect the correlation to decay to about 0.4 over one sixth of the wavelength.

## Slide 10: Universal Kriging approximation
Kriging = trend function + local departure
  Global function: simply polynomials
  Linear: ,
  No uncertainty at sample locations
  Gaussian distribution between samples
  Kriging prediction (red) = mean of the Gaussian process
Local departure
(random process)
Trend function
Global function
(low-order polynomials)
x
y
Mean of Kriging prediction
Sampling data points
Systematic Departure
Trend Model

## Slide 11: Kriging vs. PRS
Kriging PRS
PRS assumes that is a correct form, but data have error that are statistically independent
  The regression process finds the model parameters to minimize these errors in the sense of mean-squared-error
Kriging assumes that data are accurate, but the model form is uncertain  Kriging fits data
  At prediction points, error in Kriging is described by local departure

## Slide 12: Correlation
Kriging assumes that predictions are correlated inversely proportional to the distance
  Correlation controls the smoothness of Kriging predictions
Correlation matrix (between samples)
  , strong b/w near points and weak b/w far points
Correlation between prediction point and samples

## Slide 13: Kriging Predictions
Point A: prediction point = sample location
Point B: prediction smoothly interpolates samples
Extrapolation region: prediction approaches the global fn.
  becomes PRS with global function
Hyperparameter:
  controls the effect of correlation affects smoothness
(x2, y2)
(x1, y1)
(xn, yn)
interpolation
extrapolation
extrapolation
A
B
Global model
Departure
x
y
Kriging model
Samples
True function

## Slide 14: Type of Kriging Surrogates
Depending on the trend (global) function
Universal Kriging: general polynomial function
  Often linear or quadratic polynomials are used
Ordinary Kriging: constant trend function
Simple Kriging: constant trend function is known (often 0)
Assumption: Systematic departures are correlated.
Kriging prediction comes with a normal distribution of the uncertainty in the prediction
At the sample points, the uncertainty is zero
Notes: The most general version of kriging is called universal kriging, and it includes a linear trend function and the deviation which includes the local contributions and is governed by the correlation function.
The trend function is composed of known shape functions and coefficients to be determined. The shape functions are typically monomials, so that popular trend functions are linear and quadratic polynomials.
Here we will limit the description to a constant trend, a version of kriging known as ordinary kriging, with the constant estimated from the data. Another version of kriging, known as simple kriging is when the constant is assumed to be known.
As in linear regression, the kriging fit, shown in red in the figure, is only the mean of a normal distribution, and the distribution can be used to provide estimates of uncertainty in the kriging predictions, as well as guide the placements of further sampling points so as to reduce the uncertainty in the kriging prediction.
Caution: Note that the figure is misleading in that the uncertainty at the points where the data is given is zero when there is no noise. The uncertainty is larger in between data points.
The most general version of kriging is called universal kriging, and it includes a linear trend function and the deviation ├ 𝑍(𝐱)which includes the local contributions and is governed by the correlation function.
𝑦 ̂(𝐱)=∑129_(𝑖=1)^(𝑁_𝑣)▒├ 𝛽_𝑖 𝜉_𝑖 (𝐱) +𝑍(𝐱)
The trend function is composed of known shape functions 𝜉_𝑖 (𝐱) and coefficients 𝛽_𝑖 to be determined. The shape functions are typically monomials, so that popular trend functions are linear and quadratic polynomials.
Here we will limit the description to a constant trend, a version of kriging known as ordinary kriging, with the constant estimated from the data. Another version of kriging, known as simple kriging is when the constant is assumed to be known.
As in linear regression, the kriging fit, shown in red in the figure, is only the mean of a normal distribution, and the distribution can be used to provide estimates of uncertainty in the kriging predictions, as well as guide the placements of further sampling points so as to reduce the uncertainty in the kriging prediction.
Caution: Note that the figure is misleading in that the uncertainty at the points where the data is given is zero when there is no noise. The uncertainty is larger in between data points.

## Slide 15: Correlation Model
Predictions are correlated inversely proportional to the distance
Systematic departure captures this correlation
  Zero mean:
  Covariance of data:
  Variance of function:
Hyperparameter determines the shape of correlation
  describes similarity of two outputs based on the distance
  Large : correlation reaches a long distance. Predictions tend to be smooth
  Small : correlation decays fast. Predictions show fluctuation

## Slide 16: Isotropic vs. anisotropic correlation functions
(a) Isotropic correlation
(b) Anisotropic correlation

## Slide 17: Gaussian correlation function
Gaussian correlation between point and point
  : hyperparameter, decaying rate
  The correlation should decay to about 0.4 at one sixth of the wavelength and
  Approximately
  For the function we would like to estimate
When , anisotropic = isotropic correlation
Notes: The most popular correlation decay function for kriging is Gaussian. Given two points x (with components ) and s we assume that the correlation of the unknown function Z at these two points is given as
Where the larger is, the faster the decay of the correlation with distance. For =1, the decay in the ith direction is 1/e=0.37, which approximately corresponds to what we found for one sixth of the wavelength for the function sin(x). So if the wavelength in the ith direction is , we should have approximately
So for the function we have ~(6/5) so we should use .
The gaussian correlation function can also be generally referred to as gaussian kernel or basis functions.
The most popular correlation decay function for kriging is Gaussian. Given two points x (with components 𝑥_𝑖) and s we assume that the correlation of the unknown function Z at these two points is given as
𝐶(𝑍(𝐱),𝑍(𝐬),𝛉)=∏129_(𝑖=1)^(𝑁_𝑣)▒exp(−𝜃_𝑖 (𝑥_𝑖−𝑠_𝑖 )^2 )
Where the larger 𝜃_𝑖 is, the faster the decay of the correlation with distance. For 𝜃_𝑖=1, the decay in the ith direction is 1/e=0.37, which approximately corresponds to what we found for one sixth of the wavelength for the function sin(x). So if the wavelength in the ith direction is 𝑙_𝑖, we should have approximately
𝜃_𝑖 (𝑙_𝑖∕6)^2=1" or" 〖 𝜃〗_𝑖=36∕𝑙_𝑖^2
So for the function ├ 𝑦=sin(𝑥_1)∗sin(5𝑥_2 ) we have 𝑙_1≈6," " 𝑙_2≈1.2 so we should use 𝜃_1≈1," " 𝜃_2≈25.

## Slide 18: Covariance Matrix of Samples
Covariance matrix of samples
  sample points , with -dimension of input and
  Given decay rates , the covariance matrix of the data
  The correlation matrix is formed from the covariance matrix, assuming a constant standard deviation which measures the uncertainty in function values (stationary covariance)
  Need to estimate both and during the fitting process
Small for dense data, large for sparse data
  How do you decide whether the data is sparse or dense?
Notes: We use subscripts to denote components of a vector, and superscript to identify data points. We are in n dimensional space, and we have data points.
In the process of fitting the data, we will also need to estimate the decay rates and the standard deviation . The standard deviation will be small when the data is dense. Dense means that we have more than enough points to describe the waviness of the function. That means that the distance from one point to the nearest one should be an order of magnitude less than the wavelength of the function.
We use subscripts to denote components of a vector, and superscript to identify data points. We are in n dimensional space, and we have 𝑛_𝑦 data points.
In the process of fitting the data, we will also need to estimate the decay rates 𝜃_𝑘 and the standard deviation 𝜎. The standard deviation will be small when the data is dense. Dense means that we have more than enough points to describe the waviness of the function. That means that the distance from one point to the nearest one should be an order of magnitude less than the wavelength of the function..

## Slide 19: Ex7.2) Correlation Matrix
Equally spaced 5 samples in
,
  ,
  , , no correlation between samples
  ,, all samples have significant correlation, difficult to calculate

## Slide 20: 7.3 Kriging Surrogate Model
In statistical viewpoint, the best parameters maximize the likelihood function

## Slide 21: Global Function and Distribution of Errors
Global function coefficients, , and variance of data,
Errors b/w data and global function:
Assumption: error and correlation between data
Maximum likelihood estimate (MSE)
  Likelihood: PDF of getting data for given parameters, and

## Slide 22: Likelihood Function
Likelihood function
  multiplication of Gaussian distributions. : determinant of
Maximum likelihood estimate (MLE)
  Want to find , and , which maximize
  Compared to linear regression, the main difference is , but it yields a significantly different estimate
  Max. location may not be achieved at min. errors
  MLE is to find that make the differences in samples and the correlation matrix consistent with correlation
  Note that the differences are in the output space, while the correlation is defined in the input space

## Slide 23: Maximum Likelihood Estimate (MLE)
Logarithmic likelihood (assume is known for now)
  Second term penalizes the likelihood for a large variance of
  Third term penalizes model complexity (decay fast), MLE prefers correlated model (smooth model)
  Last term penalizes the lack of fitting samples (It will be shown later that this term is constant)
  MLE: trade-off between fitting performance and simplicity of the Kriging model
  Simple model = small and
  We will maximize only with 2nd and 3rd terms

## Slide 24: Maximum Likelihood Estimate (MLE)
Stationary condition
Solve for and
  Estimated parameters depend on , and thus,
  Laster term of = constant:
PRS linear regression
For unbiased estimate

## Slide 25: Global Function in MLE
How important the global function is?
  For estimating function in interpolating region, global function might not be important – local departure will make the prediction passes through samples
  However, global function becomes important in extrapolation region
  correlation is quickly diminished in the extrapolation region, and predictions follows the global function
  important to choose the global function that is close to the true functional behavior

## Slide 26: Ex7.3) Effect of Correlation on The Global Function
  Samples: , model form
  Linear regression: (no correlation)
  When
  regression chose a slope that follows the trend of the two correlated samples
  The slope increase along with the correlation
,
0
1
2
y
x
Without correlation
With correlation

## Slide 27: Ex7.4) Comparison with PRS
  In Ex7.3), with , with , and with
  Global function with MLE (
  The assumption of correlation makes the global function not to follow the trend of samples
0
1
2
y
x
RMS fit
Max. error fit
Ave. error fit
Global function
0
0.4
0.8
1.2
1.6
2
-0.8
-0.6
-0.4
-0.2
0
0.2
0.4

## Slide 28: Local Departure
Kriging passes data point  Kriging can be expressed by a linear combination of data and weights:
Minimizing mean squared error (MSE)
  Data:
  True function:
Weight function
Global error
Departure error

## Slide 29: Minimize MSE
To keep the global function unbiased, a constraint of global error being zero is added
MSE is the variance (uncertainty) in Kriging prediction
Goal: find that minimizes MSE while satisfying the unbiased constraint
  Convert the constrained optimization problem to unconstrained optimization problem using Lagrange multipler

## Slide 30: Lagrange Function for Constrained Optimization
Lagrange function (min. MSE with constraint)
Stationary conditions (KKT)
Lagrange multiplier

## Slide 31: Kriging Prediction
Kriging as linear combination of data and weight functions
  Local departure term is the weighted sum of the trend function error based on the correlation term
Trend function
Local departure

## Slide 32: Computational Cost of Kriging
Let (sample dependent terms)
  Basis function is unknown in advance
Computational cost of local departure
  calculating the correlation matrix and its inverse for all samples
  calculating the correlation vector at every prediction point
  multiplying with the inverse of the correlation matrix
impractical to calculate for large
  Instead, is solved for vector
  numerical difficulty for a large near singular

## Slide 33: Simplification for Ordinary Kriging
For ordinary Kriging, and (not a mean of data)
Linear in that the radial basis can be viewed as basis functions
The prediction is linear in the data , in common with linear regression, but is not calculated by minimizing MSE.
Note that far away from data, (not good for substantial extrapolation)
Notes: The form of the surrogate for ordinary kriging is
Where is the constant, the estimated mean value. The vector b of coefficient is , and the shape functions that it multiplies are the exponentials
So kriging is similar to linear regression, which is a linear combination of unknown coefficients time known shape function. However, there are two important differences. First the shape functions are not known, in that the decay rates will be estimated from the data (in the next slide). Second, the coefficients are not found by minimizing the rms error at the data points (which is zero, because the data is exactly interpolated).
Note that since the exponentials decay away from the data points, when we are far from all data points the prediction will be close to . So ordinary kriging is not good for substantial extrapolation. If we expect to need to extrapolate far from data points, we should use universal kriging with a trend.
The form of the surrogate for ordinary kriging is
𝑦 ̂(𝐱)=𝜇 ̂+𝐫^𝑇 𝑅^(−1) 𝐲=𝜇 ̂+𝐛^𝑇 𝐫
Where 𝜇 ̂ is the constant, the estimated mean value. The vector b of coefficient is 〖𝒃=𝑅〗^(−1) 𝐲, and the shape functions that it multiplies are the exponentials
𝑟_𝑖=exp(−∑129_(𝑘=1)^𝑛▒〖𝜃_𝑘 (𝑥_𝑘^((𝑖) )−𝑥_𝑘^ )^2 〗)
So kriging is similar to linear regression, which is a linear combination of unknown coefficients time known shape function. However, there are two important differences. First the shape functions are not known, in that the decay rates 𝜃_𝑘 will be estimated from the data (in the next slide). Second, the coefficients are not found by minimizing the rms error at the data points (which is zero, because the data is exactly interpolated).
Note that since the exponentials decay away from the data points, when we are far from all data points the prediction will be close to 𝜇 ̂ . So ordinary kriging is not good for substantial extrapolation. If we expect to need to extrapolate far from data points, we should use universal kriging with a trend.

## Slide 34: Ex7.5) Weight Function
  With the 3 samples in Ex7.3, plot as a function of when
  Weight function with
0
0.2
0.4
0.6
0.8
1
1.2
1.4
1.6
1.8
2
-0.2
0
0.2
0.4
0.6
0.8
1
w
1
w
2
w
3
y=[0 1 0]';
X=[1 0;1 1;1 2];
R=[ 1 exp(-1) exp(-4)
exp(-1) 1 exp(-1)
exp(-4) exp(-1) 1];
Rinv=inv(R);
A=X'*Rinv*X;
Ainv=inv(A);
for i=1:51
x(i)=0.04*(i-1);
r = [exp(-((0-x(i))/th)^2);exp(-((1-x(i))/th)^2);
exp(-((2-x(i))/th)^2)];
xi= [1; x(i)];
w(i,:)=r'*Rinv + (xi'-r'*Rinv*X)*Ainv*X'*Rinv;
end
plot(x,w(:,1),x,w(:,2),x,w(:,3))
legend('w_1','w_2','w_3')
Kronecker delta property of

## Slide 35: Ex7.6) Ordinary Kriging
  With the 3 samples in Ex7.3, derive the ordinary Kriging model with
  When , . When , sample mean
  Kriging prediction:

## Slide 36: Ex7.6) Ordinary Kriging cont.
  Kriging prediction passes through all sample points irrespective of the hyperparameter
  Kring predictions are smooth with a large hyperparameter : making the global function negative (), such that the differences become all positive
  With , , Majority of Kriging predictions follow the global function
0
0.5
1
1.5
2
2.5
-0.4
-0.2
0
0.2
0.4
0.6
0.8
1
Global fn
Samples

## Slide 37: Estimating hyperparameters
Estimating and depends on hyperparameter in
Maximizing the log-likelihood that the data comes from a Gaussian process defined by .
Maximum likelihood is a tough optimization problem
  the likelihood often varies slowly in a wide range of argument
  Some Kriging codes minimize the cross-validation error instead
: unbiased estimate

## Slide 38: Difficulties in Identifying Hyperparameter
is not enough to represent the functional behavior
  negative log-likelihood continues to increase with min value
  Kriging predictions will follow the global function
when the global function is the same as the true function
  log-likelihood term
  not possible to find that maximizes the likelihood function
  any that does not make singular would be valid
  since , prediction uncertainty cannot be calculated

## Slide 39: Estimating hyperparameters (ordinary Kriging)
Once is found, the estimate of the mean and standard deviation is obtained as (ordinary Kriging)
Notes: The basic assumption of kriging is that the function is a realization of a Gaussian process with given mean and covariance matrix. The fitting process consists of finding the mean and the covariance matrix from the data. The most common way of doing that is to find the mean and covariance that maximize the likelihood that the data came from them. It can be shown that this likelihood is
Where 1 denotes a vector of ones.
The dependence on the is complex since it is part of the matrix R, and so finding the that maximize the likelihood is done numerically. It is a tough optimization problem with normally large number of local maxima. On the other hand, given the , one can find and that will maximize the likelihood by differentiating the log of the likelihood with respect to these two parameters. This yields the following estimates.
Instead of using a maximum likelihood approach for the parameters, cross validation is also used by some. This means leaving out one of the points, fitting the rest with the parameters, and calculating the error at the left-out point. This is repeated for every point to produce a total error measure (e.g. rms). Then the set of parameters that yields the lowest cross validation error is chosen.
Stationary covariance assumption: wavelength of response is quite uniform in all regions of input space. So, once the covariance matrix is found using the initial data, it is constant throughout the input space.
There has also been some work on non-stationary covariance based kriging also.
Xiong, Y., Chen, W., Apley, D., & Ding, X. (2007). A non‐stationary covariance‐based Kriging method for metamodelling in engineering design. International Journal for Numerical Methods in Engineering, 71(6), 733-756.
The basic assumption of kriging is that the function is a realization of a Gaussian process with given mean and covariance matrix. The fitting process consists of finding the mean and the covariance matrix from the data. The most common way of doing that is to find the mean and covariance that maximize the likelihood that the data came from them. It can be shown that this likelihood is
𝐿=1/(2𝜋𝜎^2 )^(𝑛∕2) exp[−(∑129_(𝑖=1)^(𝑛_𝑦)▒(𝑦_𝑖−𝜇) )/(2𝜎^2 )=1/((2𝜋𝜎^2 )^(𝑛∕2) |𝑅|^(1∕2) ) exp[((𝐲−𝟏𝜇)^𝑇 𝑅^(−1) (𝐲−𝟏𝜇))/(2𝜎^2 )]
Where 1 denotes a vector of ones.
The dependence on the 𝜃_𝑘 is complex since it is part of the matrix R, and so finding the 𝜃_𝑘 that maximize the likelihood is done numerically. It is a tough optimization problem with normally large number of local maxima. On the other hand, given the 𝜃_𝑘, one can find 𝜇 and 𝜎 that will maximize the likelihood by differentiating the log of the likelihood with respect to these two parameters. This yields the following estimates.
𝜇 ̂=(𝟏^𝑇 𝑅^(−1) 𝐲)/(𝟏^𝑇 𝑅^(−1) 𝟏) 𝜎 ̂^2=((𝐲−𝟏𝜇)^𝑇 𝑅^(−1) (𝐲−𝟏𝜇))/𝑛
Instead of using a maximum likelihood approach for the parameters, cross validation is also used by some. This means leaving out one of the points, fitting the rest with the parameters, and calculating the error at the left-out point. This is repeated for every point to produce a total error measure (e.g. rms). Then the set of parameters that yields the lowest cross validation error is chosen.
Stationary covariance assumption: wavelength of response is quite uniform in all regions of input space. So, once the covariance matrix is found using the initial data, it is constant throughout the input space.
There has also been some work on non-stationary covariance based kriging also.
Xiong, Y., Chen, W., Apley, D., & Ding, X. (2007). A non‐stationary covariance‐based Kriging method for metamodelling in engineering design. International Journal for Numerical Methods in Engineering, 71(6), 733-756.

## Slide 40: Ex7.7) Likelihood Function
Plot neg. log-likelihood versus for Ex7.6
y=[0 1 0]’; X=[1 1 1]';
for k=1:100
th(k)=0.02*k;
e1=exp(-(1/th(k))^2); e2=exp(-(2/th(k))^2);
R=[1 e1 e2; e1 1 e1; e2 e1 1];
Rinv=inv(R); detR=det(R);
beta=(X'*Rinv*y)/(X'*Rinv*X);
ym=y-X*beta;
Like(k)=log((ym'*Rinv*ym/2)^4*detR);
end
plot(th,Like)
0
0.2
0.4
0.6
0.8
1
1.2
1.4
1.6
1.8
2
-4
-2
0
2
4
Negative log-likelihood
0
0.2
0.4
0.6
0.8
1
1.2
1.4
1.6
1.8
2
0
0.2
0.4
0.6
0.8
1

## Slide 41: Flat Region of Likelihood Function with Small
  the function stays constant when and monotonically increases when .
  indicator that the number of samples is too small to represent the variation of the function
  three predictions are significantly different, while there is no difference in the likelihood function
  minimizing the negative log-likelihood function may not find the optimum hyperparameter when the number of samples is not enough
What happen with small
  Uncorrelation b/w samples
  is also independent of
  important to limit not to make close to . Ideally

## Slide 42: Ex7.8) Likelihood with More Samples
5 samples:
0
0.5
1
1.5
2
2.5
-0.8
-0.4
0
0.4
0.8
Extrapolation region
0
0.2
0.4
0.6
0.8
1
1.2
1.4
1.6
1.8
2
-13
-12.5
-12
-11.5
-11
-10.5
Negative log-likelihood
Optimum
x=[0 0.5 1 1.5 2];
y=[0 0.7071 1 0.7071 0]';
X=[1 1 1 1 1]';
ny=size(x,2);
R=zeros(ny,ny);
for k=1:100
th(k)=0.02*k;
for i=1:ny
for j=1:ny
R(i,j)=exp(-((x(i)-x(j))/th(k))^2);
end
end
Rinv=inv(R);
detR=det(R);
beta(k)=(X'*Rinv*y)/(X'*Rinv*X);
ym=y-X*beta(k);
Like(k)=log((ym'*Rinv*ym/4)^8*detR);
end
figure; plot(th,Like)
Initial flat region but shows a clear global minimum

## Slide 43: 7.4 Issues in Determining Hyperparameters
The best hyperparameter depends on the number and location of samples

## Slide 44: Lower- and Upper-Bounds of Hyperparameter
Prevent too-small correlation distance
  Better to control directly:
Prevent too-large hyperparameter
  likelihood function becomes unstable
  the reciprocal condition number of decreases to zero
0
0.5
1
1.5
2
-140
-120
-100
-80
-60
-40
-20
0
Negative Log-likelihood

## Slide 45: Finding Optimum Value of Hyperparameter
minimizing the negative log-likelihood function
Neg. log-likelihood function starts decreasing after the initial flat region and has a minimum in
  Can be used unconstrained optimization algorithms in Chapter 5
  Possible to end up local optima. Recommended to start with and gradually increase
the negative log-likelihood function continues to increase after the initial flat region
  the number of samples is too small
  impossible to determine the optimal hyperparameter solely based on the likelihood function
  the difference is not significantly once the negative log-likelihood function passes the initial flat region

## Slide 46: Finding Optimum Value of Hyperparameter cont.
Kriging surrogate with a too-small number of samples, (a) negative log-likelihood function and (b) Kriging predictions with different hyperparameters
Negative log-likelihood
(a)
(b)
0.2
0.4
0.6
0.8
1
1.2
1.4
1.6
1.8
2
-10
0
10
20
0
0.5
1
1.5
2
-1.5
-1
-0.5
0
0.5
1
1.5

## Slide 47: Finding Optimum Value of Hyperparameter cont.
the negative log-likelihood function continues to decrease within the range of hyperparameter
  suggested to use the hyperparameter that makes the negative log-likelihood minimum within the range
  instability occurs when correlation between samples is too strong, and becomes singular
0
0.5
1
1.5
2
-300
-200
-100
0
6
8
10
12
14
16
18
0.4
0.6
0.8
1
1.2
Number of samples,
Negative log-likelihood

## Slide 48: Issues Related to the Number of Samples
No. of samples min.
the distance between samples decreases as the number of samples increases
  when , this relationship can be written as ,
6
7
8
9
10
11
12
13
14
0.2
0.3
0.4
0.5
0.6
0
0.2
0.4
0.6
0.8
1
-100
-80
-60
-40
-20
0
20
No. of samples
Negative Log-likelihood
6
7
8
9
10
11
12
13
14

## Slide 49: Computational Cost of Kriging Surrogate
PRS needs to solve matrix once
Kriging needs the inverse of
  Especially during optimization to find iteratively
MLE or cross-validation optimization problem solved to obtain the kriging fit is often ill-conditioned leading to poor fit, or poor estimate of the prediction variance.
Poor estimate of the prediction variance can be checked by comparing it to the cross-validation error.
Poor fits are often characterized by the kriging surrogate having large curvature near data points.
It is recommended to visualize by plotting the kriging fit and its standard error.

## Slide 50: Comparison b/w RMSE and MLE
Discontinuous
Good
MLEmin RMSE
More than 2 hyperparameters

## Slide 51: Quadratic Function Fit
Use 9 data and a constant global function to fit a quadratic function
Covariance
Too large
Good fit with poor variance
Too small
Bad fit with poor variance
Notes: The example of fiting a quadratic function was used with several kriging packages, using the points shown in the figure or also additional points outside the range. The two cases shown on the next slide are extreme cases for this simple function, but they show the kind of behavior that is occasionally encountered and can be detected by plotting the kriging fit and bounds representing two standard errors.

## Slide 52: Ex7.9) Kriging Prediction and Hyperparameter
Fit data , for the global function using ordinary Kriging with
  For ordinary Kriging, and
  y=[1 0.99 0.99 0.94 0.95]’; % measurement data
  x=[0 5 10 15 20]'; % input variable
  X=ones(5,1); % design matrix
  ny=length(y); np=size(X,2);
  Correlation matrix
  h=5.2;
  for k=1:ny; for l=1:ny;
  R(k,l)=exp(-(norm(x(k,:)-x(l,:))/h)^2);
  end; end;

## Slide 53: Ex7.9) Kriging Prediction and Hyperparameter cont.
Global function parameters
  Rinv=inv(R);
  thetaH=(X'*Rinv*X)\(X'* Rinv*y);
  sigmaH=sqrt(1/(ny-np)*((y-X*thetaH)'*Rinv*(y-X*thetaH)));
Estimate the optimum hyperparameter
  Instead of optimization the hyperparameter, we calculate it graphically
  We used this value in calculating and

## Slide 54: Ex7.9) Kriging Prediction and Hyperparameter cont.
Matlab code for the graph
Prediction at
  Exact at the sample point !
  h=zeros(20,1); Obj=zeros(20,1);
  for i=1:20
  h(i)=0.5*i;
  for k=1:ny; for l=1:ny;
  R(k,l)=exp(-(norm(x(k,:)-x(l,:))/h(i))^2);
  end; end;
  Rinv=inv(R);
  thetaH=(X'*Rinv*X)\(X'* Rinv*y);
  sigmaH=sqrt(1/(ny-np)*((y-X*thetaH)'*Rinv*(y-X*thetaH)));
  Obj(i)=log(sigmaH^(2*(ny-np))*det(R));
  end
  plot(h,Obj,'linewidth',2); grid on;

## Slide 55: Ex7.9) Kriging Prediction and Hyperparameter cont.
Prediction at
  xNew=10; %or xNew=14
  for k=1:ny; r(k,1)=exp(-(norm(x(k,:)-xNew)/h)^2); end;
  gpDepar=r'*Rinv*(y-X*thetaH);

## Slide 56: Ex7.10) Hyperparameter and Extrapolation Accuracy
equally spaced 20 samples from in
clear; ny=20; nth=10;
x=linspace(0,2*pi,ny)'; thmin=0.1;
y=sin(x)+0.2*x;
th=linspace(thmin,2.0,nth)';
s=[-pi:0.05:3*pi]';
X=ones(ny,1);
for k=1:nth % Loop for increasing hyperparameter
for i=1:ny, for j=1:ny % Correlation matrix
R(i,j)=exp(-((x(i)-x(j))/th(k)).^2);
end, end
if rcond(R) < eps, break; end % Check for reciprocal cond. No.
Rinv=inv(R);
beta=inv(X'*Rinv*X)*(X'*Rinv*y); % Global coefficient beta
ym=y-beta;
Like(k)=log((ym'*Rinv*ym/(ny-1))^(ny-1)*det(R)); % Neg. log-likelihood
for i=1:ny
r(:,i)=exp(-((s-x(i))/th(k)).^2); % Correlation at prediction point
end
yhat(:,k)=beta+r*Rinv*ym; % Kriging predictions
figure(1); plot(s,yhat); hold on;
fprintf("k=%2d th=%5.3f beta=%5.3f Like=%8.3e\n",k,th(k),beta,Like(k))
end
plot(x,y,'*',s,sin(s)+0.2*s,'k--'); hold off;
figure(2); plot(th(1:size(Like,2)),Like','b*-');

## Slide 57: Ex7.10) Hyperparameter and Extrapolation Accuracy cont.
The negative log-likelihood function continues to decrease until the correlation matrix becomes singular
: the predictions oscillate between samples since the correlation decays quickly
, all predictions are almost the same in the interpolation region
predictions are significantly different in the extrapolation region
0
0.2
0.4
0.6
0.8
1
1.2
1.4
1.6
-220
-180
-140
-100
-60
-20
-4
-2
0
2
4
6
8
10
-1
0
1
2
3
Negative log-likelihood
Kriging predictions
Interpolation region
Extrapolation region
Extrapolation region
(a)
(b)

## Slide 58: Uncertainty in Kriging Predictions
uncertainty comes from the uncertain model form, not from samples
  uncertainty is present between samples, which is represented as a Gaussian distribution
  Red curve is the mean, Gaussian distribution is shown at
  In general, 95% confidence interval is used to show prediction uncertainty
  Prediction uncertainty is zero as sample location

## Slide 59: Prediction Uncertainty
Kriging prediction is the mean prediction and MSE is the variance
Kriging prediction is Gaussian distribution
  When the # of data is small, use t-distribution
Prediction variance
  Standard error of prediction
Prediction variance for ordinary Kriging

## Slide 60: Prediction Variance = 0 at Sample location
Prediction variance at
We have
Therefore, Lagrange multiplier
Interpolating weight
Then, and
Therefore,

## Slide 61: Ex7.11) Uncertainty in Kriging Prediction
90% confidence intervals
  Standard error:
  xi=1;
  w=Rinv*r+Rinv*X*((X'*Rinv*X)\(xi'-X'*Rinv*r));
  ySigmaH=sigmaH*sqrt(w'*R*w-2*w'*r+1);
  % using the inverse calculation
  gpMean=0.9482; % from Example 7 9
  PI=[ gpMean + tinv(0.05,ny-np)*ySigmaH, ...
  gpMean + tinv(0.95,ny-np)*ySigmaH]
  % using the random samples
  ns=5e3;
  tDist=trnd(ny-np,1,ns);
  yHat=gpMean+tDist*ySigmaH;
  PI=prctile(yHat,[5 95])
 | 5 percentile | 95 percentile | 90% P.I.
x = 10 | 0.99 | 0.99 | 0
x = 14 | 0.9394 | 0.9570 | 0.0176
 | 5 percentile | 95 percentile | 90% P.I.
x = 10 | 0.99 | 0.99 | 0
x = 14 | 0.9394 | 0.9570 | 0.0176

## Slide 62: Ex7.12) Prediction Interval vs. Hyperparameter
10 equally spaced samples from true
ny=10; nth=4;
x=linspace(0,2*pi,ny)'; s=[-pi:0.05:3*pi]';
y=sin(x)+0.2*x;
th=[0.1; 0.5; 4.36; 5.5];
X=ones(ny,1);
for k=1:nth
for i=1:ny, for j=1:ny
R(i,j)=exp(-((x(i)-x(j))/th(k)).^2);
end, end
if rcond(R) < eps, break; end
Rinv=inv(R);
beta=inv(X'*Rinv*X)*(X'*Rinv*y);
sigmaH=ym'*Rinv*ym/(ny-1);
ym=y-beta;
for i=1:ny
r(:,i)=exp(-((s-x(i))/th(k)).^2);
end
yhat(:,k)=beta+r*Rinv*ym;
A=X'*Rinv*X; Ainv=inv(A);
for i=1:size(s,1)
w=r(i,:)*Rinv + (1-r(i,:)*Rinv*X)*Ainv*X'*Rinv;
ySigmaH(i,k)=sigmaH*sqrt(w*R*w'-2*w*r(i,:)'+1);
end
figure; hold on;
plot(s,yhat(:,k),x,y,'*',s,sin(s)+0.2*s,'r-','LineWidth',1);
patch([s;flipud(s)],[yhat(:,k)+tinv(0.05,ny-1)*ySigmaH(:,k); ...
flipud(yhat(:,k)+tinv(0.95,ny-1)*ySigmaH(:,k))], ...
'k','FaceAlpha',0.1);
end
Kriging predictions are relatively insensitive to
But prediction variances are sensitive to

## Slide 63: Ex7.12) Prediction Interval vs. Hyperparameter cont.
(a)
(b)
(c)
(d)

## Slide 64: Effect of Global Function
the role of global function is not to follow the trend of samples but to make the distribution of samples consistent to the given correlation
  Differences, , become as close as a Gaussian distribution with correlation matrix
  Simple Kriging (constant ) works well global function is not important in the interpolation region
Test with 8 samples from with constant and linear global functions
Constant function: ,
  Accurate prediction in the interpolation region with ignorable prediction uncertainty
  Predictions converge to the global function in the extrapolation region with significant prediction uncertainty

## Slide 65: Effect of Global Function cont.
Linear function:,
  prediction accuracy and uncertainty are similar in the interpolation region
  Predictions converge to the global function in the extrapolation region
(a)
(b)

## Slide 66: 7.5 Numerical Implementation of Kriging Surrogate
100-line of Matlab function for Kriging surrogate

## Slide 67: Computationally Efficient Implementation
Double inverse term is expensive
Adopt the algorithm in Design and Analysis of Computer Experiments (DACE) Matlab toolbox
Multi-dimensional Kriging needs to consider the format of sample pairs, the choice of the global function, and the form of the correlation function
Samples ,
  DoEs in Chapter 3 or LHS (space-filling DoE)
  Normalization
  Normalization of output QoI

## Slide 68: Multi-Dimensional Kriging Consideration
Correlation
  Make more sense to use anisotropic correlation function
  Hyperparameters
  Distance is measured in each variable direction separately
  correlation decays fast as it accumulates decay in each variable
Global function
  Low-order polynomials (not to introduce too many parameters)
  Minimize the negative log-likelihood (gradient free algorithm, Nelder-Mead simples, genetic algorithm)

## Slide 69: 100-Line Matlab Function Kriging
1 function [yp, ysig, nb]=Kriging(xs,ys,xp,trPRS,noise)
2 % INPUTS xs: ny x ndim sample points
3 % ys: ny x 1 samples
4 % xp: np x ndim prediction points
5 % trPRS: polynomial order of trend function (0, 1, 2)
6 % noise: 1 for noisy samples, 0 for no noise
7 % OUTPUTS yp: np x 1 mean predictions
8 % ysig: np x 1 prediction standard deviations
9 % nb: # of coefficients in trend function
10 %
11 [ny,ndim]=size(xs);nvar=ndim+1;np=size(xp,1);% Size of samples&predictions
12 meanx=mean(xs);stdx=std(xs);xs=(xs-meanx)./stdx;% Scaling sample locations
13 meany=mean(ys); stdy=std(ys);ys=(ys-meany)/stdy; % Scaling samples
14 xp=(xp-meanx)./stdx; % Scaling prediction points
15 %
16 nij=ny*(ny-1)/2; l=0; % # of upper-triangular component of R
17 diff=zeros(nij,ndim); % Distance between samples
18 ij=zeros(nij,2); % Index of correlation matrix
19 for i=1:ny-1
20 l=l(end)+(1:ny-i);
21 ij(l,:)=[repmat(i,ny-i,1),(i+1:ny)'];
22 diff(l,:)=repmat(xs(i,:),ny-i,1)-xs(i+1:ny,:);
23 end
24 %
25 % Estimating hyper-parameters using max. likelihood estimate
26 par=struct('xs',xs,'ys',ys,'d',diff,'ij',ij,'trPRS',min(trPRS,2));
27 hyp0 = [ny^(-1/4)*ones(ndim,1); min(0.1,noise)];
28 lb=[0.01*ones(ndim,1);0];ub=[6*ones(ndim,1);noise];% Lower- & upper-bounds
29 options=optimset('Display','off','TolFun',1e-6,'DiffMinChange',0.001);
30 hypOpt=fmincon(@(hyp) fitKRG(hyp,par),hyp0,[],[],[],[],lb,ub,[],options);
31 %hypOpt = ga(@(hyp) fitKRG(hyp,par),nvar,[],[],[],[],lb,ub,[],options)';
32 %hypOpt = simulannealbnd(@(hyp) fitKRG(hyp,par),hyp0,lb,ub,options);

## Slide 70
33 hypmle=hypOpt(1:size(xs,2)); t=max(0,hypOpt(end));
34 fprintf('Hyperparam:%8.3g\n',hypmle.*stdx');
35 if noise ~= 0, fprintf('Noise frac:%8.3g\n',tau); end
36 %
37 [~,fit]=fitKRG(hypOpt,par); % Fitting Kriging surrogate
38 %
39 xi = trend(xp,trPRS); nb=size(xi,2); % Trend basis vector at np points
40 xrep=repmat(xp',ny,1); xrep=transpose(reshape(xrep,ndim,np*ny));
41 d=xrep-repmat(xs,np,1); % Distance b/w predictions & samples
42 r = (1-t)*exp(sum(-(d./hypmle').^2,2)); % Correlation b/w preds & samples
43 r = reshape(r,ny,np);
44 yp=xi*fit.beta + (fit.alpha*r)'; % Kriging predictions
45 yp=yp*stdy+meany; % Unscaling predictions
46 %
47 rt=fit.C\r;
48 q=fit.G\(xi'-fit.Ft'*rt);
49 sigma2=fit.sigma2.*stdy.^2; % Process variance
50 ysig=sqrt(sigma2.*(1-sum(rt.^2,1)+sum(q.^2,1))'); % Prediction STD
51 fprintf('Total std :%8.3g\n',sqrt(sigma2)*stdy);
52 if noise~=0, fprintf('Noise std :%8.3g\n',sqrt(tau*sigma2)*stdy); end
53 end
54 %
55 function [negLogLK,fit]=fitKRG(xvar,par)
56 % Negative log-likelihood estimate for given hyper-parameter
57 %
58 % INPUTS hyp : Hyper-parameter
59 % par : Model parameters structure
60 % OUTPUTS negLogLK : Negative log-likelihood function
61 % fit : Necessary parameters for function evaluation
62 %
63 hyp=xvar(1:size(par.xs,2)); t=xvar(end);
64 H = trend(par.xs,par.trPRS); % Design matrix
65 ny=size(par.ys,1); nb=size(H,2); % ny: # of samples, nb: # of coeff.
66 r = (1-t).*exp(sum(-(par.d./hyp(:)').^2, 2)); % Correlation b/w samples
67 idx=find(r>0);

## Slide 71
68 ii=(1:ny)';
69 mu=(10+ny)*eps; % Small diagonal to prevent singularity
70 R=sparse([par.ij(idx,1);ii],[par.ij(idx,2);ii],[r(idx);ones(ny,1)+mu]);
71 [C,~]=chol(R); % Cholesky decomposition R = C'*C
72 C=C';
73 Ft=C\H;
74 Yt=C\par.ys;
75 [Q,G]=qr(Ft,0);
76 b=G\(Q'*Yt); % Coefficients of trend function
77 rho=(Yt-Ft*b); % rho = Cinv*(y-Xb)
78 alpha=rho'/C; % alpha = (y-Xb)'*Rinv
79 detR = sum(log(full(diag(C)).^2)); % Determinant of correlation matrix
80 sigma2=sum(rho.^2)/(ny-nb); % Process variance
81 negLogLK=detR + (ny-nb)*log(sigma2); % Negative log-likelihood
82 fit = struct('sigma2',sigma2,'beta',b,'alpha',alpha,'C',C,'Ft',Ft,'G',G');
83 end
84 %
85 function H=trend(x,order)
86 % Basis vector of trend function
87 %
88 [m,n]=size(x);
89 if order==0, H=ones(m,1); % Constant trend function basis
90 elseif order==1, H=[ones(m,1), x]; % Linear trend fucntion basis
91 elseif order==2 % Quadratic trend function basis
92 nn=(n+1)*(n+2)/2;
93 H=[ones(m,1) x zeros(m,nn-n-1)];
94 j=n+1; q=n;
95 for k=1:n
96 H(:,j+(1:q))=repmat(x(:,k),1,q).*x(:,k:n);
97 j=j+q; q=q-1;
98 end
99 end
100 end
Refer to textbook for detailed explanations

## Slide 72: Ex7.13) 1D Kriging Surrogate
8 samples from
  1 myfun=@(x) 0.5*((6*x-2).^2.*sin(12*x-4))+10*(x-0.5)+5; % In-line function
  2 xs=[0.1548,0.7148,0.4934,0.9932,0.5862,0.0007,0.3638,0.8198]'; % Samples
  3 ys=myfun(xs); % Samples from true function
  4 trPRS=0; % Ordinary Kriging
  5 xp=(0:0.01:1)'; % Prediction points
  6 [yp, ysig, nb]=Kriging(xs,ys,xp,trPRS,0); % Build Kriging surrogate
  7 ny=size(ys,1); % Number of samples
  8 cilb = yp + tinv(0.025,ny-nb)*ysig; % Lower-bounds of confidence intervals
  9 ciub = yp + tinv(0.975,ny-nb)*ysig; % Upper-bounds of confidence intervals
  10 ytrue=myfun(xp); % True function values at prediction points
  11 figure; hold on; % Plotting results
  12 xShaded=[xp;sort(xp,'descend')]; yShaded=[cilb;ciub(end:-1:1)];
  13 patch(xShaded,yShaded,[.24 .73 .89],'EdgeColor','none');
  14 plot(xp,yp,'r-',xs,ys,'k+',xp,ytrue,'k-','Markersize',10,'Linewidth',1.5)
  15 xlabel('x');ylabel('y(x)');
  16 legend('95% PI','Kriging prediction','Samples','True function');

## Slide 73: Ex7.13) 1D Kriging Surrogate cont.
0
0.2
0.4
0.6
0.8
1
x
0
5
10
15
20
y
(
x
)
95% PI
Kriging prediction
Samples
True function

## Slide 74: Ex7.14) Kriging Surrogate for Branin-Hu Function
20 LHS samples, evaluate accuracy at grid
1 BraninHu = @(x) (x(:,2)-1.275*(x(:,1)/pi).^2+5*(x(:,1)/pi)-6).^2 ...
2 +10*(1-1/(8*pi))*cos(x(:,1))+10;
3 rng('default'); N=31; dN=15/(N-1); ny=20;
4 xs=lhsdesign(ny,2,'iteration',5000); % 20 LHS samples
5 xs=xs.*[15, 15]+[-5, 0];
6 ys=BraninHu(xs); % Samples from true function
7 trPRS=0; % Ordinary Kriging
8 [XX,YY]=meshgrid(-5:dN:10, 0:dN:15); % NxN grid of predictions
9 xp=[reshape(XX,N^2,1) reshape(YY,N^2,1)]; % Prediction points
10 [yp, ysig, nb]=Kriging(xs,ys,xp,trPRS,0); % Build Kriging surrogate
11 YP=reshape(yp,N,N); % Predictions at grid
12 YT=reshape(BraninHu(xp),N,N); % True function at grid
13 figure(1); scatter(xs(:,1),xs(:,2),'filled'); % Plot sample locations
14 axis([-5 10 0 15]); xlabel('x_1');ylabel('x_2');
15 figure(2); hold on; surf(XX,YY,YP); % Plot of predictions
16 plot3(xs(:,1),xs(:,2),ys,'ro'); % Plot of samples
17 axis([-5 10 0 15]);xlabel('x_1');ylabel('x_2');zlabel('y');
18 figure(3); hold on; surf(XX,YY,YT) % PLot of true function
19 plot3(xs(:,1),xs(:,2),ys,'ro'); % Plot of samples
20 axis([-5 10 0 15]);xlabel('x_1');ylabel('x_2');zlabel('y');
21 eRMS=sqrt(sum(sum((YT-YP).^2))/N^2) % RMS error at NxN grid points
22 eav=sum(sum(abs(YT-YP)))/N^2 % Average error at NxN grid points
23 emax=max(max(abs(YT-YP))) % Maximum error at NxN grid points

## Slide 75: Ex7.14) Kriging Surrogate for Branin-Hu Function cont.
and
, , and
(a)
-5
0
5
10
x
1
0
5
10
15
x
2
(b)
(c)
Kriging prediction
True function

## Slide 76: Ex7.14) Kriging Surrogate for Branin-Hu Function cont.
likelihood as a function of hyperparameters
  complicated behavior over the range of hyperparameters
  : narrow valley, shows a clear period along direction
  No clear period along direction, local minimum
  Kriging prediction will not be significantly different when .

## Slide 77: Plotting Prediction Intervals for High Dimensions
plot a high-dimensional function along a line that goes though one of the diagonals of the design domain
BraninHu = @(x) (x(:,2)-1.275*(x(:,1)/pi).^2+5*(x(:,1)/pi)-6).^2 ...
+10*(1-1/(8*pi))*cos(x(:,1))+10;
rng('default'); ny=20;
xs=lhsdesign(ny,2,'iteration',5000); % 20 LHS samples
xs=xs.*[15, 15]+[-5, 0]; %xs=[xs;-5 0;10 0;-5 15;10 15];
ys=BraninHu(xs); % Samples from true function
trPRS=0; % Ordinary Kriging
s=(0:0.01:1)'; N=size(s,1); % Parameter along a diagonal direction
xp=[-5+15*s 15*s]; % xp=[-5+15*s 15-15*s];
[yp,ysig,nb]=Kriging(xs,ys,xp,trPRS,0); % Build Kriging surrogate
yt=BraninHu(xp); % True function for comparison
cilb = yp + tinv(0.025,ny-nb)*ysig; % Lower-bounds of confidence intervals
ciub = yp + tinv(0.975,ny-nb)*ysig; % Upper-bounds of confidence intervals
figure; hold on; % Plotting results
xShaded=[s;sort(s,'descend')]; yShaded=[cilb;ciub(end:-1:1)];
patch(xShaded,yShaded,[.24 .73 .89],'EdgeColor','none');
plot(s,yp,'r-',s,yt,'k-','Markersize',10,'Linewidth',1.5)
xlabel('s');ylabel('y(s)');
legend('95% PI','Kriging prediction','True function');
eRMS=sqrt(sum((yt-yp).^2)/N); % RMS error at NxN grid points
eav=sum(abs(yt-yp))/N; % Average error at NxN grid points
emax=max(abs(yt-yp)); % Maximum error at NxN grid points
fprintf('RMS error:%8.3g\nAve error:%8.3g\nMax error:%8.3g\n',eRMS,eav,emax);

## Slide 78: Plotting Prediction Intervals for High Dimensions cont.
0
0.2
0.4
0.6
0.8
1
s
0
50
100
150
200
250
300
350
y
(
s
)
95% PI
Kriging prediction
True function
0
0.2
0.4
0.6
0.8
1
s
-20
0
20
40
60
y
(
s
)
95% PI
Kriging prediction
True function
from to
from to
, , Larger error at corner region
, , Larger error at corner region

## Slide 79: 7.6 Kriging with Nuggets
When samples include random noise, it is important to separate noise variance from process variance

## Slide 80: Numerical Error in Simulation
many samples include random noise even in computer simulations
Shape design variables change mesh
mesh in the previous design may not be consistent with the mesh in the current design
due to the noise, sensitivity calculated by a small perturbation can be wrong
necessary to develop a Kriging surrogate model with regression capability
Dimension
F
25
25.1
25.2
25.3
25.4
25.5
0.3155
0.3156
0.3156
0.3156
0.3157
Dimension
Displacement

## Slide 81: Kriging with Nuggets
A version of Kriging surrogate modeling with noisy data
  additional values are added to the diagonal terms of
  Matlab calls it Gaussian process regression (GPR)
Sample model
  noise follows a zero-mean Gaussian distribution
With local departure , two covariance matrices
  : homogeneous noise (constant ), iid Gauessian noise
  : independent heterogeneous (heteroscedastic) noise, differ for each sample but not correlated
  : general heteroscedastic noise

## Slide 82: Kriging Surrogate with Correlated Noise
Covariance matrix for general heteroscedastic noise (impractical)
  impossible to separate the correlation matrix and the process variance
  Likelihood
  Challenging unless is parameterized
  Coefficients of global function:
  Mean prediction:
  Prediction variance with

## Slide 83: Kriging Surrogate with Homogeneous Noise
Covariance matrix for homogeneous noise
  Total variance: fraction of noise variance
  : noise-free Kriging, : no local departure (PRS)
  can separate the correlation matrix from the covariance matrix
  Likelihood
  MLE

## Slide 84: Kriging Surrogate with Homogeneous Noise cont.
MLE
Mean prediction
Prediction variance with
  The same Krigng.m can be used with noise=1

## Slide 85: Ex7.15) Kriging Surrogate with Noise
10 samples from , add noise, fit ordinary Kriging
1 myfun = @(x) sin(x); % In-line function
2 rng('default'); ny=10; nstd=0.1; % No. of samples, and noise std
3 xs=linspace(0,2*pi,ny)'; % Samples
4 ys=myfun(xs); % Samples from true function
5 noise=lhsnorm(0,nstd^2,ny); noise=nstd*(noise-mean(noise))/std(noise);
6 fprintf('Sample noiseSTD:%8.3g\n',std(noise));
7 ys=ys+noise;
8 trPRS=0; % Ordinary Kriging
9 xp=(0:0.01:2*pi)'; % Prediction points
10 [yp, ysig, nb]=Kriging(xs,ys,xp,trPRS,1); % Build Kriging surrogate
11 cilb = yp + tinv(0.025,ny-nb)*ysig; % Lower-bounds of confidence intervals
12 ciub = yp + tinv(0.975,ny-nb)*ysig; % Upper-bounds of confidence intervals
13 ytrue=myfun(xp); % True function values at predictio points
14 figure; hold on; % Plotting results
15 xShaded=[xp;sort(xp,'descend')]; yShaded=[cilb;ciub(end:-1:1)];
16 patch(xShaded,yShaded,[.24 .73 .89],'EdgeColor','none');
17 plot(xp,yp,'r-',xs,ys,'k+',xp,ytrue,'k-','Markersize',10,'Linewidth',1.5)
18 xlabel('x');ylabel('y(x)');
19 legend('95% PI','Kriging prediction','Samples','True function’);
No noise in sample, ,
No noise in sample, fit with noise, , ,
Noise in sample, fit without noise, ,
Noise in sample, fit wit noise: , ,

## Slide 86: Ex7.15) Kriging Surrogate with Noise cont.
(a)
(b)
(c)
(d)
0
1
2
3
4
5
6
x
-1.5
-1
-0.5
0
0.5
1
1.5
y
(
x
)
95% PI
Kriging prediction
Samples
True function
0
1
2
3
4
5
6
x
-1.5
-1
-0.5
0
0.5
1
1.5
y
(
x
)
95% PI
Kriging prediction
Samples
True function
0
1
2
3
4
5
6
x
-1.5
-1
-0.5
0
0.5
1
1.5
y
(
x
)
95% PI
Kriging prediction
Samples
True function
0
1
2
3
4
5
6
x
-1.5
-1
-0.5
0
0.5
1
1.5
y
(
x
)
95% PI
Kriging prediction
Samples
True function

## Slide 87: Likelihood Function with Noise
No noise in samples: neg. log-likelihood decreases rapidly as approaches zero
Noisy samples: neg. log-likelihood rapidly increases as approaches zero
(a)
(b)
No noise in samples
Noisy samples

## Slide 88: Likelihood Function with Noise cont.
identified noise standard deviation is underestimated
Sample |  |  |  |  |  |  | 
0.00 | 3.36 | 0 | 0.785 | 0 | 1.83E-6 | 1.45E-6 | 5.34E-6
0.05 | 3.29 | 0.000862 | 1.220 | 0.0357 | 0.0219 | 0.0182 | 0.0425
0.10 | 2.91 | 0.00503 | 0.994 | 0.0705 | 0.044 | 0.0362 | 0.088
0.15 | 2.54 | 0.0183 | 0.788 | 0.107 | 0.0665 | 0.0543 | 0.135
0.20 | 2.31 | 0.0408 | 0.707 | 0.143 | 0.0879 | 0.0714 | 0.179
0.25 | 2.14 | 0.0747 | 0.661 | 0.181 | 0.109 | 0.0877 | 0.221
0.30 | 2.0 | 0.118 | 0.642 | 0.221 | 0.129 | 0.104 | 0.261
0.00 | 3.36 | 0 | 0.785 | 0 | 1.83E-6 | 1.45E-6 | 5.34E-6
0.05 | 3.29 | 0.000862 | 1.220 | 0.0357 | 0.0219 | 0.0182 | 0.0425
0.10 | 2.91 | 0.00503 | 0.994 | 0.0705 | 0.044 | 0.0362 | 0.088
0.15 | 2.54 | 0.0183 | 0.788 | 0.107 | 0.0665 | 0.0543 | 0.135
0.20 | 2.31 | 0.0408 | 0.707 | 0.143 | 0.0879 | 0.0714 | 0.179
0.25 | 2.14 | 0.0747 | 0.661 | 0.181 | 0.109 | 0.0877 | 0.221
0.30 | 2.0 | 0.118 | 0.642 | 0.221 | 0.129 | 0.104 | 0.261
No. samples |  |  |  |  |  |  | 
5 | 1.41 | 0.00041 | 0.592 | 0.012 | 0.0853 | 0.0747 | 0.143
7 | 1.62 | 0.00292 | 0.552 | 0.0298 | 0.0942 | 0.0811 | 0.178
10 | 2.53 | 0.00917 | 0.735 | 0.0704 | 0.0657 | 0.0579 | 0.124
15 | 3.06 | 0.00558 | 0.993 | 0.0741 | 0.0459 | 0.0398 | 0.0816
20 | 2.91 | 0.00503 | 0.994 | 0.0705 | 0.044 | 0.0362 | 0.088
25 | 2.7 | 0.00799 | 0.835 | 0.0747 | 0.0326 | 0.0268 | 0.0683
30 | 2.66 | 0.00874 | 0.772 | 0.0722 | 0.0328 | 0.0262 | 0.117
No. samples |  |  |  |  |  |  | 
5 | 1.41 | 0.00041 | 0.592 | 0.012 | 0.0853 | 0.0747 | 0.143
7 | 1.62 | 0.00292 | 0.552 | 0.0298 | 0.0942 | 0.0811 | 0.178
10 | 2.53 | 0.00917 | 0.735 | 0.0704 | 0.0657 | 0.0579 | 0.124
15 | 3.06 | 0.00558 | 0.993 | 0.0741 | 0.0459 | 0.0398 | 0.0816
20 | 2.91 | 0.00503 | 0.994 | 0.0705 | 0.044 | 0.0362 | 0.088
25 | 2.7 | 0.00799 | 0.835 | 0.0747 | 0.0326 | 0.0268 | 0.0683
30 | 2.66 | 0.00874 | 0.772 | 0.0722 | 0.0328 | 0.0262 | 0.117